Chandra On-Orbit Protected SCS Handbook

# Introduction

This volume is the successor to the very popular, best-selling, SCS Handbook Rev. J that was approved in March of 2012. Since that time, several tasks involving making SCS modifications have been performed. This Revision brings the SCS Handbook up to date with PR-319 as the latest patch loaded onboard.  Recall that protected SCSs refer to the 127 slots that lie within the checksummed region of OBC memory, hence are protected from bit level corruption. These protected SCSs require a software patch to change their contents.  If you are using the electronic copy of this document, hyperlinks are indicated in BLUE.

NOTES - quick links to useful tables:

Table 1 is the table of contents for the protected SCS listed in this handbook.

Table 2 is a listing of the protected stored command sequences indicating their slot size (the number of commands that can be placed into each slot), plus each SCS starting and ending address in OBC memory

Table 3 is a listing of the sizes of the mission stored command sequence, included in this document for reference.

Table 4 is the latest Safe Modes Summary chart, included in this document for reference.

Table 5 shows the allowed and invalid SCS transitions

Table 6 contains all the SCS control commands

Table 7 is a listing of the Safe Mode related Modifications required due to H/W Reconfiguration

Table 8 is a listing of the Non-Safe Mode related Modifications required due to H/W Reconfiguration

Following these tables, and prior to the SCS listings themselves, is a brief overview of Stored Command Sequences.

This document is to remain current with the SCS image on the Chandra Spacecraft. Change pages are to be used, and a revision record is to be maintained. Electronic copies are also to be maintained.

Revision Record

| Rev # | Date | Description of Change | Change Author |
| --- | --- | --- | --- |
| Original | Pre-Launch | Original Issue | TRW Operations Team |
| Rev. A | March 7, 2000 | Post-OAC Comprehensive Cleanup | D. Muleady, TRW Chandra Operations |
| Rev. B | May 14, 2001 | Addition of OTG Nudge Move SCSs 55, 56, 57 and 58 | D. Muleady |
|  |  | Change to SCS 82, OTG Safing SCS |  |
|  |  | Corrections to: |  |
|  |  | SCS 73 step 8, Relative Time Delay is 1mc, not 2 mc |  |
|  |  | SCS 73 step 8, Relative Time Delay is 1mc, not 2 mc |  |
| Rev. C | July 27, 2004 | Updated to reflect on-orbit SCS configurations: SCS 31: Corrected text to for TX-A and PA-A are turned on SCS 82: Updated to reflect code to halt OTG motion upon SCS 107 run Various references to SCS 82 changed to reflect new name (OTG Emergency Halt) and function Old SCS 29 updated and moved to SCS 30 Brand new SCS 29 created for Eclipse Load Control SCS 32 and 33 updated for use for Eclipse Entrance and Exit SCSs 14, 78 and 82 updated to call appropriate SCSs SCS 83 designated a No-op SCS SCS 118 (Post-IUS Separation Tasks) and all references to it renamed to OBC Reset Reconfiguration Tasks – References in SCSs 7, 8, 9, 11, 12, 13, 14, 23, 25, 26, 27, 37, and 80. Description updated to reflect what it’s currently used for. Updates to SCS 31 and 34 for IRU Swap SCS 36 updated to reflect on-orbit values Add SCS 55, 56, 57, and 58 – OTG nudge SCSs Spare SCS descriptions updated. SCS 104 HRC mechanism commanding removed, call to SCS 105 removed, time delay added SCS 106 step count updated. Starts from 1 instead of 0. SCS 101 added to include checksummed CPE patches SCS 31 modified to enable and activate SCS 101 | F. Richard Myers |
| Rev. D | April 18, 2005 | Changes made in order to avoid long time periods at poor thermal attitudes for the propulsion lines as part of PR-196 Update to SCS 107 to activate SCS 84 SCS 84 modified to issue command to enter Normal Sun Mode – SCS 84 will no longer be a spare SCS | Christine Harbison, F. Richard Myers |
| Rev. E | October 31, 2005 | Modifications to SCS 107 to only move the SIM once, replacing the call to SCS 81 with a call to SCS 108 | F. Richard Myers |
| Rev. F | July 17, 2006 | New SCS 15 for Propulsion Line Temperature Monitor (PR-209). | F. Richard Myers |
| Rev. G | October 17, 2006 | Update to Table 4 Safe Modes Summary Flow Chart | Paul Viens |
| Rev. H | May 24, 2011 | Corrected Comment in SCS 32 about disabling the Angular Momentum Unloading Logic Added SCS 120 Update (PR-217) plus entry in Tables 1 and 2 Table 8, added note that failure of VDE-A requires changes to SCS 120 to command VDE-B Table 8, added note for required patching of primary database if staying on IP-B SCS 14: updated value of Momentum AutoUnload Threshold Corrected SCS 23 SADA monitor threshold to 172F Corrected SCS 27 flow diagram title Updated SCS 29 F_Eclipse flag current threshold Deleted extraneous SCS 31 command mnemonic AIB2CAYS in step 63 of the SCS table Corrected SCS 31 misspelled command mnemonic in step 65 of the SCS table Corrections were made to the constraints section of SCS 16, 26, 27, 28, 31, 60 Added SCS step reference column to SCS tables Added SCS step description in Stored Command Sequence Description Corrected a variety of field name typos for multi-part and modifiable commands in several SCSs | F. Richard Myers Daniel Wong |
| Rev. I | October 13, 2011 | Science Only Safing Action (SOSA) changes to SCSs 15, 27, 123 (new SCS entry) and 107 Table 3 (Mission Stored Command Sequence Slot Sizes and Addresses) –new SCS sizes and addresses Table 4 Safe Mode Summary Flow Chart –updated chart Added new section describing SOSA changes Removed command AORWMBDS in SCSs 17 – 22, and replaced with equivalent AORWMOMD command that is used in SCS 107 | Daniel Wong |
| Rev. J | March 22, 2012 | Removed mentioning of SA Position Monitoring being re-enabled in SCS 23. Updated SCS 90 for new HRC-S MCP ramp up step values via PR-307 | Daniel Wong |
| Rev. K | August 23, 2012 | Updated SCS 101 for CPE patch PR-319 (Momentum Auto-unload Threshold Limit) | Daniel Wong |

Table 1 Protected Stored Command Sequences Handbook Contents

Introduction	1

Stored Command Sequence Description	18

Chandra Safing SCS Modifications due to H/W Reconfiguration	24

Chandra SCS Modifications due to Science Only Safing Action Load Splitting	27

SCS #: 1 -- Initialize Online State	29

SCS #: 2 -- Safe State Transition	30

SCS #: 3 -- Deployment State Transition	31

SCS #: 4 -- Off-Line State Transition	32

SCS #: 5 -- OO - CCDM RCTU Command Wrap Test	33

SCS #: 6 -- OO - Attitude/Rate Error Monitor Fault	34

SCS #: 7 -- OO - IRU Monitor Fault Safing Action	35

SCS #: 8 -- OO - Sun Position Monitor Fault Safing Action	36

SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action	37

SCS #: 10 -- OO - Attitude Reference in Eclipse Monitor	38

SCS #: 11 -- OO - EPS Sunlight Overload Fault	39

SCS #: 12 -- OO - EPS Eclipse Overload Fault	41

SCS #: 13 -- OO - PCAD Sensor Processing Fault	42

SCS #: 14 -- OO - RW Unloading Monitor Fault	43

SCS #: 15 -- Propulsion Line Temperature Monitor Fault Safing Action	44

SCS #: 16 -- Attitude Reference in Sunlight Monitor	45

SCS #: 17 -- RW #1 Fault Handling	47

SCS #: 18 -- RW #2 Fault Handling	49

SCS #: 19 -- RW #3 Fault Handling	51

SCS #: 20 -- RW #4 Fault Handling	53

SCS #: 21 -- RW #5 Fault Handling	55

SCS #: 22 -- RW #6 Fault Handling	57

SCS #: 23 -- OO - SADA Position or Temperature Monitor Fault	59

SCS #: 24 -- Unexpected Connection of the Batteries	64

SCS #: 25 -- EP RCTU Monitor Fault	65

SCS #: 26 -- TS RCTU Monitor or Telescope Thermal Control Fault	70

SCS #: 27 -- SIM RCTU Monitor Fault Safing	76

SCS #: 28 -- Bright Star or Commanded Attitude Monitor	81

SCS #: 29 – Eclipse Load Control SCS	84

SCS #: 30 -- Battery Connection to Bus Safing Action	90

SCS #: 31 -- Safe Mode Reconfiguration	93

SCS #: 32 -- Eclipse Entry	109

SCS #: 33 -- Eclipse Exit	112

SCS #: 34 -- Configure PCAD	117

SCS #: 35 -- Activate Sensor Processing	119

SCS #: 36 -- Enter Standby Mode	122

SCS #: 37 -- OO - Normal Sun Mode First Entry	131

SCS #: 38 – Idle ACA Windows	138

SCS #: 39 -- Telescope OBA Heater Zone Shutdown	152

SCS #: 40 -- ACIS Instrument Shutdown	154

SCS #: 41 -- HRC Instrument Shutdown	163

SCS #: 42 -- Trim Heater Prime Disable	172

SCS #: 43 -- Trim Heater Redundant Disable	181

SCS #: 44 -- ESA and ESA Heater Prime Disable	186

SCS #: 45 -- ESA and ESA Heater Redundant Disable	188

SCS #: 46 -- Fuel Tank Heater Prime and Redundant Disable	190

SCS #: 47 -- Transmitter and Power Amp Prime Disable	191

SCS #: 48 -- Transmitter and Power Amp Redundant Disable	193

SCS #: 49 -- FLCA Prime Disable	195

SCS #: 50 -- FLCA Redundant Disable	197

SCS #: 51 -- RCS Catbed Heaters Prime Disable	199

SCS #: 52 -- RCS Catbed Heaters Redundant Disable	200

SCS #: 53 -- LAE Heaters Prime Disable	201

SCS #: 54 -- LAE Heaters Redundant Disable	203

SCS #: 55 – MCE-B LETG Insert Nudge	205

SCS #: 56 – MCE-B HETG Insert Nudge	207

SCS #: 57 -- MCE-B LETG Retract Nudge	208

SCS #: 58 --  MCE-B HETG Retract Nudge	209

SCS #: 59 -- Spare SCS	210

SCS #: 60 -- PC RCTU Monitor Fault	211

SCS #: 61 -- ESA and ESA Heater Prime Enable	215

SCS #: 62 -- ESA and ESA Heater Redundant Enable	217

SCS #: 63 -- Transmitter and Power Amp Prime Enable	219

SCS #: 64 -- Transmitter and Power Amp Redundant Enable	221

SCS #: 65 -- Fuel Tank Heater Prime and Redundant Enable	223

SCS #: 66 -- FLCA Prime Enable	224

SCS #: 67 -- FLCA Redundant Enable	227

SCS #: 68 -- Telescope OBA Heater Zone Enable	230

SCS #: 69 -- HRC Turn On (into Standby)	231

SCS #: 70 -- ACIS Turn-on into Standby	245

SCS #: 71 -- RCS Catbed Heaters Prime Enable	249

SCS #: 72 -- RCS Catbed Heaters Redundant Enable	250

SCS #: 73 -- LAE Injector Heaters Prime Enable (all 4 engines)	251

SCS #: 74 -- LAE Injector Heaters Redundant Enable (all 4 engines)	253

SCS #: 75 -- Trim Heater Prime Enable	255

SCS #: 76 -- Trim Heater Redundant Enable	268

SCS #: 77 -- OO - Halt OBC Safing Action	272

SCS #: 78 -- OO - Battery Connection / Halt OBC Safing Action	273

SCS #: 79 -- OO - NSM Transition	274

SCS #: 80 -- OO - Standby State Timeout	277

SCS #: 81 -- SIM Move to Safe Position	286

SCS #: 82 -- OTG Emergency Halt	292

SCS #: 83 – No-op SCS	296

SCS #: 84 – Command Normal Sun Mode	297

SCS #: 85 -- Spare SCS	299

SCS #: 86 -- Spare SCS	300

SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands	301

SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands	305

SCS #: 89 -- HRC Scheduled/Dither HRC-I HV Ramp Up Commands	309

SCS #: 90 -- HRC Scheduled/Dither HRC-S HV Ramp Up Commands	330

SCS #: 91 -- HRC Dither Control	351

SCS #: 92 -- HRC-I MCP HV On	354

SCS #: 93 -- HRC-S MCP HV On	359

SCS #: 94 -- OBA Heater Enable	364

SCS #: 95 -- EPHIN Failure	367

SCS #: 96 – PEA Reset	368

SCS #: 97 -- Spare SCS	369

SCS #: 98 -- Bright Star Normal Sun Mode	370

SCS #: 99 -- Bright Star SI Safing	371

SCS #: 100 – Spare SCS	372

SCS #: 101 – Checksum CPE Patches	373

SCS #: 102 – Spare SCS	381

SCS #: 103 – Spare SCS	382

SCS #: 104 -- HRC Safing Part 1	383

SCS #: 105 -- HRC Safing Part 2, Door Partially Close	388

SCS #: 106 – ACIS Safing	398

SCS #: 107 -- Main SI Safing	400

SCS #: 108 – SIM Move to HRC-S	407

SCS #: 109 -- Spare SCS	413

SCS #: 110 -- Spare SCS	414

SCS #: 111 -- Spare SCS	415

SCS #: 112 -- Spare SCS	416

SCS #: 113 -- Spare SCS	417

SCS #: 114 -- Spare SCS	418

SCS #: 115 -- Spare SCS	419

SCS #: 116 -- Spare SCS	420

SCS #: 117 -- Spare SCS	421

SCS #: 118 -- OBC Reset Reconfiguration Tasks	422

SCS #: 119 -- Spare SCS	430

SCS #: 120 – Momentum Unload Cutoff Monitor	431

SCS #: 121 -- Spare SCS	435

SCS #: 122 -- Spare SCS	436

SCS #: 123 -- Terminate and Disable Observing SCSs 131 - 135	437

SCS #: 124 -- Spare SCS	439

SCS #: 125 -- Spare SCS	440

SCS #: 126 -- Spare SCS	441

SCS #: 127 -- Spare SCS	442

Table 2 Protected SCS Slot Sizes and Addresses

| SCS # | Size, Cmds | Start Address | End Address | Name |
| --- | --- | --- | --- | --- |
| 1 | 5 | 1B000 | 1B009 | Initialize Online |
| 2 | 5 | 1B00A | 1B013 | Safe Transition |
| 3 | 5 | 1B014 | 1B01D | Deploy Transition |
| 4 | 5 | 1B01E | 1B027 | Offline Transition |
| 5 | 5 | 1B028 | 1B031 | CCDM RCTU Command Wrap Fault |
| 6 | 5 | 1B032 | 1B03B | Attitude Rate Monitor Fault |
| 7 | 5 | 1B03C | 1B045 | IRU Monitor Fault |
| 8 | 10 | 1B046 | 1B059 | Sun Position Monitor Fault |
| 9 | 10 | 1B05A | 1B06D | Spacecraft Mom Monitor Fault |
| 10 | 5 | 1B06E | 1B077 | Attitude Ref Eclipse Monitor |
| 11 | 5 | 1B078 | 1B081 | EPS Sun Overload Fault |
| 12 | 5 | 1B082 | 1B08B | EPS Eclipse Overload Fault |
| 13 | 5 | 1B08C | 1B095 | PCAD Sensor Processor Fault |
| 14 | 5 | 1B096 | 1B09F | RW Unload Monitor Fault |
| 15 | 5 | 1B0A0 | 1B0A9 | Propulsion Line Temp Monitor Fault |
| 16 | 20 | 1B0AA | 1B0D1 | Attitude Ref Sun Monitor Fault |
| 17 | 15 | 1B0D2 | 1B0EF | RW1 Momentum Monitor Fault |
| 18 | 15 | 1B0F0 | 1B10D | RW2 Momentum Monitor Fault |
| 19 | 15 | 1B10E | 1B12B | RW3 Momentum Monitor Fault |
| 20 | 15 | 1B12C | 1B149 | RW4 Momentum Monitor Fault |
| 21 | 15 | 1B14A | 1B167 | RW5 Momentum Monitor Fault |
| 22 | 15 | 1B168 | 1B185 | RW6 Momentum Monitor Fault |
| 23 | 40 | 1B186 | 1B1D5 | SADA Position or Temp Monitor Fault |
| 24 | 10 | 1B1D6 | 1B1E9 | Unexpected Battery Connect Fault |
| 25 | 40 | 1B1EA | 1B239 | EP RCTU Monitor Fault |
| 26 | 60 | 1B23A | 1B2B1 | TS RCTU Monitor Fault |
| 27 | 45 | 1B2B2 | 1B30B | SIM RCTU Monitor Fault |
| 28 | 5 | 1B30C | 1B315 | Bright Star Acquisition Monitor Fault |
| 29 | 20 | 1B316 | 1B33D | Eclipse Load Control |
| 30 | 60 | 1B33E | 1B3B5 | Battery Connection to Bus Safing Action |
| 31 | 225 | 1B3B6 | 1B577 | Safe Mode Reconfiguration |
| 32 | 50 | 1B578 | 1B5DB | Eclipse Entrance |
| 33 | 50 | 1B5DC | 1B63F | Eclipse Exit |
| 34 | 10 | 1B640 | 1B653 | Configure PCAD |
| 35 | 15 | 1B654 | 1B671 | Activate Sensor Processing |
| 36 | 110 | 1B672 | 1B74D | Enter Standby Mode |
| 37 | 90 | 1B74E | 1B801 | First Normal Sun Mode |
| 38 | 50 | 1B802 | 1B865 | ACA Fid Light Reset |
| 39 | 20 | 1B866 | 1B88D | OBA Heater Zone Shutoff |
| 40 | 130 | 1B88E | 1B991 | ACIS Shutdown |
| 41 | 75 | 1B992 | 1BA27 | HRC Shutdown |
| 42 | 70 | 1BA28 | 1BAB3 | Trim Heater Prime Disable |
| 43 | 60 | 1BAB4 | 1BB2B | Trim Heater Redundant Disable |
| 44 | 20 | 1BB2C | 1BB53 | ESA Prime Disable |
| 45 | 20 | 1BB54 | 1BB7B | ESA Redundant Disable |
| 46 | 20 | 1BB7C | 1BBA3 | Tank Heater Disable |
| 47 | 20 | 1BBA4 | 1BBCB | Transmitter Prime Disable |
| 48 | 20 | 1BBCC | 1BBF3 | Transmitter Redundant Disable |
| 49 | 20 | 1BBF4 | 1BC1B | FLCA Prime Disable |
| 50 | 20 | 1BC1C | 1BC43 | FLCA Redundant Disable |
| 51 | 10 | 1BC44 | 1BC57 | RCS Heater Prime Disable |
| 52 | 10 | 1BC58 | 1BC6B | RCS Heater Redundant Disable |
| 53 | 20 | 1BC6C | 1BC93 | LAE Heater Prime Disable |
| 54 | 20 | 1BC94 | 1BCBB | LAE Heater Redundant Disable |
| 55 | 10 | 1BCBC | 1BCCF | MCE-B LETG Insert Nudge |
| 56 | 10 | 1BCD0 | 1BCE3 | MCE-B HETG Insert Nudge |
| 57 | 10 | 1BCE4 | 1BCF7 | MCE-B LETG Retract Nudge |
| 58 | 10 | 1BCF8 | 1BD0B | MCE-B HETG Retract Nudge |
| 59 | 10 | 1BD0C | 1BD1F | Spare |
| 60 | 25 | 1BD20 | 1BD51 | PC RCTU Monitor Fault |
| 61 | 20 | 1BD52 | 1BD79 | ESA Prime Enable |
| 62 | 20 | 1BD7A | 1BDA1 | ESA Redundant Enable |
| 63 | 20 | 1BDA2 | 1BDC9 | Transmitter Prime Enable |
| 64 | 20 | 1BDCA | 1BDF1 | Transmitter Redundant Enable |
| 65 | 20 | 1BDF2 | 1BE19 | Tank Heater Enable |
| 66 | 20 | 1BE1A | 1BE41 | FLCA Prime Enable |
| 67 | 20 | 1BE42 | 1BE69 | FLCA Redundant Enable |
| 68 | 10 | 1BE6A | 1BE7D | OBA Thermal Control Enable |
| 69 | 100 | 1BE7E | 1BF45 | HRC Turn On |
| 70 | 50 | 1BF46 | 1BFA9 | ACIS Turn On |
| 71 | 10 | 1BFAA | 1BFBD | RCS Heater Prime Enable |
| 72 | 10 | 1BFBE | 1BFD1 | RCS Heater Redundant Enable |
| 73 | 20 | 1BFD2 | 1BFF9 | LAE Heater Prime Enable |
| 74 | 20 | 1BFFA | 1C021 | LAE Heater Redundant Enable |
| 75 | 75 | 1C022 | 1C0B7 | Trim Heater Prime Enable |
| 76 | 60 | 1C0B8 | 1C12F | Trim Heater Redundant Enable |
| 77 | 5 | 1C130 | 1C139 | Halt OBC |
| 78 | 10 | 1C13A | 1C14D | VDE Off Halt |
| 79 | 35 | 1C14E | 1C193 | NSM Transition |
| 80 | 70 | 1C194 | 1C21F | Standby State Timeout |
| 81 | 15 | 1C220 | 1C23D | SIM Move to Safe Position |
| 82 | 75 | 1C23E | 1C2D3 | OTG Emergency Halt |
| 83 | 10 | 1C2D4 | 1C2E7 | No-op SCS |
| 84 | 10 | 1C2E8 | 1C2FB | Command Normal Sun Mode |
| 85 | 50 | 1C2FC | 1C35F | Spare |
| 86 | 10 | 1C360 | 1C373 | Spare |
| 87 | 25 | 1C374 | 1C3A5 | Ramp Down HRC-I HV |
| 88 | 25 | 1C3A6 | 1C3D7 | Ramp Down HRC-S HV |
| 89 | 120 | 1C3D8 | 1C4C7 | Ramp Up HRC-I HV |
| 90 | 120 | 1C4C8 | 1C5B7 | Ramp Up HRC-S HV |
| 91 | 20 | 1C5B8 | 1C5DF | Dither Control |
| 92 | 25 | 1C5E0 | 1C611 | HRC-I MCP HV On |
| 93 | 25 | 1C612 | 1C643 | HRC-S MCP HV On |
| 94 | 10 | 1C644 | 1C657 | OBA Heater Enable |
| 95 | 10 | 1C658 | 1C66B | EPHIN Failure |
| 96 | 10 | 1C66C | 1C67F | PEA Reset |
| 97 | 10 | 1C680 | 1C693 | Spare |
| 98 | 10 | 1C694 | 1C6A7 | Bright Star Normal Sun Mode |
| 99 | 10 | 1C6A8 | 1C6BB | Bright Star SI Safing |
| 100 | 10 | 1C6BC | 1C6CF | Spare |
| 101 | 200 | 1C6D0 | 1C85F | Checksum CPE Patches |
| 102 | 200 | 1C860 | 1C9EF | Spare |
| 103 | 200 | 1C9F0 | 1CB7F | Spare |
| 104 | 200 | 1CB80 | 1CD0F | HRC Safing Part 1 |
| 105 | 200 | 1CD10 | 1CE9F | HRC Safing Part 2 |
| 106 | 100 | 1CEA0 | 1CF67 | ACIS Safing |
| 107 | 100 | 1CF68 | 1D02F | Main SI Safing SCS |
| 108 | 100 | 1D030 | 1D0F7 | SIM Move to HRC-S Position |
| 109 | 100 | 1D0F8 | 1D1BF | Spare |
| 110 | 100 | 1D1C0 | 1D287 | Spare |
| 111 | 100 | 1D288 | 1D34F | Spare |
| 112 | 100 | 1D350 | 1D417 | Spare |
| 113 | 100 | 1D418 | 1D4DF | Spare |
| 114 | 100 | 1D4E0 | 1D5A7 | Spare |
| 115 | 100 | 1D5A8 | 1D66F | Spare |
| 116 | 100 | 1D670 | 1D737 | Spare |
| 117 | 100 | 1D738 | 1D7FF | Spare |
| 118 | 110 | 1D800 | 1D8DB | OBC Reset Reconfiguration Tasks |
| 119 | 100 | 1D8DC | 1D9A3 | Spare |
| 120 | 100 | 1D9A4 | 1DA6B | Momentum Unload Cutoff Monitor |
| 121 | 100 | 1DA6C | 1DB33 | Spare |
| 122 | 100 | 1DB34 | 1DBFB | Spare |
| 123 | 100 | 1DBFC | 1DCC3 | Terminate and Disable Observing SCSs 131 - 135 |
| 124 | 100 | 1DCC4 | 1DD8B | Spare |
| 125 | 100 | 1DD8C | 1DE53 | Spare |
| 126 | 100 | 1DE54 | 1DF1B | Spare |
| 127 | 60 | 1DF1C | 1DF93 | Spare |

Table 3 Mission Stored Command Sequence Slot Sizes and Addresses

| SCS # | Size, Cmds | Start Address | End Address |
| --- | --- | --- | --- |
| 128 | 1830 | 32545 | 33390 |
| 129 | 1830 | 33391 | 341DC |
| 130 | 1830 | 341DD | 35028 |
| 131 | 2040 | 35029 | 36018 |
| 132 | 2040 | 36019 | 37008 |
| 133 | 2040 | 37009 | 37FF8 |
| 134 | 3 | 37FF9 | 38044 |
| 135 | 512 | 38045 | 38444 |
| 136 | 512 | 38445 | 38844 |
| 137 | 256 | 38845 | 38A44 |
| 138 | 256 | 38A45 | 38C44 |
| 139 | 256 | 38C45 | 38E44 |
| 140 | 256 | 38E45 | 39044 |
| 141 | 128 | 39045 | 39144 |
| 142 | 128 | 39145 | 39244 |
| 143 | 128 | 39245 | 39344 |
| 144 | 128 | 39345 | 39444 |
| 145 | 128 | 39445 | 39544 |
| 146 | 64 | 39545 | 395C4 |
| 147 | 64 | 395C5 | 39644 |
| 148 | 64 | 39645 | 396C4 |
| 149 | 64 | 396C5 | 39744 |
| 150 | 64 | 39745 | 397C4 |
| 151 | 64 | 397C5 | 39844 |
| 152 | 64 | 39845 | 398C4 |
| 153 | 64 | 398C5 | 39944 |
| 154 | 64 | 39945 | 399C4 |
| 155 | 64 | 399C5 | 39A44 |
| 156 | 64 | 39A45 | 39AC4 |
| 157 | 64 | 39AC5 | 39B44 |
| 158 | 64 | 39B45 | 39BC4 |
| 159 | 64 | 39BC5 | 39C44 |
| 160 | 64 | 39C45 | 39CC4 |
| 161 | 64 | 39CC5 | 39D44 |
| 162 | 64 | 39D45 | 39DC4 |
| 163 | 64 | 39DC5 | 39E44 |
| 164 | 64 | 39E45 | 39EC4 |
| 165 | 64 | 39EC5 | 39F44 |
| 166 | 64 | 39F45 | 39FC4 |
| 167 | 64 | 39FC5 | 3A044 |
| 168 | 64 | 3A045 | 3A0C4 |
| 169 | 64 | 3A0C5 | 3A144 |
| 170 | 64 | 3A145 | 3A1C4 |
| 171 | 64 | 3A1C5 | 3A244 |
| 172 | 32 | 3A245 | 3A284 |
| 173 | 32 | 3A285 | 3A2C4 |
| 174 | 32 | 3A2C5 | 3A304 |
| 175 | 32 | 3A305 | 3A344 |
| 176 | 32 | 3A345 | 3A384 |
| 177 | 32 | 3A385 | 3A3C4 |
| 178 | 32 | 3A3C5 | 3A404 |
| 179 | 32 | 3A405 | 3A444 |
| 180 | 32 | 3A445 | 3A484 |
| 181 | 32 | 3A485 | 3A4C4 |
| 182 | 32 | 3A4C5 | 3A504 |
| 183 | 32 | 3A505 | 3A544 |
| 184 | 32 | 3A545 | 3A584 |
| 185 | 32 | 3A585 | 3A5C4 |
| 186 | 32 | 3A5C5 | 3A604 |
| 187 | 32 | 3A605 | 3A644 |
| 188 | 32 | 3A645 | 3A684 |
| 189 | 32 | 3A685 | 3A6C4 |
| 190 | 32 | 3A6C5 | 3A704 |
| 191 | 32 | 3A705 | 3A744 |
| 192 | 32 | 3A745 | 3A784 |
| 193 | 32 | 3A785 | 3A7C4 |
| 194 | 32 | 3A7C5 | 3A804 |
| 195 | 32 | 3A805 | 3A844 |
| 196 | 32 | 3A845 | 3A884 |
| 197 | 16 | 3A885 | 3A8A4 |
| 198 | 16 | 3A8A5 | 3A8C4 |
| 199 | 16 | 3A8C5 | 3A8E4 |
| 200 | 16 | 3A8E5 | 3A904 |
| 201 | 16 | 3A905 | 3A924 |
| 202 | 16 | 3A925 | 3A944 |
| 203 | 16 | 3A945 | 3A964 |
| 204 | 16 | 3A965 | 3A984 |
| 205 | 16 | 3A985 | 3A9A4 |
| 206 | 16 | 3A9A5 | 3A9C4 |
| 207 | 16 | 3A9C5 | 3A9E4 |
| 208 | 16 | 3A9E5 | 3AA04 |
| 209 | 16 | 3AA05 | 3AA24 |
| 210 | 16 | 3AA25 | 3AA44 |
| 211 | 16 | 3AA45 | 3AA64 |
| 212 | 16 | 3AA65 | 3AA84 |
| 213 | 16 | 3AA85 | 3AAA4 |
| 214 | 16 | 3AAA5 | 3AAC4 |
| 215 | 16 | 3AAC5 | 3AAE4 |
| 216 | 16 | 3AAE5 | 3AB04 |
| 217 | 16 | 3AB05 | 3AB24 |
| 218 | 16 | 3AB25 | 3AB44 |
| 219 | 16 | 3AB45 | 3AB64 |
| 220 | 16 | 3AB65 | 3AB84 |
| 221 | 16 | 3AB85 | 3ABA4 |
| 222 | 16 | 3ABA5 | 3ABC4 |
| 223 | 16 | 3ABC5 | 3ABE4 |
| 224 | 16 | 3ABE5 | 3AC04 |
| 225 | 16 | 3AC05 | 3AC24 |
| 226 | 16 | 3AC25 | 3AC44 |
| 227 | 16 | 3AC45 | 3AC64 |
| 228 | 16 | 3AC65 | 3AC84 |
| 229 | 16 | 3AC85 | 3ACA4 |
| 230 | 16 | 3ACA5 | 3ACC4 |
| 231 | 16 | 3ACC5 | 3ACE4 |
| 232 | 16 | 3ACE5 | 3AD04 |
| 233 | 16 | 3AD05 | 3AD24 |
| 234 | 16 | 3AD25 | 3AD44 |
| 235 | 16 | 3AD45 | 3AD64 |
| 236 | 16 | 3AD65 | 3AD84 |
| 237 | 16 | 3AD85 | 3ADA4 |
| 238 | 16 | 3ADA5 | 3ADC4 |
| 239 | 16 | 3ADC5 | 3ADE4 |
| 240 | 16 | 3ADE5 | 3AE04 |
| 241 | 16 | 3AE05 | 3AE24 |
| 242 | 16 | 3AE25 | 3AE44 |
| 243 | 16 | 3AE45 | 3AE64 |
| 244 | 16 | 3AE65 | 3AE84 |
| 245 | 16 | 3AE85 | 3AEA4 |
| 246 | 16 | 3AEA5 | 3AEC4 |
| 247 | 16 | 3AEC5 | 3AEE4 |
| 248 | 16 | 3AEE5 | 3AF04 |
| 249 | 16 | 3AF05 | 3AF24 |
| 250 | 16 | 3AF25 | 3AF44 |
| 251 | 16 | 3AF45 | 3AF64 |
| 252 | 16 | 3AF65 | 3AF84 |
| 253 | 16 | 3AF85 | 3AFA4 |
| 254 | 16 | 3AFA5 | 3AFC4 |
| 255 | 16 | 3AFC5 | 3AFE4 |

Table 4 Safe Modes Summary Flow Chart

# Stored Command Sequence Description

Some of the following material has been excerpted from DM05, Software Requirements Specification. Refer to DM05 for more detail on the FSW SCS processing subfunction.

Stored Command Sequences (SCSs) are blocks of one or more commands stored in OBC memory. These SCSs can contain Absolute Time Sequences (ATSs) or Relative Time Sequences (RTSs).  An ATS is a stored command sequence to be issued at a specific time (based on the OBC VCDU count converted to Major Frame/Minor Cycle). Examples of ATSs used at the OCC are the three daily load sequence pairs, SCS slots 128 through 133.  An RTS is a stored command sequence to be issued after a particular time increment has elapsed since the issuance of a previous command or after an event wait occurrence set in an SCS. An RTS can also be activated by ground command. SCS control commands can be interleaved with ATSs or RTSs in an SCS. SCSs, not containing ATSs, can be repeatable.

The commands stored in SCSs can be satellite hardware commands (e.g., to be sent to the CTU to control the spacecraft or command the payload), commands for the flight software (e.g., enable/disable software functions, enter certain states, direct the software to perform a specific action like turning on or off a particular software feature or function, or to set a bit in memory), and commands to control the SCS.  Satellite hardware commands are 28-bit commands containing an RCTU address, the command type, and the 21-bit command.  All stored commands (except stored SCS control commands) are routed to the Command Processing Subfunction. In the next minor cycle, these commands are interpreted as if they were ground commands, but the command accept or reject counter is not incremented.

Table 5 shows the SCS state transitions and the possible errors from invalid SCS transitions. Figure 1 shows the SCS State Transition Diagram.  There are four operational states for SCSs. An SCS can be active, inactive, suspended or disabled.  A specific SCS can be terminated if it is active and all active ground SCSs can be terminated with the “terminate all ground SCSs” command.  An active SCS can be processed by the OFP every minor cycle.  An inactive SCS is not processed.  An SCS can be temporarily suspended and then resumed or terminated as long as it is active and timing conflicts do not exist.

Table 5 SCS State Transitions

|  | Command |
| --- | --- |
| State | Activate | Terminate | Suspend | Resume | Enable | Disable | Call |
| Active | E | Inactive | Suspended | E | E | Disabled | *SCS Runs |
| Inactive | Active | E | E | E | E | Disabled | SCS Runs |
| Suspended | E | Inactive | E | Active | E | Disabled | *SCS Runs |
| Disabled | E | E | E | E | Inactive | E | X |
|  | E = Log an OBC Error, Request Ignored (Invalid SCS Transition, Error Code 0408 + Data) |
|  | X = No Error, Request Ignored |
|  | * A separate instance of the SCS runs in parallel with Active or Suspended SCS |

SCS Error Code Deciphering:

| FFFF | FFFF | CCCC | PP | EE | DDDD | DDDD |
| --- | --- | --- | --- | --- | --- | --- |

F – Major Frame

C – Minor Cycle

P – On-Board Flight Program (OFP) Process = 04 hex ( CCDM Partition 2

E – Error Code = 08 hex ( Invalid SCS Transition

D – Error Log Data Field = Hex of 32-bit OBC command that generated error

| SCS State Transition Command | Error Log Entry Hex* |
| --- | --- |
| Activate | FFFF FFFF CCCC 0408 X840 SSRR |
| Terminate | FFFF FFFF CCCC 0408 X841 SS00 |
| Suspend | FFFF FFFF CCCC 0408 X842 SS00 |
| Resume | FFFF FFFF CCCC 0408 X843 SS00 |
| Enable | FFFF FFFF CCCC 0408 X844 SS00 |
| Disable | FFFF FFFF CCCC 0408 X845 SS00 |

* F-Major Frame,    C-Minor Cycle,    X - Don’t Care,    S – SCS ID,    R – Repeat Count

SCSs are activated, terminated, suspended, resumed, enabled, or disabled by OBC software commands from the ground, another SCS or another flight software function. An SCS can suspend or terminate itself via internal SCS control commands.  When an SCS is activated, it can be executed once (repeat count = 0), be repeated a specified number of times (repeat count = 1-254) or be repeated forever (repeat count = 255).

In addition to the triggering of SCSs by invocation, the control of issuing the stored commands, embedded in active SCSs, can be modified through SCS internal commands (i.e. commands that cannot be sent from the ground. See Table 6). These deal primarily with the timely issuance of the stored hardware commands or the OBC software commands.  Delay commands can be interleaved in such a way as to provide an absolute delay or a relative delay between the commands, otherwise up to 20 commands per minor cycle are sent to Command Processing for distribution.

An SCS Call command can be used to invoke an SCS, from another SCS, thereby suspending the calling SCS until the invoked SCS has completed.  A called SCS runs under the calling SCS priority, whereas an activated SCS runs under its own priority. So that means the activated SCS could run before, after or in parallel (interleaved) with the SCS that executed the activation. The only way that SCSs can run in parallel (if more than one is activated) is if the SCS contains time delays. When a time delay is reached in an SCS, SCS processing is allowed to executed other activated SCSs of lower priority until the delay is complete. To invoke an SCS, from another SCS, without the invoking SCS suspending, an Activate SCS can be used. Up to 5 SCSs can be “nested” in this way. Note that the Disable SCS command only disables the top most SCS of a nested group of SCSs, whereas the Terminate SCS command to the top most SCS of a nested group also terminates the occurrence of each lower level SCS in the nest. Note: Other occurrences of the lower level SCSs in other nests are not terminated.

Table 6 itemizes the SCS control commands that affect an entire SCS and those that affect the processing within an SCS plus those that have the capability for both.  All SCS commands that can act externally on an entire SCS and have the capability to be embedded in an SCS, have the same 16-bit OBC software command format whether external or embedded.

Each SCS command has an associated step number which is set and updated as the SCS is processed.  The OFP keeps track of which commands in the SCS have been processed.  The OFP can also report the status of each SCS (current state and step number) in OBC generated telemetry for up to 5 SCSs.  Once commands are in the command queue, they will be issued even if an SCS state transition occurs.

For the purposes of this handbook, the accounting for the elements of a Stored Command Sequence can be done using either “steps” or “counts”.  Both values are listed in the command list tables presented for each SCS in this document.  As suggested above, the “steps” value represents the basic block of command bits that will be processed by the OBC at one time.  The “step” being processed by the OBC is represented in telemetry using the MSIDs COSCIC01 thru COSCIC14 (Current Execution Index of Active SCS (Slot xx)).  Alternatively, the “count” value is used to identify the specific command that is defined in the ground system command databases, and is the unit of measure used to drive the command accept and reject counters reported in telemetry.  All commands, whether they be a single pre-defined command, a single command with modifiable fields, or a multi-part command, are assigned an individual/unique “count” number in the tables below.  In the cases of modifiable or multi-part commands, all of the elements of those commands will share the same “count” value.  However, the assignment of “step” values is done differently.  In the case of single pre-defined commands, the “step” value will be the same as the “count” value, since the command fits entirely within the 32-bit blocks of command bits being processed by the OBC at one time.  The same is true for single commands with modifiable fields, where in this case all of the fields for the command will have the same step number.  However, in the case of multi-part commands it is possible to have a series of step numbers assigned to the command elements, depending on the number of bits that are needed to implement the command.  Since the multi-part commands may take up several 28-bit blocks, the “step” number values roughly correspond to the number of 28-bit blocks needed to employ each of the multipart commands.  In some cases, individual elements of the multi-part command may span two different step numbers as there is no attempt to force the individual multi-part command elements to start on the 28-bit boundaries.

Figure 1 - SCS State Transition Diagram

Table 6 SCS Control Commands

| SCS Commands |  | Required State of SCS |
| --- | --- | --- |
| The following SCS Control Commands can be sent from the ground as a real-time command or can be embedded in an SCS |
| Activate SCS# | N/A | Inactive |
| *Terminate SCS# | N/A | Active/Suspended |
| Suspend SCS# | N/A | Active |
| Resume SCS# | N/A | Suspended |
| Clear SCS# | N/A | Inactive |
| Terminate All Ground SCSs | N/A | Active/Suspended |
| Enable SCS# | N/A | Disabled |
| Disable SCS# | N/A | Active/Inactive/Suspended |
| *CAUTION: It is NOT possible to directly TERMINATE a CALLED SCS. You must TERMINATE the top ACTIVATED SCS that CALLED the SCS. |
| The following SCS Control Commands can only be embedded in SCSs, they cannot be sent from the ground as real-time commands. |
| Command | Required State of Source SCS | Required State of Target SCS |
| Absolute Time Delay | Active | N/A |
| Relative Time Delay | Active | N/A |
| SCS Call | Active | Active, Inactive, Suspended** |
| Event Wait | Active | N/A |
| Set SCS Step # - Unconditional Branch | Active | N/A |
| Set Loop Counter# | Active | N/A |
| Decrement Loop Counter, Branch not=0 | Active | N/A |
| End SCS | Active | N/A |
| Halt OBC (for “protected” SCSs only) | Active | N/A |
| Branch on Event Condition | Active | N/A |
| **CAUTION: A CALLED SCS is NOT shown as ACTIVE, which is the check performed by SCS processing. Therefore note the following cases: It is possible to CALL an ACTIVE SCS, and have two instances running. It is possible to ACTIVATE a CALLED SCS, and have two instances running. It is possible to CALL a SUSPENDED SCS, and have one instance running, and one suspended. |

# Chandra Safing SCS Modifications due to H/W Reconfiguration

The following tables describe the changes required to the protected SCSs should equipment failures occur. This table is based on no failures having occurred since launch, and that the A-side boxes form the nominal equipment complement. Note that a failed box is indicated for each case, with most of the cases involving a B-side box. If the A-side box is failed, generally no change is required to the default SCS because they are already configured to fail over to the B-side.

Table 7 Safe Mode related Modifications due to H/W Reconfiguration

Safe Mode related:

| Unit | Failure | Change Required to SCS and/or Preselects - On-Orbit |
| --- | --- | --- |
| CTU | CTU-B has failed | 31 - Select CTU A & data bus A Command bus B off, A on Select A telemetry request & reply busses CTU A to format 5 Change EIA preselects to use CTU-A |
|  | CTU-A has failed | 80 Select CTU B and data bus B (new command) |
| IU | IU-B has failed | 31 - IU A select transponder A & B IU mode select mode bits to select transponder Change EIA preselects to use IU-A |
| OBC | OBC-B has failed | Change EIA preselects to use OBC-A |
| EP RCTU | EP-RCTU B has failed | 31 - B off, A on 25 - B off, A on Remove check for A ON prior to switchover |
| PC RCTU | PC-RCTU B has failed | 31 - B off, A on |
| IRU | IRU-2 has failed | 31 - IRU 2 off, 1 on IRU 1 to high range Set corresponding CPE PLR relays IRU-1 Temp controls ON IRU-2 Temp controls OFF 79 - (OK, sets both IRUs to high range) 37 - (OK, sets both IRUs to high range) |
| VDE | VDE-B has failed | 31 - VDE B off, A on Close iso #5 (vs #3) 78 - VDE B off 80 - VDE B off at beginning, on at end 34 – Select VDE side B |
| ADE | ADE-B has failed | 31 - B off, A on 23 - B off, A on 80 - Reinit ADE B EPIC counters 34 – Select ADE side B |
| SPE | SPE-B has failed | 31 - B off, A on 34 – Select SPE side B |
| IOE | IOE-B has failed | 31 - B off, A on Enable CPE via IOE-B |
| FSSA | FSSA-B has failed | 31 - B off, A on Set corresponding CPE PLR relays |
| EIA | EIA Channel 0 Failed | SCS 31 contains only channel 0 commands for the following. The SCS would have to be changed to use channel 1 commands if channel 0 fails: PCL131EN ENAB CLOSE 1-3 (CHAN 0) PF131CL FORWARD CLOSE 1-3 (CHAN 0) PIV3F1CL CLOSE ISOVALVE 3 (WITH FORWARD CURRENT) (CHAN 0) PCL131DS DISA CLOSE 1-3 (CHAN 0) AIR2HRP1 IRU-2 HIGH RANGE PRI (CHAN 0) ACPEB1EN Enable CPE, IOE-B (Slice A4, Ch.0) |

Table 8 Non-Safe Mode related Modifications due to H/W Reconfiguration

Non-Safe Mode related:

| Unit | Failure | SCS - On-Orbit |
| --- | --- | --- |
| CPE | CPE-A has failed | 31 - Set all CPE PLR relays for CPE B |
| TS RCTU | TS-RCTU B has failed | 26 - B off, A on Remove check for A on prior to failover |
| SI RCTU | SI-RCTU B has failed | 27 - B off, A on Remove check for A on prior to failover |
| TS SEA | TS SEA B has failed | 26 - B off, A on |
| IP | IP-B has failed | 26 - B off, A on Select IP-A Select Primary Database |
|  | IP-A has failed | 31 – Select Secondary Database 80 – Select Secondary Database NOTE: The proper database selection was left out of these safing actions. If we stay on IP-B, the primary database should be patched to reflect the appropriate B-side calibrations. |
| TS MCE | TS MCE-A has failed | 31 – Select Secondary OTG source 80 – Select Secondary OTG source 82 – Use All MCE-B commands for OTG emergency halt |
| SI SEA | SI SEA-A has failed | 75 – Redundant Flexure Heaters |
| Load-shed and power recovery units |  | for most, Power ON and Power OFF are in separate SCSs for Prime and Redundant Units 32 – Configured by Power SSE for the next eclipse event 33 – Configured by Power SSE for the next eclipse event 75 & 76 – restrictions on some heaters being powered simultaneously. Change a heater in 75, may have to change one in 76. Consult Thermal SSE. |
| VDE | VDE-A has failed | 120 – Modify for appropriate commanding for VDE - B |

# Chandra SCS Modifications due to Science Only Safing Action Load Splitting

Safing prior to the implementation of PR-271 for high radiation stopped the onboard mission command loads, which could have fairly quickly created undesirable conditions or constraint violations.  Maneuver-only command loads were often needed to keep Chandra "safe after safing" by maneuvering to a better attitude until recovery to nominal science operations was possible. The increasing number of constraints as the mission has progressed has led to a greater need for these "maneuver-only" loads following safing for high radiation.

Flight Software Patch PR-271 modified the CCDM subsystem part of the flight software to be compatible with a load where the "observing" commanding and "vehicle" commanding are contained in different mission SCSs.  With this “split” load, the safing subsystem response to high radiation is such that only "observing" commanding ceases when the science instruments are safed.  The "vehicle" commanding (e.g. maneuvers, eclipse handling, momentum unloads) continues after a high radiation safing event.

The basic mechanism for accomplishing the split between "vehicle" commands and "observing" commands is to put each type of command in its own SCS for execution by the OBC. Vehicle commands go into SCSs 128, 129 and 130; observing commands go into SCSs 131, 132 and 133. There is a fixed correspondence between vehicle and observing SCSs: 128 ↔ 131, 129 ↔ 132, 130 ↔ 133.  This SCS utilization scheme requires modifications to the sizes and starting addresses for a number of mission SCS slots. The sizes for SCSs 128-133 are based on estimates derived from current usage and reasonable assignment of commands into vehicle/observing categories. Note that a significant portion of "SCS space", currently unusable in SCS 130 because of a page boundary issue, can be "reclaimed" with the new size/address allocations.

To properly implement the modified safing actions, PR-271 patched several protected SCSs:

- SCS 15 (Propulsion Line Temperature Monitor Fault Safing Action) - Added "Terminate All Ground SCSs" command.

- SCS 27 (SIM RCTU Monitor Fault Safing) - Added  "Terminate All Ground SCSs" command.

- SCS 123 (Terminate and Disable Observing SCSs 131 - 135) - modified to contain the following sequence of commands:

  - Terminate SCS 131.

  - Terminate SCS 132.

  - Terminate SCS 133.

  - Terminate SCS 134.

  - Terminate SCS 135.

  - Disable SCS 131.

  - Disable SCS 132.

  - Disable SCS 133.

  - Disable SCS 134.

  - Disable SCS 135.

- SCS 107 (Main SI Safing) - replaced "Terminate All Ground SCSs" command with call to SCS 123.

- SCS 107 - added command to turn off all fiducial lights at the end.

# SCS #: 1 -- Initialize Online State

Description:

This SCS is activated called by the OBC FSW upon initialization to the online state

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is a placeholder, left over when the FSW folks anticipated they would need a few commands to initialize the on-line state.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 2 -- Safe State Transition

Description:

This SCS is activated by the OBC upon transition to safe mode.

The contents of the SCS are calls to SCS 111 for the transfer orbit phase, or to SCS 31 for the science orbit phase.

Main Steps in SCS:

Call to SCS #: 31 -- Safe Mode Reconfiguration

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

SCS 2 is hard-coded into the flight software to be called in case of safe mode entry. The safe mode response is dictated by the contents of SCS 2, which is either a call to SCS 111 during the transfer orbit, or to SCS 31 for the science orbit. As part of the LL2OO patch during OAC, a call to SCS 31 replaced the call to SCS 111.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 3 -- Deployment State Transition

Description:

This SCS gets activated by the OBC FSW upon entry to the Deployment State (activation of SCS 3 is hard-coded into the FSW).

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This was used by the FSW to activate SCS 111 when commanded to the deployment state at the beginning of the mission up until the IUS and Chandra separate.  Patch Request PR-93 resulted in SCS 3 being stubbed out so that no SCS is called if the Observatory was ever inadvertently commanded to the deployment state.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 4 -- Off-Line State Transition

Description:

This SCS was called by the OBC FSW, but was commented out long ago. It is no longer used by anyone.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 5 -- OO - CCDM RCTU Command Wrap Test

Description:

This SCS is activated when the CCDM RCTU Command Wrap Safing Monitor trips.  This monitor looks for no response from the EP RCTU and the PC RCTU.  Lack of response from either RCTU is an indication that the OBC is having communication problems, and this SCS halts the OBC to induce a failover into Safe Mode.

Main Steps in SCS:

Calls SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish halting the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.  This SCS is called because there is a communications problem between the OBC and the RCTUs which could be caused by the OBC or the cmd/data busses.  By halting the processor, a Safe Mode Transition will accomplish switching OBCs as well as the cmd/data busses (in addition to the EP and PC RCTUs).

If the CCDM RCTU Cmd Wrap Monitor trips, it is likely that any or all of the following errors will appear in the OBC Error Log:

Invalid RCTU Response (0227) will probably appear for the EP and/or the PC RCTU

Command Wrap Errors (0221) may appear for the EP or the PC RCTU

EP RCTU Monitor error (0e15) may appear, which activates SCS #: 25 -- EP RCTU Monitor Fault

PC RCTU Monitor error (0e1e) may appear, which activates SCS #: 60 -- PC RCTU Monitor Fault

CCDM RCTU Command Wrap Fault (0e01) will appear, which activates SCS #: 5 -- OO - CCDM RCTU Command Wrap Test.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 80 -- OO - Standby State Timeout.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 6 -- OO - Attitude/Rate Error Monitor Fault

Description:

This SCS is activated when the Attitude/Rate Error Safing Monitor trips.  This monitor looks for attitude errors and rate errors.

Main Steps in SCS:

Calls SCS #: 78 -- OO - Battery Connection / Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish the following:

Call SCS #: 30 -- Battery Connection to Bus Safing Action to connect the batteries to the bus

Turn off VDE A

Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  All are required to ensure proper safing following an attitude error or a rate error.

When the Attitude/Rate Error Safing Monitor trips, an error code of 0E02 will appear in the OBC Error Log, and OBC Health and Status will activate SCS 6.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL – SCS NUMBER -- SCS Number | 78 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 7 -- OO - IRU Monitor Fault Safing Action

Description:

This SCS is activated when the IRU Fault Safing Monitor trips.  This monitor protects against gyro failures by performing two tests:

- Miscompare:  Compares 4 gyro outputs to see if they are consistent

- Zero output:  Watches for lack of output pulses from the gyro.

Main Steps in SCS:

Call SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish the following:

Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  All are required to ensure proper safing following an IRU failure.

When the IRU Monitor trips, an error code of 0E03 will appear in the OBC Error Log, and OBC Health and Status will activate SCS 7.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 8 -- OO - Sun Position Monitor Fault Safing Action

Description:

This SCS is activated when the Sun Position Safing Monitor trips.  This monitor protects against sun in the HRMA sun exclusion region and on the ACIS radiator.  It uses CSS data and, if available, FSS data to compute the projection of the sun in the spacecraft XY plane and check this against pre-defined limits.  It also compares the CSS data against the FSS data for consistency.

Main Steps in SCS:

Call SCS #: 78 -- OO - Battery Connection / Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish the following:

Call SCS #: 30 -- Battery Connection to Bus Safing Action to connect the batteries to the bus

Turn off VDE A

Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  All are required to ensure proper safing following an attitude error or a rate error.

When the Sun Position Monitor trips, an error code of 0e04 will appear in the OBC Error Log, and OBC Health and Status will activate SCS 8.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 78 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action

Description:

This SCS is activated when the Spacecraft Momentum Safing Monitor trips.  This monitor protects against stuck thruster faults.  It compares integrated thruster torques against actual momentum changes as measured by reaction wheel tachs and gyro rates.

Main Steps in SCS:

Call SCS #: 78 -- OO - Battery Connection / Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish the following:

Call SCS #: 30 -- Battery Connection to Bus Safing Action to connect the batteries to the bus

Turn off VDE A

Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  All are required to ensure proper safing following an attitude error or a rate error.

When the Spacecraft Momentum Monitor trips, an error code of 0e05 will appear in the OBC Error Log, and OBC Health and Status will activate SCS 9.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 78 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 10 -- OO - Attitude Reference in Eclipse Monitor

Description:

This SCS is activated when the Attitude Reference in Eclipse Safing Monitor trips.  This monitor detects loss of stars in the Aspect Camera Assembly.

Main Steps in SCS:

Call SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish halting the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase only.  SCS 10 does not apply to the Transfer Orbit phase since the Aspect Camera Assembly is not yet operational.

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.

When the Attitude Reference in Eclipse Monitor trips, an error code of 0e06 will appear in the OBC Error Log, and OBC Health and Status will activate SCS 10.

This SCS defaults to disabled upon OBC reset, and is enabled by ground command in preparation for the On-Orbit Phase.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 11 -- OO - EPS Sunlight Overload Fault

Description:

This SCS is activated when the Bus Overload Safing Monitor (aka SOL Monitor) trips.  This monitor is tripped after the EPS software has detected an unexpected connection of the batteries in sunlight and was unsuccessful at disconnecting the batteries following a load shed.

Main Steps in SCS:

Call SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish halting the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.

When the Bus Overload Monitor trips, the following errors will be observed in the OBC Error Log:

Unexpected Connection of the Batteries (0e14) (aka Safing EPS Battery Disconnect) will appear, which activates SCS #: 24 -- Unexpected Connection of the Batteries

Invalid SCS Transition (0408) may appear showing that SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands was terminated when it wasn’t running

Invalid SCS Transition (0408) may appear showing that SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands was terminated when it wasn’t running

Invalid SCS Transition (0408) may appear showing that SCS #: 33 --  was terminated when it wasn’t running

Invalid SCS Transition (0408) may appear showing that SCS 33 was enabled even though it was already enabled

Sunlight Overload Fault (0e07) (aka Safing EPS Unexpected Connection) will appear, and OBC Health and Status will activate SCS 11.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 12 -- OO - EPS Eclipse Overload Fault

Description:

This SCS is activated when the Eclipse Overload Safing Monitor (aka EOL Monitor) trips.  This monitor checks the battery State of Charge against a trend line.  If two of three batteries fall below the trend line, the Eclipse Overload (EOL) fault flag is set.

Main Steps in SCS:

Call SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to accomplish halting the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.

When Eclipse Overload Monitor trips, the Eclipse overload error (0e08) (aka Safing EPS Battery Polarity)  will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 12.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 13 -- OO - PCAD Sensor Processing Fault

Description:

This SCS is activated when the CSS/FSS/IRU Data Validity Monitor trips.  This monitor checks data validity status from the IOE and the CCDM equipment.  If these units indicate that the data are invalid, the Data Validity Monitor sets a fault flag which triggers this SCS.

Main Steps in SCS:

Call SCS #: 77 -- OO - Halt OBC Safing Action, which is a “common” SCS called by a number of Safing Actions to halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.

When the PCAD Data Validity Monitor trips, the PCAD Sensor Processing error (0e09) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 13.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 14 -- OO - RW Unloading Monitor Fault

Description:

This SCS is activated when the Reaction Wheel Unloading Monitor trips.  This monitor helps protect against a failed VDE or loss of an IRU in NSM by checking the magnitude of the total spacecraft momentum.  Normally, the OBC RW unloading logic will automatically attempt to unload the reaction wheels to zero momentum if the magnitude exceeds 40.0 ft-lb-sec (if the autounloading feature is enabled).  However, if the momentum exceeds a limit of 60 ft-lb-sec, the monitor will set a fault flag that will ultimately lead to a safe mode transition.

Main Steps in SCS:

Call SCS #: 30 -- Battery Connection to Bus Safing Action to connect the batteries to the bus

Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that the batteries get connected and that the final action is to Halt the Processor.

When the RW Unloading Monitor trips, the Safing PCAD RW Unloading error (0e0a) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 14.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSOHALT | SCS HALT OBC |  |  |  |  |  |  |  | LR | OBC |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 15 -- Propulsion Line Temperature Monitor Fault Safing Action

Description:

This SCS is activated by the Propulsion Line Temperature Monitor when a fault condition is present in order to trigger Normal Sun Mode

Main Steps in SCS:

- Terminate all Ground SCSs

- Disable PCAD Subfunction 37 – Propulsion Line Temperature Monitor

- Activate SCS #: 79 -- OO - NSM Transition.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSs |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSD | PCAD_Subfunction | 37 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 79 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 16 -- Attitude Reference in Sunlight Monitor

Description:

This SCS is activated when the attitude reference is lost in while in sunlight.  This monitor detects loss of stars in the Aspect Camera Assembly field of view.  The logic for this function is part of the OBC Health and Status Safing Actions.  If the ACA_Sequence flag is set to FALSE due to the inability of the ACA sequence routine to find sufficient guide-, acquisition- or bright-stars and the EPS management has set the F_Eclipse flag to SUN, then this SCS will be activated.

Main Steps in SCS:

Step 1:  Terminate all ground SCS’s.  This doesn’t disable them.  The desire is to stop absolute time tagged command sequences which change the mission configuration such as maneuvers, SIM movement, etc.

Steps 2-10:  Enable/reinitialize the IRU, sun position, attitude/rate error, s/c momentum, RW momentum, RW unloading, and solar array position monitors and the solar array control law.  Normally, these functions are already enabled, so the purpose is to reinitialize these functions.

Step 11:  Activate SCS #: 79 -- OO - NSM Transition which contains commands for entry to Normal Sun Mode.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase only.  SCS 16 does not apply to the Transfer Orbit phase since the Aspect Camera Assembly is not yet operational.  The Transfer Orbit version contains only an End SCS command.

Constraints/Considerations:

If this SCS is modified, be sure that the final action is to call SCS 79.  Failure to terminate mission SCS’s may result in maneuvers from unknown starting points or exposing an SI to a potentially harmful X-ray source.

When the Attitude Reference in Sunlight Monitor trips, an error code of 0e0c will appear in the OBC Error Log, and OBC Health and Status will activateSCS#: 16.

This SCS defaults to disabled upon OBC reset, and is enabled by ground command in preparation for the On-Orbit Phase prior to Normal Point Mode operation.

There is no monitor to disable.  The only way to disable this function is to disable this SCS.  If this safing action is disabled, PCAD will be left in Normal Point Mode holding on gyro’s.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 34 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 38 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 23 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 79 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 17 -- RW #1 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #1 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE1OF | WDE-1 PWR CONV OFF |  | AWDE1X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 18 -- RW #2 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #2 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE2OF | WDE-2 PWR CONV OFF |  | AWDE2X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 19 -- RW #3 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #3 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE3OF | WDE-3 PWR CONV OFF |  | AWDE3X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 20 -- RW #4 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #4 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE4OF | WDE-4 PWR CONV OFF |  | AWDE4X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 21 -- RW #5 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #5 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE5OF | WDE-5 PWR CONV OFF |  | AWDE5X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 22 -- RW #6 Fault Handling

Description:

This SCS is activated when a problem is detected with RW #6 or its associated Wheel Drive Electronics (WDE).

PCAD operation can tolerate the failure of up to 2 reaction wheels and respective WDEs.  It is a design goal to avoid safe mode for a RW failure. Therefore when a problem is detected, the problem wheel is deactivated and Chandra controls with the remaining 5 wheels.

Main Steps in SCS:

- Disable all the other 5 reaction wheel fault SCSs to prevent inadvertent shutdown of any other wheels. The risk is that all wheels could be shut down inadvertently when only one wheel is at fault.

- Disable reaction wheel torque commands to the affected wheel.

- Disable the reaction wheel bias. This is required in order to increase the momentum storage envelope under 5 wheel control, which is what Chandra will be controlling with if one of these RW SCSs is activated.

- Re-initialize the Spacecraft Momentum Monitor (PCAD sub-function 32)

- Turn of the affected wheel drive electronics

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit phase

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | CODISAS1 | CODISASX - SCS NUMBER -- | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | CODISAS1 | CODISASX - SCS NUMBER -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISAS1 | CODISASX - SCS NUMBER -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | CODISAS1 | CODISASX - SCS NUMBER -- | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CODISAS1 | CODISASX - SCS NUMBER -- | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 0 AND 5 | 5 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AORENA | ENABLE DISABLE FLAG -- 1=ENABLE 0=DISABLE | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AWDE6OF | WDE-6 PWR CONV OFF |  | AWDE6X | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 23 -- OO - SADA Position or Temperature Monitor Fault

Description:

This SCS is activated when the SADA Position or Temperature Monitor trips.  The position monitor protects against a failed ADE by comparing the SADA resolvers to the open loop SADA  control position estimate and triggering the safing action if the difference is greater than 5 deg. for either SADA.  The temperature monitor is triggered if either SADA temperature exceeds 172 deg. F. The glitch filter is 8.2 sec for both monitors.  These thresholds represent the current settings and may be adjusted.

Main Steps in SCS:

Step 1:  Terminate all ground SCS’s.  This doesn’t disable them.  The desire is to stop absolute time tagged command sequences which change the mission configuration such as maneuvers, SIM movement, etc.

Step 2:  Set the PCAD mode to standby.  This suspends attitude control.

Step 3:  Enable/reinitialize the solar array control law.  This causes the solar array control to set the estimated SADA position to the resolver reading when the PCAD mode goes to Normal Sun Mode.

Steps 4 & 5:  Disable the SADA Position and Temperature monitors.

Steps 6-19:  Set software ADE selection to B.  Turn off ADE A, turn on ADE B, and configure the ADE EPIC excitation and step clocks.

Steps 20-24:  Enable/reinitialize the IRU, sun position, s/c momentum, RW momentum and RW unloading.  Normally, these functions are already enabled, so the purpose is to reinitialize these functions.

Activate SCS #: 79 -- OO - NSM Transition which:

Sets the IRU’s to high range.

Sets the yaw bias to zero, the solar array control and sun mode to auto,  disables RW momentum bias, and commands PCAD to NSM.

Terminates the SI safing SCS and then run the SI safing SCS (SCS #: 107 -- Main SI Safing).

What Phase is this SCS used in? What Patches are Required for Normal Operations?

On-orbit phase.

Constraints:

If this SCS is modified, be sure that the final action is to activate SCS 79.  Also, failure to terminate mission SCS’s may result in maneuvers from unknown starting points or exposing an SI to a potentially harmful X-ray source.

When the SADA position or temperature monitors trip, error code 0E13 will be observed in the OBC Error Log, and OBC Health and Status will activate SCS #: 23 -- OO - SADA Position or Temperature Monitor Fault.  The specific monitor that tripped the safing action may be determined from the fault status word in the error log.

This SCS defaults to disabled upon OBC reset and is automatically enabled by SCS #: 118 -- OBC Reset Reconfiguration Tasks which is called by SCS #: 80 -- OO - Standby State Timeout when the OBC is reset and not in safe mode.

This safing action may be disabled by either disabling the monitor or the safing action.  It is preferable to disable the monitor to avoid filling the error log.  If this safing action is disabled, the spacecraft is vulnerable to power problems such as bus overvoltage.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOSBMODE | OBC SET PCAD MODE STANDBY |  | AOPCADMD | STBY |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSE | PCAD Subfunction for EN | 23 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AOPCADSD | PCAD_Subfunction | 35 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOPCADSD | PCAD_Subfunction | 36 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AOADEB | SELECT ADE SIDE B |  | AOADESEL | B |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | ADEAOF | ADE-A PWR OFF |  | ADEAPWR | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | ADEAOF | ADE-A PWR OFF |  | ADEAPWR | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | ADEBON | ADE-B PWR ON |  | ADEBPWR | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | ADEBON | ADE-B PWR ON |  | ADEBPWR | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3IN | ADE-B INIT, CT3, SELECT 4.096 MHZ (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADBC3A |  | AOADBC3C |  | AOADBC3E |  | PC | SD |  |  |  |  |
| 15-16 | 15 | ADEBO3_1 | ADEBO3IN Data Bits D13 to D0 of Data Field -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_3 | ADEBO3IN Least Significant Word and First Command Word -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_4 | ADEBO3IN Filler bit -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_5 | ADEBO3IN Address Part of Data Field -- Address part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_6 | ADEBO3IN Channel Part of Data Field -- Channel part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_7 | ADEBO3IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-16 | 15 | ADEBO3_8 | ADEBO3IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4IN | ADE-B INIT, CT3, DIVIDE BY 166 (24.67 KHZ) (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADBC3A |  | AOADBC3C |  | AOADBC3E |  | PC | SD |  |  |  |  |
| 17-18 | 16 | ADEBO4_1 | ADEBO4IN Data Bits D13 to D0 of Data Field -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_3 | ADEBO4IN Least Significant Word and First Command Word -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_4 | ADEBO4IN Filler bit -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_5 | ADEBO4IN Address Part of Data Field -- Address part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_6 | ADEBO4IN Channel Part of Data Field -- Channel part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_7 | ADEBO4IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-18 | 16 | ADEBO4_8 | ADEBO4IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3IN | ADE-B INIT, CT3, SELECT 4.096 MHZ (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADBC3A |  | AOADBC3C |  | AOADBC3E |  | PC | SD |  |  |  |  |
| 20-21 | 18 | ADEBO3_1 | ADEBO3IN Data Bits D13 to D0 of Data Field -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_3 | ADEBO3IN Least Significant Word and First Command Word -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_4 | ADEBO3IN Filler bit -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_5 | ADEBO3IN Address Part of Data Field -- Address part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_6 | ADEBO3IN Channel Part of Data Field -- Channel part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_7 | ADEBO3IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20-21 | 18 | ADEBO3_8 | ADEBO3IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4IN | ADE-B INIT, CT3, DIVIDE BY 166 (24.67 KHZ) (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADBC3A |  | AOADBC3C |  | AOADBC3E |  | PC | SD |  |  |  |  |
| 22-23 | 19 | ADEBO4_1 | ADEBO4IN Data Bits D13 to D0 of Data Field -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_3 | ADEBO4IN Least Significant Word and First Command Word -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_4 | ADEBO4IN Filler bit -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_5 | ADEBO4IN Address Part of Data Field -- Address part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_6 | ADEBO4IN Channel Part of Data Field -- Channel part of the data field |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_7 | ADEBO4IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-23 | 19 | ADEBO4_8 | ADEBO4IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 20 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 20 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 21 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 21 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 22 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 22 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 23 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 23 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 24 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 24 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 34 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 25 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 25 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 79 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 25 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 30 | 26 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 24 -- Unexpected Connection of the Batteries

Description:

This SCS is used when the OBC detects an unexpected charge or discharge relay connect problem. The EPS fault handling software detects the problem and sets the Batt_Disconnect fault flag. The action is to let EPS FSW try and fix the problem, while Chandra is commanded to terminate the mission SCSs and transition PCAD to Normal Sun Mode.

Main Steps in SCS:

- Terminate all ground SCSs

- Activate SCS #: 79 -- OO - NSM Transition which:

Sets the IRU’s to high range.

Sets the yaw bias to zero, the solar array control and sun mode to auto,  disables RW momentum bias, and commands PCAD to NSM.

Terminates the SI safing SCS and then run SCS #: 107 -- Main SI Safing.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit phase.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COACTS1 | COACTSX - SCS NUMBER – SCS Number | 79 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 25 -- EP RCTU Monitor Fault

Description:

This SCS is activated when the EP RCTU Monitor trips.  This monitor protects against a failed EP RCTU, or if the RCTU has been shut down by an SEU.

Main Steps in SCS:

(See attached flow chart)  Check to see if the SCS was triggered due to a wrap fault, or an EPS fault.  If it was an EPS fault, fail over the converter and telemetry processor, and initialize EPS.

If a wrap fault occurred, check to see which RCTU is on.  If Prime is on, cycle Prime RCTU converter power, else cycle the redundant power

Initialize EPS and wait two seconds

Check to see if the wrap fault has cleared.  If yes, exit.  If no, and Prime converter is on, fail over the converter and telemetry processor, and initialize EPS.  Else, exit.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during all Mission Phases.

Constraints:

If this SCS is edited, be sure that the RCTU is brought back on line within one second of the failure.  Many other protected SCSs are designed with this one second value in mind.  Commands that go through this RCTU are doubled up with one second delays between them in the event that the RCTU is shut down by an SEU.

When the EP RCTU Monitor trips, the EPS TLM Error Or Cmd Wrap error (0e15) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 25.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 80 -- OO - Standby State Timeout and SCS #: 118 -- OBC Reset Reconfiguration Tasks.

Flow SCS 25-1 EP RCTU Monitor Fault

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 23 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CEPPCPOF | RCTU-EP PRI CONV PWR OFF |  | CTUEPA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CEPPCPOF | RCTU-EP PRI CONV PWR OFF |  | CTUEPA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | CEPPCPON | RCTU-EP PRI CONV PWR ON |  | CTUEPA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | CEPPCPON | RCTU-EP PRI CONV PWR ON |  | CTUEPA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 10 | 10 | COSBRCH | SCS SET STEP# (I.E.UNCONDITIONAL BRANCH) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSBRCH1 | COSBRCH - SCS STEP -- SCS Step Number | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | CEPRCPOF | RCTU-EP RED CONV PWR OFF |  | CTUEPB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | CEPRCPOF | RCTU-EP RED CONV PWR OFF |  | CTUEPB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | CEPRCPON | RCTU-EP RED CONV PWR ON |  | CTUEPB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | CEPRCPON | RCTU-EP RED CONV PWR ON |  | CTUEPB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 18 | 18 | EOINISET | Set initialization flag to true |  | EGCTTEL3 | OVRT |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 23 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 35 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 19 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 35 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | CEPPCPOF | RCTU-EP PRI CONV PWR OFF |  | CTUEPA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 23 | 23 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | CEPPCPOF | RCTU-EP PRI CONV PWR OFF |  | CTUEPA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 25 | 25 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | CEPRCPON | RCTU-EP RED CONV PWR ON |  | CTUEPB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 27 | 27 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | CEPRCPON | RCTU-EP RED CONV PWR ON |  | CTUEPB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 29 | 29 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | CEPTBON | RCTU-EP TLM PROC B ON (OH) |  | CEPTLMB | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 32 | CEPTBON | RCTU-EP TLM PROC B ON (OH) |  | CEPTLMB | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | EOINISET | SET EPS INIT FLAG |  | EGCTTEL3 | OVRT |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 36 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 26 -- TS RCTU Monitor or Telescope Thermal Control Fault

Description:

This SCS is activated when the TS RCTU Monitor trips.  This monitor protects against a failed TS RCTU, or if the RCTU has been shut down by an SEU.

Main Steps in SCS:

(See attached flow chart)  Disable Thermal Control.

Check to see if the SCS was triggered due to a wrap fault, or Thermal fault.  If it was a Thermal fault, fail over the converter, the telemetry processor, the IP, and the SEA, and re-enable/reinitialize Thermal Control.

If a wrap fault occurred, check to see which RCTU is on.  If Prime is on, cycle Prime RCTU converter power, else cycle the redundant power

Wait two seconds

Check to see if the wrap fault has cleared.  If yes, Re-enable/reinitialize Thermal Control and exit.  If no, fail over the converter the telemetry processor, the IP, and the SEA, and re-enable/reinitialize Thermal Control, and exit.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during all Mission Phases.

Constraints:

If this SCS is edited, be sure that the RCTU is brought back on line within one second of the failure.  Many other protected SCSs are designed with this one second value in mind.  Commands that go through this RCTU are doubled up with one second delays between them in the event that the RCTU is shut down by an SEU.

When the TS RCTU Monitor trips, the telescope thermal alarm or TS Cmd Wrap error (0e16) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 26.

When this SCS was originally generated, the command to select the secondary database for use with the redundant IP and SEU swap was left out. The secondary equipment will work with the prime database selected, but this configuration should be corrected if it is decided that the secondary equipment will be used for operations. There is no danger to the OBA or HRMA for any length of time using the prime database with the secondary equipment, however the system is not optimized in this configuration.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 80 -- OO - Standby State Timeout and SCS #: 118 -- OBC Reset Reconfiguration Tasks.

Flow SCS 26-1 TS RCTU Monitor Fault

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4OTTCPDS | TEL THERMAL CONTROL PROCESS DISABLE |  | 4OTCPEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | 4OHMTCDS | DISABLE HRMA THERMAL CONTROL |  | 4OACHRMH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4OOBTCDS | DISABLE OBA THERMAL CONTROL |  | 4OACOBAH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 25 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 23 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 21 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 14 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | CTSPCPOF | RCTU-TS PRI CONV PWR OFF |  | CTUTSA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | CTSPCPOF | RCTU-TS PRI CONV PWR OFF |  | CTUTSA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | CTSPCPON | RCTU-TS PRI CONV PWR ON |  | CTUTSA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | CTSPCPON | RCTU-TS PRI CONV PWR ON |  | CTUTSA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 13 | 13 | COSBRCH | SCS SET STEP# (I.E.UNCONDITIONAL BRANCH) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSBRCH1 | COSBRCH - SCS STEP -- SCS Step Number | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | CTSPCROF | RCTU-TS RED CONV PWR OFF |  | CTUTSB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 15 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | CTSPCROF | RCTU-TS RED CONV PWR OFF |  | CTUTSB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 17 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | CTSPCRON | RCTU-TS RED CONV PWR ON |  | CTUTSB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | CTSPCRON | RCTU-TS RED CONV PWR ON |  | CTUTSB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 25 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 52 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | CTSPCPOF | RCTU-TS PRI CONV PWR OFF |  | CTUTSA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | CTSPCPOF | RCTU-TS PRI CONV PWR OFF |  | CTUTSA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | CTSPCRON | RCTU-TS RED CONV PWR ON |  | CTUTSB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | CTSPCRON | RCTU-TS RED CONV PWR ON |  | CTUTSB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | CTSTPBON | RCTU-TS TLM PROC B ON (OH) |  | CTSTLMB | ON |  |  |  |  | TS | HLP |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | CTSTPBON | RCTU-TS TLM PROC B ON (OH) |  | CTSTLMB | ON |  |  |  |  | TS | HLP |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 4IPSPADS | IP A: DISABLE SECONDARY PWR CONV |  | 4IPIRAX | DISA | 4IP5AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | 4IPSPADS | IP A: DISABLE SECONDARY PWR CONV |  | 4IPIRAX | DISA | 4IP5AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 4IPSPBEN | IP B: TURN ON -- ENAB SECONDARY PWR CONV |  | 4IPIRBX | ENAB | 4IP5BV |  |  |  | TS | HLP |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41 | 41 | 4IPSPBEN | IP B: TURN ON -- ENAB SECONDARY PWR CONV |  | 4IPIRBX | ENAB | 4IP5BV |  |  |  | TS | HLP |  |  |  |  |
| 42 | 42 | 4OIPSELB | SELECT INSTRUMENTATION PROCESSOR B |  | 4OCDIPSL | IP_2 |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | 44 | 4SESP1DS | SEA 1: DISA SECONDARY POWER CONV |  | 4S1IRX | DISA | 4SP51V |  |  |  | TS | HLP |  |  |  |  |
| 45 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 46 | 46 | 4SESP1DS | SEA 1: DISA SECONDARY POWER CONV |  | 4S1IRX | DISA | 4SP51V |  |  |  | TS | HLP |  |  |  |  |
| 47 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 48 | 48 | 4SESP2EN | SEA 2: TURN BOX ON -- ENAB DC/DC CONV |  | 4S2IRX | ENAB | 4SP52V |  |  |  | TS | HLP |  |  |  |  |
| 49 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 50 | 50 | 4SESP2EN | SEA 2: TURN BOX ON -- ENAB DC/DC CONV |  | 4S2IRX | ENAB | 4SP52V |  |  |  | TS | HLP |  |  |  |  |
| 51 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 52 | 52 | 4OTTCPEN | TEL THERMAL CONTROL PROCESS ENABLE |  | 4OTCPEN | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | 4OHMTCEN | ENABLE HRMA THERMAL CONTROL |  | 4OACHRMH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 55 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 55 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 94 |  |  |  |  |  |  |  |  |  |  |  |  |
| 56 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 9 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 27 -- SIM RCTU Monitor Fault Safing

Description:

This SCS is activated when the SIM RCTU Monitor trips.  This monitor protects against a failed SI RCTU, or if the RCTU has been shut down by an SEU.

Main Steps in SCS:

See attached flow chart:

- Terminate all Ground SCSs

- Check to see which RCTU is on.  If Prime is on, cycle Prime RCTU converter power, else cycle the redundant power

- Wait two seconds

- Check to see if the wrap fault has cleared.  If it has not cleared, and the prime converter is indicated on, then there is a possible failure of the prime converter. Turn off the prime converter, and turn on the redundant converter and telemetry processor. If the wrap test has cleared, then the prime converter is back on.

- Either branch leads to the Terminate SCS #: 107 -- Main SI Safing, delay 3 MF, and call SCS 107, then exit.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during all Mission Phases.

This SCS was patched to replace the call SCS 81 statement with the call SCS 107 statement as part of the SI safing enhancement.

Constraints:

If this SCS is edited, be sure that the RCTU is brought back on line within one second of the failure.  Many other protected SCSs are designed with this one second value in mind.  Commands that go through this RCTU are doubled up with one second delays between them in the event that the RCTU is shut down by an SEU.

When the SI RCTU Monitor trips, the SI Cmd Wrap error (0e17) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 27.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 80 -- OO - Standby State Timeout and SCS #: 118 -- OBC Reset Reconfiguration Tasks.

Flow SCS 27-1 SIM RCTU Monitor Fault

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSs |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CSIPOF | RCTU-SI PRI CONV PWR OFF |  | CTUSIA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | CSIPOF | RCTU-SI PRI CONV PWR OFF |  | CTUSIA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CSIPON | RCTU-SI PRI CONV PWR ON |  | CTUSIA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | CSIPON | RCTU-SI PRI CONV PWR ON |  | CTUSIA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COSBRCH | SCS SET STEP# (I.E.UNCONDITIONAL BRANCH) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSBRCH1 | COSBRCH - SCS STEP -- SCS Step Number | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | CSIROF | RCTU-SI RED CONV PWR OFF |  | CTUSIB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 13 | 13 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | CSIROF | RCTU-SI RED CONV PWR OFF |  | CTUSIB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 15 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | CSIRON | RCTU-SI RED CONV PWR ON |  | CTUSIB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 17 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | CSIRON | RCTU-SI RED CONV PWR ON |  | CTUSIB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 26 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 33 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 22 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 33 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | CSIPOF | RCTU-SI PRI CONV PWR OFF |  | CTUSIA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 23 | 23 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | CSIPOF | RCTU-SI PRI CONV PWR OFF |  | CTUSIA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 25 | 25 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | CSIRON | RCTU-SI RED CONV PWR ON |  | CTUSIB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 27 | 27 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | CSIRON | RCTU-SI RED CONV PWR ON |  | CTUSIB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 29 | 29 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | CSITBON | RCTU-SI TLM PROC B ON (OH) |  | CSITLMB | ON |  |  |  |  | SI | HLP |  |  |  |  |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 32 | CSITBON | RCTU-SI TLM PROC B ON (OH) |  | CSITLMB | ON |  |  |  |  | SI | HLP |  |  |  |  |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1536 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 28 -- Bright Star or Commanded Attitude Monitor

Description:

This SCS is used in one of two events: 1) the PCAD mode has transitioned to Bright Star Hold, meaning that the spacecraft has lost the ability to identify a known attitude reference from the stars it sees, but still has the ability to hold attitude on bright stars 2) The commanded attitude monitor has tripped, meaning that the spacecraft determined that the next command quaternion would put the spacecraft into a known exclusion zone if allowed to execute. The response by this SCS is also governed on whether an additional SCS is enabled or not.

For observations where the sun is in the fine sun sensor FOV, SCS 98 is disabled, and after the call to SCS 98 is ignored, SCS 99 is activated. SCS 99 has only the Activate SCS 107 in it, so in essence Chandra would hold on bright stars but safe all the instruments.

For observations where the sun is NOT in the fine sun sensor FOV, then SCS 98 is enabled. If the monitor trips, SCS 98 gets called, and performs tasks that include transitioning Chandra to Normal Sun Mode. SCS 98 also contains the commands to disable SCS 99, so SCS 99 never gets a chance to run. SCS 98 via SCS 79 has the commands to safe the instrument.

Refer to flow chart FLOW SCS 28-1 for a quick overview.

Main Steps in SCS:

- Terminate all ground mission SCSs.

- Disable PCAD subfunction 38, which is the command attitude monitor (cmd_att_mon)

- Call SCS #: 98 -- Bright Star Normal Sun Mode. This SCS is normally disabled for observations that have the sun in the fine sun sensor field of view. SCS 98 Calls SCS #: 79 -- OO - NSM Transition then disables SCS 99 to keep it from running when the SCS processing returns to SCS 28 after this call. Therefore if the sun is in the field of view, on the next command, SCS 99, gets activated

- Activate SCS #: 99 -- Bright Star SI Safing. This SCS only contains an activate SCS #: 107 -- Main SI Safing command.

- End SCS.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This is used in the on-orbit phase.

Constraints:

SAFE MODE or OBC RESET note: This SCS must be remain disabled during safe mode recovery until the proper ephemeris time offset has been uplinked via patch.

Flow SCS 28-1 Function Flow

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTRMALL | TERMINATE ALL GROUND SCSS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSD | PCAD_Subfunction | 38 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 98 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 99 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 29 – Eclipse Load Control SCS

Description:

This SCS is used during eclipse season.  During normal configuration, this SCS monitors the EPS eclipse flag “F-Eclipse” and when TRUE, will run SCS #: 32 -- Eclipse Entry.  There is also a penumbra only configuration which is used during a Penumbra eclipse.

Main Steps in SCS:

Nominal Configuration

- Wait on flag F-Eclipse.

- When F-Eclipse Flag True, call SCS #: 32 -- Eclipse Entry.

Penumbra Configuration

- Set Eclipse entrance timeout.

- Set eclipse timeout (Lower Bound)

- Set eclipse timeout2 (Upper Bound).

- Branch on flag F_Eclipse_1st flag

- Relative Time Delay

- Branch on EPS_INTERFACE.FAULT_Indicator = EPS_INTERFACE_TYPES.Batt_Disconnect (TRUE when 2 or more batteries connected)

- Activate SCS #: 32 -- Eclipse Entry

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit phase.

Constraints:

None

Normal Configuration

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSEVTWT | EVENT WAIT (SCS ONLY) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | COSEVTW1 | Event Number in K Constant Table | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COACTS1 | COACTSX - SCS NUMBER – SCS Number | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

Penumbra Only Configuration

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1-3 | 1 | EOECLETO | Eclipse Entrance Timeout (ST) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | EOECLET1 | EOECLETO Header |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | EOECLET2 | EOECLETO Commands Following |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | EOECLET3 | EOECLETO Filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | EOECLET4 | EOECLETO Timeout Period | 7024 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 2 | EOECLSTO | Eclipse Timeout (ST) Lower Bound |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 2 | EORCLTO1 | EOECLSTO - Header |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 2 | EORCLTO2 | EOECLSTO - Number of words |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 2 | EOECTS3 | EOECLSTO - Fixed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 2 | EOECTS24 | EOECLSTO - Lower Bound | 4683 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 3 | EOECLST2 | Eclipse Timeout2 (Upper Bound) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 3 | EORCLT21 | EOECLST2 - Header |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 3 | EORCLT22 | EOECLST2 – Number of Words |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 3 | EORCLT23 | EOECLST2 – Filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 3 | EORCLT24 | EOECLST2 - Timeout | 5151 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 4 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 4 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 4 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 4 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 6 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 6 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 6 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 6 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 7 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 7 | COACTS1 | COACTSX - SCS NUMBER – SCS Number | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 7 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 8 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 30 -- Battery Connection to Bus Safing Action

Description:

This safing SCS is used as an intermediate step by several monitors. This SCS contains conditional event branches that check to see if a battery is disabled or not by the flight software. It performs this check to make sure that a battery already disabled is not connected to the bus. A disabled battery has failed in some way, and should not be used.

A check is made for each battery. If the check is passed, then the K1, K2 and K5 relays for each battery are set to the closed position, connecting the battery to the bus and placing full charge on the batteries. If the check is not passed, then the K-relay commands are bypassed.

Main Steps in SCS:

Conditional event checks for each battery.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This is used in the on-orbit phase.

This SCS is used by the following SCSs:

SCS #: 6 -- OO - Attitude/Rate Error Monitor Fault

SCS #: 8 -- OO - Sun Position Monitor Fault Safing Action

SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action

SCS #: 14 -- OO - RW Unloading Monitor Fault

Constraints:

Unlike most safing SCSs, this one did not get built with doubled up commands. However, that is not a problem as long as we have 3 good batteries. If a single command did not get through to connect a battery, Chandra can operate on 2 batteries. If however sometime in the mission we have to disable a battery to prevent it from being used, then this SCS should be patched to double up the commands to connect the batteries. This would preclude a situation where only ONE good battery gets connected because of a single dropped command.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | EB1K1CL | BATT 1 K1 CLOSE |  | EB1K1 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | EB1K2CL | BATT 1 K2 CLOSE |  | EB1K2 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | EB1K5ON | BATT 1 K5 ON |  | EB1K5 | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 14 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 15 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | EB2K1CL | BATT 2 K1 CLOSE |  | EB2K1 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | EB2K2CL | BATT 2 K2 CLOSE |  | EB2K2 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | EB2K5ON | BATT 2 K5 ON |  | EB2K5 | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 15 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | EB3K1CL | BATT 3 K1 CLOSE |  | EB3K1 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 17 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | EB3K2CL | BATT 3 K2 CLOSE |  | EB3K2 | CLOS |  |  |  |  | EP | HLP |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | EB3K5ON | BATT 3 K5 ON |  | EB3K5 | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 31 -- Safe Mode Reconfiguration

Description:

This is the main SCS that is used to reconfigure Chandra into Safe Mode during On-Orbit Operations.  It is activated when the OBC enters State 4, the Safe Mode State (see Figure 1).  This SCS is executed by the new On-Line OBC, as determined by the EIA preselects.

This SCS was modified to call the SI safing SCS 107 as part of the SI safe mode enhancement.

Refer to Table 4 Safe Modes Summary Flow Chart for more information on safe mode actions.

Main Steps in SCS:

- Select the CTU B, data bus B, and telemetry request and reply bus B.  Switch to redundant equipment to remove the potential cause of the Safe Mode transition.

- Turn off command bus A to avoid potential for collisions caused by ground operators sending commands over the A bus.  Turn on command bus B.

- Turn off prime EP and PC RCTU converters.  Turn on redundant EP and PC RCTU converters and telemetry processors.

- Enable EP and PC RCTU wrap monitors and corresponding safing actions SCS #: 25 -- EP RCTU Monitor Fault & SCS #: 60 -- PC RCTU Monitor Fault.  SEUs can occur even while in Safe Mode.  Safing SCSs will cycle converter power to return the RCTU to operation within one second.

- Turn off VDE A.

- Enable and close isovalve 3 (with forward current).

- Turn off:

  - Gyros 1 and 2 in IRU 2,

  - IRU 2 temperature controls, and

  - IRU 2.

- Reset the corresponding CPE power loss recovery relays: GYRO SEL B1 = NO, GYRO SEL B2 = NO.

- Turn on IRU 1 and set IRU 1 to High Range in preparation for CPE-controlled Safe Sun Mode or RCS SSM.  Turn on Gyros 1 and 2 in IRU 1, and corresponding IRU temperature controls.

- Reset the corresponding CPE power loss recovery relays: GYRO SEL A1 = YES, GYRO SEL A2 = YES.

- Turn on VDE B.

- Turn off A side of the following units, and turn on the B side:  ADE, SPE, IOE, FSSA.

- Reset CPE power loss recovery relay to reflect FSSA B.

- Select CTU format 5.

- Select EPS OBC subformat to allow uninterrupted CPE commanding.

- Enable the CPE via IOE B to allow the CPE to control.

- Resync the CPE to external sync.  During the transition to Safe Mode, CPE lost external sync and transitioned to internal sync (ALT).  A non-checksummed memory load to the CPE is performed to command the CPE back to external sync (NORM).

- Enable Telescope Support Process, which defaults to Inactive in the OBC Safe Mode State.

- Disable Battery Thermal control, Battery Peak Power control, and OTG motion.  Enable and Initialize Telescope Thermal control, HRMA and OBA Thermal control.

- Return to Normal OBC subformat now that CPE memory loads are complete.

- Configure IU for IU B to Transponder A, 512 Kbps bit rate.

- Turn off PA-B and TX-B, and turn on PA-A and TX-A.

- IU B select Transponder A and select Transponder B.

- Initialize and Enable EPS manager.

- Enable and activate SCS #: 101 – Checksum CPE Patches to install all checksummed CPE patches.

- Enable all RCTU command wrap monitors and remaining corresponding safing SCSs SCS #: 26 -- TS RCTU Monitor or Telescope Thermal Control Fault and SCS #: 27 -- SIM RCTU Monitor Fault Safing.

- Safe Instruments by calling SCS #: 107 -- Main SI Safing.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase only.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  These commands are necessary to ensure that the Observatory is safed in the event of a Safe Mode transition, that operations continue on “B-side” hardware, and that the CPE is enabled so as to perform attitude control.

This SCS defaults to enabled upon OBC reset.  Disabling this SCS has no effect since the only time it is used is after an OBC reset, and at that time, it will be re-enabled.

All hardware commands are repeated in order to protect against an SEU.  Repeated blocks of commands to hardware through RCTU’s must be separated by a one second delay.

All EIA commands must be separated by a minimum time delay equal to the command pulse width (CARD CCDM-C-008).

All RCTU commands must be separated by at least one minor cycle (CARD CCDM-L-001).

Figure SCS 31-1.   OBC State Transition Diagram

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COCTUBB | SELECT CTU B AND DATA BUS B--Selects CTU B and Data Bus B |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CBUSADS | CMD BUS PWR A OFF / CTX DIS |  | CCTXA | DISA |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | CBUSBEN | CMD BUS PWR B ON / CTX EN |  | CCTXB | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | CBUSADS | CMD BUS PWR A OFF / CTX DIS |  | CCTXA | DISA |  |  |  |  | LR | HLP |  |  |  |  |
| 7 | 7 | CBUSBEN | CMD BUS PWR B ON / CTX EN |  | CCTXB | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | CEPPCPOF | RCTU-EP PRI CONV PWR OFF |  | CTUEPA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 10 | 10 | CEPRCPON | RCTU-EP RED CONV PWR ON |  | CTUEPB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | CTUBTQBB | CTU-B TLM REQUEST BUS SELECT B |  | CTUTMRQB | B |  |  |  |  | LR | HLP |  |  |  |  |
| 13 | 13 | CTUBTRBB | CTU-B TLM REPLY BUS SELECT B |  | CTUTMRYB | B |  |  |  |  | LR | HLP |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | CEPTBON | RCTU-EP TLM PROC B ON (OH) |  | CEPTLMB | ON |  |  |  |  | EP | HLP |  |  |  |  |
| 16 | 16 | CTUBTQBB | CTU-B TLM REQUEST BUS SELECT B |  | CTUTMRQB | B |  |  |  |  | LR | HLP |  |  |  |  |
| 17 | 17 | CTUBTRBB | CTU-B TLM REPLY BUS SELECT B |  | CTUTMRYB | B |  |  |  |  | LR | HLP |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | CPCPOF | RCTU-PC PRI CONV PWR OFF |  | CTUPCA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 20 | 20 | CPCRON | RCTU-PC RED CONV PWR ON |  | CTUPCB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | CPCTBON | RCTU-PC TLM PROC B ON (OH) |  | CPCTLMB | ON |  |  |  |  | PC | HLP |  |  |  |  |
| 23 | 23 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COWRAPED | Set RCTU Command Wrap Enable/Disable |  |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 24 | 24 | EP_RCTU | EP RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 24 | 24 | PC_RCTU | PC RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 24 | 24 | TS_RCTU | TE RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 0 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 24 | 24 | SI_RCTU | SI RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 0 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 25 | 25 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 25 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 60 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | COSLPCT | SCS SET LOOP CNTR |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | COSLPCT1 | COSLPCT - LOOP COUNTER -- Loop Counter | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | AVDEAOF | VDE-A PWR OFF |  | AVDEAX | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 29 | 29 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | PCL131EN | ENAB CLOSE 1-3 (CHAN 0) |  | PIV13C1X | ENAB | PIV13C2X | ENAB |  |  | EP | SD | 2 | 2 | 32 | K4 |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | PF131CL | FORWARD CLOSE 1-3 (CHAN 0) |  | PIV13RC1 | NORM | PIV13RC2 | NORM |  |  | EP | SD | 4 | 3 | 32 | K5 |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | PIV3F1CL | CLOSE ISOVALVE 3 (WITH FORWARD CURRENT) (CHAN 0) |  | PF1MV1C1 | CLOS | PF1MV1C2 | CLOS |  |  | EP | SD | 2 | 6 | 128 | K12 |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | PCL131DS | DISA CLOSE 1-3 (CHAN 0) |  | PIV13C1X | DISA | PIV13C2X | DISA |  |  | EP | SD | 3 | 4 | 32 | K4 |
| 37 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 6 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSDBRNZ | SCS DECREMENT AND BRANCH NON ZERO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | COSLPCT | SCS SET LOOP CNTR |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | COSLPCT1 | COSLPCT - LOOP COUNTER -- Loop Counter | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40 | 40 | AI2G1OF | IRU-2 GYRO 1 OFF |  | AIRU2G1I |  |  |  |  |  | PC | HLP |  |  |  |  |
| 41 | 41 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | AIB1CANO | IRU GYRO SEL B1 NO (PWR LOSS RECOV SETUP) , CPE-A |  | AG3SELA | NO |  |  |  |  | PC | LCC |  |  |  |  |
| 43 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | 44 | AI2G2OF | IRU-2 GYRO 2 OFF |  | AIRU2G2I |  |  |  |  |  | PC | HLP |  |  |  |  |
| 45 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 46 | 46 | AIB2CANO | IRU GYRO SEL B2 NO (PWR LOSS RECOV SETUP) , CPE-A |  | AG4SELA | NO |  |  |  |  | PC | LCC |  |  |  |  |
| 47 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 48 | 48 | AI2TCOF | IRU-2 TEMPERATURE CONTROLS (ALL) OFF |  |  |  |  |  |  |  | PC | HLP |  |  |  |  |
| 49 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 50 | 50 | AIRU2OF | IRU-2 PWR OFF |  | AIRU2 | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 51 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 52 | 52 | AIRU1ON | IRU-1PWR ON |  | AIRU1 | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 53 | 53 | AIR1HRP1 | IRU-1 HIGH RANGE PRI (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 54 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | COSDBRNZ | SCS DECREMENT AND BRANCH NON ZERO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSLPCT | SCS SET LOOP CNTR |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSLPCT1 | COSLPCT - LOOP COUNTER -- Loop Counter | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57 | 57 | AI1G1ON | IRU-1 GYRO 1 ON |  | AIRU1G1I |  |  |  |  |  | PC | HLP |  |  |  |  |
| 58 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | AIA1CAYS | IRU GYRO SEL A1 YES (PWR LOSS RECOV SETUP) , CPE-A |  | AG1SELA | YES |  |  |  |  | PC | LCC |  |  |  |  |
| 60 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 61 | AI1G2ON | IRU-1 GYRO 2 ON |  | AIRU1G2I |  |  |  |  |  | PC | HLP |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 63 | 63 | AIA2CAYS | IRU GYRO SEL A2 YES (PWR LOSS RECOV SETUP) , CPE-A |  | AG2SELA | YES |  |  |  |  | PC | LCC |  |  |  |  |
| 64 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65 | 65 | AI1G1TON | IRU-1 GYRO 1 TEMPERATURE CONTROL ON |  | AIRU1G1T |  |  |  |  |  | PC | HLP |  |  |  |  |
| 66 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 67 | 67 | AI1G2TON | IRU-1 GYRO 2 TEMPERATURE CONTROL ON |  | AIRU1G2T |  |  |  |  |  | PC | HLP |  |  |  |  |
| 68 | 68 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 68 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 69 | AI1VTCON | IRU-1 VFC TEMPERATURE CONTROL ON |  |  |  |  |  |  |  | PC | HLP |  |  |  |  |
| 70 | 70 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 70 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 71 | 71 | AVDEBON | VDE-B PWR ON |  | AVDEBX | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 72 | 72 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 72 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 73 | 73 | ADEAOF | ADE-A PWR OFF |  | ADEAPWR | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 74 | 74 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 74 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75 | 75 | ADEBON | ADE-B PWR ON |  | ADEBPWR | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 76 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 77 | 77 | ASPEAOF | SPE-A PWR OFF |  | ASPEAX | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 78 | 78 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 78 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 79 | 79 | ASPEBON | SPE-B PWR ON |  | ASPEBX | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 80 | 80 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 80 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 81 | 81 | AIOEAOF | IOE-A OFF |  | AIOEA | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 82 | 82 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 82 | 82 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 83 | 83 | AIOEBON | IOE-B ON |  | AIOEB | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 84 | 84 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 84 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 85 | 85 | AFSSAAOF | FSSA-A PWR OFF |  | AFSSAA | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 86 | 86 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 86 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 87 | AFSSABON | FSSA-B PWR ON |  | AFSSAB | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 88 | 88 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 88 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 89 | 89 | AFBCAREC | FSSA B ON/A OFF (PWR LOSS RECOVERY SETUP) , CPE-A |  | AFSSAFLG | BON |  |  |  |  | PC | LCC |  |  |  |  |
| 90 | 90 | CSELFMT5 | CTU TLM MODE CTRL SELECT FORMAT 5 |  | CTUFMTSL | FMT5 |  |  |  |  | LR | SD |  |  |  |  |
| 91 | 91 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 91 | 91 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 92 | 92 | COSDBRNZ | SCS DECREMENT AND BRANCH NON ZERO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 93 | 93 | OFMTSEPS | OBC TLM SMODE SLCT EPS DATA--OBC Telemetry Sub-Mode Format Select - EPS calculated or processed data |  | COTLRDSF | EPS |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 94 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 94 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 95 | 95 | COSLPCT | SCS SET LOOP CNTR |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 95 | 95 | COSLPCT1 | COSLPCT - LOOP COUNTER -- Loop Counter | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 96 | 96 | ACPEB1EN | Enable CPE, IOE-B (Slice A4, Ch.0) |  | ACPEB1X | ENAB | ACPEB2X | ENAB |  |  | EP | SD | 5 | 5 | 32 | K27B |
| 97 | 97 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 97 | 97 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 7 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 98 | 98 | ACMEMLCL | CPE CLEAR MEMORY LOAD BUFFER |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 99 | 99 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 99 | 99 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 100 | 100 | ACPMMLD0 | CPE Ram Load Command Header--This command specifies the first serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 100 | 100 | ACPECN02 | CPE Memory Load Header Constant -- This field is defined with a constant, a value of binary (0000 0000) - essentially a space filler since the CPE requires word pairs. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 101 | 101 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 101 | 101 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 102 | 102 | ACPMMLD1 | CPE Ram Load Command Word Count--This command specifies the second serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 102 | 102 | ACPECB12 | CPE Memory Load Checksum Bypass Flag -- This flag, when set, alerts the CPE firmware that the contents of the buffer are modifying a defined checksummed region of CPE RAM memory. A new expected checksum must be loaded in the sequence if load is performed within a checksummed region of CPE RAM memory. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 102 | 102 | ACPESQ13 | CPE Memory Load Sequence Flag -- This flag, when set, indicates that the current load buffer is the last in a sequence of load buffers or the only load buffer in a sequence. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 102 | 102 | ACPEWL14 | CPE Memory Load Word Count -- This field is used to specifiy the number of data (byte pairs) or word that follow in the load sequence. 0 represents 64 data byte pairs follow. Each data byte pair is a sequence of two commands carring the 8 MSBs and the 8 LSBs of a single CPE data word. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 103 | 103 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 103 | 103 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 104 | 104 | ACPMMLD2 | CPE Ram Load Command MSB Start Address--This command specifies the third serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 104 | 104 | ACPEAD22 | CPE Memory Load MSByte Start Address -- This field is used to specify the most significant byte of a 16-bit start address at which the data load begins. | 161 |  |  |  |  |  |  |  |  |  |  |  |  |
| 105 | 105 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 105 | 105 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 106 | 106 | ACPMMLD3 | CPE Ram Load Command LSB Start Address--This command specifies the fourth serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 106 | 106 | ACPEAD32 | CPE Memory Load LSByte Start Address -- This field is used to specify the least significant byte of a 16-bit start address at which the data load begins. | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 107 | 107 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 107 | 107 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 108 | 108 | ACPMMLD4 | CPE Ram Load Command MSB Data--This command specifies the fifth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 108 | 108 | ACPEDT42 | CPE Memory Load MSByte Of Data -- This field is used to specify the most significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 109 | 109 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 109 | 109 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 110 | 110 | ACPMMLD5 | CPE Ram Load Command LSB Data--This command specifies the sixth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 110 | 110 | ACPEDT52 | CPE Memory Load LSByte Of Data -- This field is used to specify the least significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 111 | 111 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 111 | 111 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 112 | 112 | ACPMMLD8 | Ram Load Command MSB Buffer Checksum--This command specifies the second to the last serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 112 | 112 | ACPECS82 | CPE Memory Load MSByte of Memory Buffer Checksum -- This field is used to specify the most significant byte of a 16-bit memory load buffer checksum. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 113 | 113 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 113 | 113 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 114 | 114 | ACPMMLD9 | Ram Load Command LSB Buffer Checksum--This command specifies the last serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 114 | 114 | ACPECS92 | CPE Memory Load LSByte of Memory Buffer Checksum -- This field is used to specify the least significant byte of a 16-bit memory load buffer checksum. | 239 |  |  |  |  |  |  |  |  |  |  |  |  |
| 115 | 115 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 115 | 115 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 116 | 116 | ACMEMLD | CPE COMPLETE MEMORY LOAD |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 117 | 117 | COSDBRNZ | SCS DECREMENT AND BRANCH NON ZERO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 118 | 118 | OOTSPEN | Telescope Support Process Enable |  | COTHEMEN | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 119 | 119 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 119 | 119 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 120 | 120 | 4OBATCDS | DISABLE BATTERY THERMAL CONTROL |  | 4OACBATH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 121 | 121 | 4OBAPKDS | DISABLE BATTERY PEAK POWER CONTROL |  | 4OPPMEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 122 | 122 | 4OOTGDS | DISABLE OTG MOTION |  | 4OOTGMEF | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 123 | 123 | 4OTTCPEN | TEL THERMAL CONTROL PROCESS ENABLE |  | 4OTCPEN | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 124 | 124 | 4OTELTCI | INITIALIZE TELESCOPE THERMAL CONTROL |  | 4OINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 125 | 125 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 125 | 125 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 5 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 126 | 126 | 4OTTHCDB | TELE THERM CONTROL DATA BASE SELECT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 126 | 126 | 4OTTHCD1 | 4OTTHCDB- Filler -- |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 126 | 126 | 4OTTHCD2 | 4OTTHCDB - Data Base to select -- 0-Primary Database 1-Secondary Database 2-Tertiary Database | 00 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 127 | 127 | 4OHMTCEN | ENABLE HRMA THERMAL CONTROL |  | 4OACHRMH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 128 | 128 | 4OOBTCEN | ENABLE OBA THERMAL CONTROL |  | 4OACOBAH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 129 | 129 | 4OOTGPT | SELECT OTG PRIMARY DATA SOURCE |  | 4OOTGDAS | PRI |  |  |  |  | NA | NA |  |  |  |  |
| 130 | 130 | OFMTSNRM | OBC TLM FMT SELECT - DEFAULT--OBC Telemetry Sub-Mode Format Select - Normal PCAD default telemetry |  | COTLRDSF | NORM |  |  |  |  | NA | NA |  |  |  |  |
| 131 | 131 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 131 | 131 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 930 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 132 | 132 | CIMODESL | IU MODE SELECT - BIT RATE /ENCODING--VARIABLE FIELD COMMAND THAT SELECTS ENCODING TYPE, ACA CALIBRATION, TRANSPONDER SELECTION, MODULATION SELECTION, AND BIT RATE SELECTION. UPON POWER-UP, CCSDS ENCODING IS ON, CONVOLUTION EONCODING IS ON, ACA CALIBRATION IS OFF, ACA SIDE A IS SELECTED, TRANSMITTER A DRIVER IS ENABLED, A TRANSMITTER IS SELECTED, B TRANSMITTER DRIVER IS ENABLED, B TRANSMITTER IS SELECTED, DIRECT MODULATION NRZ-L IS SELECTED, AND 512KB/S DATA RATE IS SELECTED. |  |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUENRTS | IU Mode Select Encode And Rate Command Select -- These bits select the IU Mode Select Command variable field section which is used to set CCSDS or Convolution Encoding on or off, set ACA Calibration on or off and select ACA side A or B, set transponder mode, set modulation mode, and select bit rate for transmission. Set to binary (000000). |  |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUCCSDS | IU Mode Select CCSDS Encoding On Or Off -- This bit is used to set CCSDS encoding on or off. 0 = Off, 1 = On. | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUCONVE | IU Mode Select Convolution Encoding On Or Off -- This bit is used to set Convolution encoding on or off. 0 = Off, 1 = On. | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUACASD | IU Mode Select ACA Side -- This bit is used to select ACA side A or B. 0 = Select ACA Side A, 1 = Select ACA Side B. | 0 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUACALB | IU Mode Select ACA Calibration -- This bit is used to set the IU to ACA Calibration Mode. 0 = ACA Calibration Off, 1 = ACA Calibration On. | 0 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUXPNDR | IU Mode Select Transponder -- This bit is used to select Transponder A or B side. 0 = select xmttr (A) if IU side (A) is active, select xmttr (B) if IU Side (B) is active. 1 = select xmttr (B) if IU side (A) is active, select xmttr (A) if IU side (B) is active. | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUMODUL | IU Mode Select Modulation -- These bits are used to select Modulation Mode. Binary (00) = STS Mode, 2 Kb/s. Binary (10) = DSN Subcarrier Mode, 32 Kb/s. Binary (11) = DSN Direct Modulation, rates >= 64 Kb/s. | 11 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 132 | 132 | CIUBRSEL | IU Mode Select Bit Rate -- This bits are used to select the bit rate for transmission. Binary (000) = 2 Kb/s Binary (001) = 32 Kb/s Binary (010) = 64 Kb/s Binary (011) = 128 Kb/s Binary (100) = 256 Kb/s Binary (101) = 512 Kb/s, Automatically selected when ACA Calibration mode is On. Binary (110) = 1024 Kb/s Binary (111) = Not Used | 101 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 133 | 133 | CPABOF | PA-B OFF |  | CPA2 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 134 | 134 | CPAAON | PA-A ON |  | CPA1 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 135 | 135 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 135 | 135 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 136 | 136 | CPABOF | PA-B OFF |  | CPA2 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 137 | 137 | CPAAON | PA-A ON |  | CPA1 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 138 | 138 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 138 | 138 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 139 | 139 | CTXBOF | TX-B OFF |  | CTXBX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 140 | 140 | CTXAON | TX-A ON |  | CTXAX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 141 | 141 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 141 | 141 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 142 | 142 | CTXBOF | TX-B OFF |  | CTXBX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 143 | 143 | CTXAON | TX-A ON |  | CTXAX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 144 | 144 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 144 | 144 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 145 | 145 | CIUBXPA | IU-B SELECT TRANSPONDER A (SEL 0) |  | CIUAXPNS | BA |  |  |  |  | LR | HLP |  |  |  |  |
| 146 | 146 | CIUBXPB | IU-B SELECT TRANSPONDER B (SEL 1) |  | CIUBXPNS | BB |  |  |  |  | LR | HLP |  |  |  |  |
| 147 | 147 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 147 | 147 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 148 | 148 | CIUBXPA | IU-B SELECT TRANSPONDER A (SEL 0) |  | CIUAXPNS | BA |  |  |  |  | LR | HLP |  |  |  |  |
| 149 | 149 | CIUBXPB | IU-B SELECT TRANSPONDER B (SEL 1) |  | CIUBXPNS | BB |  |  |  |  | LR | HLP |  |  |  |  |
| 150 | 150 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 150 | 150 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 151 | 151 | EOINISET | Set initialization flag to true |  | EGCTTEL3 | OVRT |  |  |  |  | NA | NA |  |  |  |  |
| 152 | 152 | EOEMGSTN | EPS Manager State (B4) Normal--Build 4 |  | EGCTTEL1 | NORM |  |  |  |  | NA | NA |  |  |  |  |
| 153 | 153 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 153 | 153 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 154 | 154 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 154 | 154 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 101 |  |  |  |  |  |  |  |  |  |  |  |  |
| 155 | 155 | COACTSX | Activate SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 155 | 155 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 101 |  |  |  |  |  |  |  |  |  |  |  |  |
| 155 | 155 | COACTS2 | COACTSX – REPEAT COUNT – Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 156 | 156 | COWRAPED | Set RCTU Command Wrap Enable/Disable |  |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 156 | 156 | EP_RCTU | EP RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 156 | 156 | PC_RCTU | PC RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 156 | 156 | TS_RCTU | TE RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 156 | 156 | SI_RCTU | SI RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 157 | 157 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 157 | 157 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 26 |  |  |  |  |  |  |  |  |  |  |  |  |
| 158 | 158 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 158 | 158 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 27 |  |  |  |  |  |  |  |  |  |  |  |  |
| 159 | 159 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 159 | 159 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 160 | 160 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 32 -- Eclipse Entry

Description:

This SCS was originally designed to perform a load shed function, reducing loads for all fault conditions. This SCS is now edited and patched by the FOT to provide the desired load levels (either turning off equipment, or turning on equipment) required for pending eclipses. In addition, this SCS implements several CARD items applicable to eclipse conditions as indicated below:

SCS 32 is now called during eclipse entry.

Main Steps in SCS:

- Disable PCAD subfunction #21, Angular Momentum Unloading Logic. This function is disabled to prevent commands from an auto-unloading event from colliding with the hardware commands following in SCS 32. This also satisfies the requirement for no auto-unloading during the eclipse event. SCS 33 contains the command to re-enable this function at eclipse exit.

- Branch on F_Short_Eclipse = TRUE (Event  32)

- IF_Short_Eclipse is TRUE, Select Telescope Tertiary Database, Re-initialize Telescope Thermal Control, Run SCS #: 71 -- RCS Catbed Heaters Prime Enable, SCS #: 72 -- RCS Catbed Heaters Redundant Enable, and SCS #: 73 -- LAE Injector Heaters Prime Enable (all 4 engines).

- End SCS Command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase only.

Constraints:

The first command in this SCS, or ahead of any calls to equipment SCSs, must be disable PCAD monitor function #21, Angular Momentum Logic.

Calls to SCSs should be separated by at least 1 minor-cycle relative time delay.

Figure SCS 32-1 Eclipse Entry

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AOFUNCDS | PCAD Subfunction Disable |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AOFUNCDS | PCAD subfunction Angular Momentum Unloading Logic | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | 4OTTCDBT | Select tertiary telescope thermal db |  | 4OTCDBSL | TRI |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 71 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 72 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 73 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 33 -- Eclipse Exit

Description:

This SCS was originally designed to perform a power recovery function, restoring loads for all fault conditions that SCS #: 32 -- Eclipse Entry had turned off. This SCS is now edited and patched by the FOT to provide the desired load levels (either turning off equipment, or turning on equipment) required after exiting eclipses or recovering from a fault condition. This SCS is a complement to SCS #: 32 -- Eclipse Entry, in that whatever loads SCS #: 32 -- Eclipse Entry adds or subtracts, this SCS nominally performs the opposite functions. The EPS software always calls SCS 33 after disconnecting the batteries from the bus in sunlight, either due to exiting from eclipse or after a fault that had connected the batteries to the bus. For this reason, SCS 33 is also used to implement several PCAD CARD items.

There are four main eclipse profiles that use SCS 32: Short, Medium, Long and Lunar.

Main Steps in SCS:

- Re-enable PCAD subfunction #30, Sun Position Monitor. This function is disabled prior to eclipse entry.

- Re-enable PCAD subfunction #31, Attitude Error and Rate Error Monitor. This function is disabled prior to eclipse entry.

- Jump to re-enabling Angular Momentum Unloading logic if Short eclipse flag is false (event 32).

- Calls to SCS #: 51 -- RCS Catbed Heaters Prime Disable, SCS #: 52 -- RCS Catbed Heaters Redundant Disable, and SCS #: 53 -- LAE Heaters Prime Disable or equipment required to add or diminish load power. Note that for short eclipses the OBA heaters use the Tertiary Database to increase the load power for a short period of time. SCS 33 would contain the commands to use the primary or secondary database after eclipse exit.

- 12-hour relative time delay. This delay is required between re-activation of the prime and redundant ISIM trim heaters. This command is not required if the ISIM prime and redundant trim heaters are not part of the loadshed (i.e. short eclipse, medium eclipse). This time delay is only used for long eclipses and is added via patching.

- Re-enable PCAD subfunction #21, Angular Momentum Unloading Logic. This is the prime method for re-enabling this function after the eclipse event.

- Enable and Activate SCS #: 29 – Eclipse Load Control SCS.

- End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase only.

Constraints:

The first two commands must always be to re-enable PCAD subfunctions #30 and #31.

The near last command in this SCS must be enable PCAD monitor function #21, Angular Momentum Logic.

Calls to SCSs should be separated by at least 1 minor-cycle relative time delay.

Figure SCS 33-1 Eclipse Exit

SCS 33 Eclipse Exit

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AOPCADSE | PCAD Subfunction for EN | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSE | PCAD Subfunction for EN | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURRED. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE COMMAND PROCESSOR WILL CONTINUE | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | 4OTTCDBP | Select Primary telescope thermal db |  | 4OTCDBSL | PRI |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 51 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 52 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 53 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | AOPCADSE | PCAD Subfunction for EN | 21 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COENASX | ENABLE SCS |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | COENAS1 | SCS # | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COACTSX | ACTIVATE SCS |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COACTS1 | SCS # | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COACTS2 | Repeat Count | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 34 -- Configure PCAD

Description:

This SCS is used to set up the OBC PCAD S/W settings with relationship to the current hardware configuration.  It is currently set up for A side equipment and using accumulated tachometer counts from the WDE’s.  These settings are used to control which sensor data is used in the OBC processing and to which actuators commands are sent.  ACA processing and commanding is not configured by this SCS.

This SCS was originally configured to be called by SCS 116 during the deployment phase. Now it is used for Safe Mode Recovery operations.

Main Steps in SCS:

- Command the OBC to select SPE-A for data retrieval (CSS and FSS).

- Command the OBC to use FSS-A misalignments for data processing.

- Command the OBC to use gyro configuration 2 k-constants in data processing.  At launch configuration 1 is set up for IRU-A and configuration 2 is set up for IRU-B.

- Command the OBC to use accumulated tachometer counts from the WDE’s rather than pulse interval counts.  This command should not be changed.  The AXAF system is designed for use of Tachometer rather than pulse interval data.  The pulse interval selection command exists primarily for diagnostics if it is ever needed.

- Command the OBC to send thruster commands to VDE-A.

- Command the OBC to send SADA commands to and to read SA resolver data from ADE-A.

- Command a one second delay to allow processing time before execution of SCS #: 35 -- Activate Sensor Processing which normally follows right on the heels of this SCS.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

No patches are required for nominal operation, however, this SCS should be patched whenever the equipment configuration for the SPE, ADE, VDE, IRU changes or FSS changes.   Changing the setup performed in this SCS is just one step required to use other than A side equipment.  Use the OP03b Vol. 4 PCAD equipment reconfiguration procedures to ensure all necessary steps are taken.

Constraints:

Do not remove 1 second delay at the end, it is needed for OBC processing to complete prior to calling SCS 35.

Do not command OBC to use RW Pulse Interval Data, performance will be degraded.

Order of commands does not matter, except the delay must come last.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AOSPEA | SELECT SPE SIDE A |  | AOSPESEL | A |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOFSSA | SELECT FINE SUN SENSOR HEAD A |  | AOFSSSEL | A |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOGYRO2 | SELECT GYRO CONFIGURATION 2 |  | AOGYRSEL | CFG2 |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AORWPULS | SET REACTION WHEEL TACH DATA TYPE PULSE |  | AORWTYPE | PULS |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOVDEA | SELECT VDE SIDE A |  | AOVDESEL | A |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AOADEA | SELECT ADE SIDE A |  | AOADESEL | A |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 35 -- Activate Sensor Processing

Description:

This SCS is designed to initialize all the sensor processing functions which run in Standby Mode (not ACA data processing which is initialized just after the ACA is turned on).  It also sets the PCAD manager state to initialize.

Main Steps in SCS:

- Enable/initialize CSSA data processing, FSSA data processing, IRU data processing, RWA data processing, and SADA data processing.

- Initialize PCAD manager.

- Delay approximately 8 seconds to allow initializations to complete prior to running any other SCS.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS was originally called by SCS 116 PCAD/MUPs activation during the transfer orbit.  It is called just after SCS #: 34 -- Configure PCAD.  It is normally followed by SCS 36 Enter Standby Mode.  No patches are required for normal operations.

This SCS is now used as part of a recovery to OBC operations from Safe Mode.  It is not equipment dependent, so no changes are required in the event of equipment configurations.

Constraints:

Sensor Processing subfunction initialization is not order dependent, but must come before the command to set the PCAD manager state to Initialize.

The 8 second delay at the end is required to allow sensor processing to complete prior to running SCS 36.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | AORWTQED | ENABLE/DISABLE RW TORQUE CMD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AORWTQED | RW WHEEL NUMBER -- WHEEL NUMBER BETWEEN 1 AND 6 (Wheel number -1 from 0-5) | 5 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AORWFIL1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | AORENA | ENABLE DISABLE FLAG -- 0=DISABLE 1=ENABLE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AOPCADSE | PCAD Subfunction for EN | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | AOSWINIT | OBC INIT PCAD |  | AOMGRSTA | INIT |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 125 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 36 -- Enter Standby Mode

Description:

This SCS  enables all the sub-functions necessary for standby mode, initializes all commanded parameters necessary for standby mode, and commands standby mode entry.  It also initializes quite a few commanded parameters which are not strictly necessary for standby mode operation such as: ACA Processing commanded parameters, S/C ephemeris parameters, maneuver parameters, dither parameters, momentum unloading parameters, delta-v burn parameters, solar array control mode and thruster selection.  An attempt was made to initialize all commanded parameters in the PCAD OBC S/W in either SCS 36 or SCS #: 37 -- OO - Normal Sun Mode First Entry even if they will be updated by the ground prior to their first use.  This is to prevent any accidental use of un-initialized parameters.

Main Steps in SCS:

- Initialize sub-functions necessary for SBM operation: Target Reference, CSS Sun Vector, FSS Sun Vector, S/C Angular Rate, Kinematic Integration, S/C Ephemeris Computation, Sun Ephemeris Computation, and Reaction Wheel Momentum Monitor.

- Command Acquisition Star, Guide Star, Bright Star and Fid Light Parameters to default values.

- Initialize all ACA images windows to active.

- Set ACA integration time to the default value, approximately .7 seconds.

- Enable Stellar Aberration Correction.

- Command OBC to send commands to PEA-A.

- Initialize the S/C ephemeris

- Set maneuver parameters for transfer orbit maneuvers on wheels.

- Set dither parameters to default values.

- Set the autonomous momentum unloading limit to 27.9 ft-lb-sec and the desired system momentum vector to (0.0,0.0,0.0) ft-lb-sec.

- Set the solar array mode to autonomous control (as opposed to ground control).

- Set the Thruster selection for momentum unloading to MUPs thrusters.

- Initialize the DV burn duration to 0.0 seconds.

- Command Standby Mode.

- Delay 2.05 seconds to allow the transition to Standby Mode to Complete.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS was originally called by SCS 116 MUPs/PCAD activation prior to IUS separation and just following SCS 35.  It is used to enter SBM for the first time.  All commands are to the OBC software and are not hardware dependent.  If this SCS is called after the IPS activation and prior to the IPS shutdown, the ground will want to command the thruster selection to RCS to take advantage of RCS unloading.  No patches are expected for Normal operations or contingencies.

This SCS is now used as part of a recovery to OBC operations from Safe Mode.

Constraints:

Many commands are included just to initialize the commanded software parameters.  Steps 1, 7, 14, and 15 are the only ones required for standby mode operation.

Although the commanded attitude monitor is nominally scheduled for SBM, it is not enabled for the standby mode 1st entry because the on-board attitude estimate and solar ephemeris have not yet been initialized.  Do not include initialization of the commanded attitude monitor in this SCS.

The two-second delay at the end is to allow time for the sub-functions to initialize and the transition to SBM to take place, do not remove it.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACQPAR | UPDATE ACQUISITION STAR REFERENCE PARAMETERS (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 9 | AOACQPR1 | Update Acquisition Star Reference Parameters Command 1 -- 1st command of a multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACQPR2 | Update Acquisition Star Reference Parameters Command 2 -- 2nd command of multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOAFLR5 | AOAFLR5 spare – filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACQADJ | Acq_F_Adjust -- Type of adjustment to make to acquisition star search Parmeters (brightness or position or none) | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACSZSF | Acq_Size_SF -- Acquisition Size Threshold | 665 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACTHSF | Acq_Thresh_SF -- Acquisition Threshold Scale Factor | 2200 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOAFLR6 | AOAFLR6 spare – filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACQSEL | Acq_Select -- Acquisition Select | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACDELY | Acq_Delta_Y_Thresh -- Threshold used for identifying pairs of acquisition stars see DM05 to identify acquisition stars | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9-14 | 9 | AOACDELZ | Acq_Delta_Z_Thresh -- Threshold used for identifying pairs of acquisition stars see DM05 to identify acquisition stars | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUIPAR | UPDATE GUIDE STAR REFERENCE PARAMETERS (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15-20 | 10 | AOGUIPR1 | AOGUIPR1 Update Guide Star Reference Parameters Command 1 -- 1st command word of a multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUIPR2 | AOGUIPR2 Update Guide Star Reference Parameters Command 1 -- 2nd command word of a multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUSZTH | Guide_Size_SF -- Guide Star Search Box Size Scale Factor | 665 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUTHSF | Guide_Thresh_SF -- Guide Star Minimum Magnitude Threshold Scale Factor | 2200 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGFLR7 | AOGFLR7 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUIDIM | Guide_Dimension -- Guide Star Search Box Dimension | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGFLR8 | AOGFLR8 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUIRES | Guide_High_Res -- High Resolution Flag | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGFLR9 | AOGFLR9 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUISEL | Guide_Sel -- Guide Star Brightness/Position Indicator | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUDELY | Guide_Delta_Y_Thresh -- Threshold used for identifying guide stars | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15-20 | 10 | AOGUDELZ | Guide_Delta_Z_Thresh -- Threshold used for identifying guide stars | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDPAR | UPDATE FIDUCIAL LIGHT REFERENCE PARAMETERS (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21-26 | 11 | AOFIDPR1 | AOFIDPR1 Update Fid Light Reference Parameters Command 1 -- 1st command word of a multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDPR2 | AOFIDPR2 Update Fid Light Reference Parameters Command 1 -- 2nd command word of a multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFISZSF | Fid_Size_SF -- Fid Light Search Box Size Scale Factor | 665 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFITHSF | Fid_Thresh_SF -- Fid Light Minimum Magnitude Scale Factor | 2200 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFLR10 | AOFLR10 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDDIM | Fid_Dimension -- Fid Light Search Box Dimension | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFLR11 | AOFLR11 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDRES | Fid_High_Res -- Fid Light High Resolution Flag | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFLR12 | AOFLR12 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDSEL | Fid_Sel -- Fid Light Brightness/Position Indicator | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDELY | Fid_Delta_Y_Thresh -- Fid Light Y Position Threshold | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21-26 | 11 | AOFIDELZ | Fid_Delta_Z_Thresh -- Fid Light Z Position Threshold | 9.7e-05 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOBRIPAR | UPDATE BRIGHT STAR REFERENCE PARAMETERS (MULT-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27-30 | 12 | AOBRIPR1 | Update Bright Star Parameters Command 1 -- 1st Command of a Multi-part command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOBRIPR2 | Update Bright Star Parameters Command 2 -- 2nd command of a Multi-part Command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOFLR13 | AOFLR13 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOBRIMAX | Bright_Max_Mag -- Bright Star Maximum Magnitude | 3123 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOFLR14 | AOFLR14 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27-30 | 12 | AOBRIMIN | Bright_Min_Mag -- Bright Star Minimum Magnitude | 1536 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 13 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 13 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 13 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 13 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 14 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 14 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 14 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 14 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 15 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 15 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 15 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 15 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 16 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 16 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 16 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 16 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 17 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 17 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 17 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 17 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 18 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 18 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 18 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 18 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 19 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 19 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 19 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 19 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 20 | AOIMSTAT | ACTIVATE/DEACTIVATE IMAGE WINDOW |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 20 | AOWINDOW | Image Window Number -- Number for the image window being enabled or disabled | 7 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 20 | AOFLR15 | AOFLR15 spare -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 20 | AOACTIVE | Image Window Status -- Status for each image window | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39-41 | 21 | AOSETINT | SET ACA INTEGRATION TIME |  | AOACINTT |  |  |  |  |  | NA | NA |  |  |  |  |
| 39-41 | 21 | AOSTINT1 | Set Integration Time Cmd 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39-41 | 21 | AOSTINT2 | Set integration Time Cmd 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39-41 | 21 | AOACACMD | ACA Command Code -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39-41 | 21 | AOACTIME | ACA Integration Time -- Integration Time : lsb = 1/4 minor cycle | 0000000101100 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39-41 | 21 | AOFLR16 | AOFLR16 spare -- filler |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | 22 | AOSTABFT | SET STELLAR ABERRATION CORRECTION FLAG/TRUE |  | AOABERRN | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 23 | AOPEAA | OBC SELECT PEA SIDE A |  | AOPEASEL | A |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOEPHUPS | UPDATE S/C EPHEMERIS (STORED) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOEPHEM1 | Update Ephemeris Command 1 -- 1st command of a mult-part command |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOEPHEM2 | Update Ephemeris Command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AORATIO | A2P_Ratio -- A2P Ratio - Square Root of Ratio of Apogee to Perigee Distance | 2.9842745 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOARGPER | Arg_Perigee -- Arg_Perigee - Argument of perigee | 4.714 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOECCENT | Eccentricity -- Orbital eccentricity | 7.981e-01 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AO1MINUS | Half_1mCosI -- Half ImCosI = (1-cos(i))/2 (i=orbital inclination) | 6.10085018e-02 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AO1PLUS | Half_1pCosI -- Half IpCosI = (1+cos(i))/2 (i=Orbital Inclination) | 9.38991487e-01 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOMOTION | Mean_Motion -- Mean Orbital Motion | 2.7196e-05 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOITERAT | Num_Iterations -- Number of iterations for the solution of Kepler's equation | 9 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOORBANG | Orb_Ang_Mom -- Specific Orbital Angular Momentum | 1.085171e+05 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOPERIGE | Perigee_Time -- Time of Perigee | 0.0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOASCEND | RA_Ascend_Node -- Right ascension of the ascending mode | 3.4882 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOSINI | SinI -- Sin(i) - i= orbital inclination | 4.786918e-01 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOSLR | SLR -- Semi Latus Rectum | 2.954326e+04 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44-60 | 24 | AOSQRTMU | Sqrt_Mu_A_Esq -- (Mu * a * e **2) ** 0.5 | 1.4374096e+05 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 25 | AOSTEADY | SET ATTITUDE CMD MODE STEADY |  | AOFATTMD | STDY |  |  |  |  | NA | NA |  |  |  |  |
| 62-67 | 26 | AOMANPAR | SET MANEUVER PROFILE PARAMETERS (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62-67 | 26 | AOMANPR1 | Set Maneuver profile parameters command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 62-67 | 26 | AOMANPR2 | Set Maneuver profile parameters command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 62-67 | 26 | AOJERK | Jerk_Time -- Jerk Time | 6.0e1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 62-67 | 26 | AOOMEGA | Omega_Max -- Maximum Rate | 1.309e-3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 62-67 | 26 | AOALPMAX | Alpha_Max -- Maximum Acceleration | 2.18166e-6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AODITPAR | SET DITHER PARAMETERS (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68-76 | 27 | AODITPR1 | Set Dither Parameters command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AODITPR2 | Set Dither Parameters command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AOANGP | Dither_Ang_P -- Dither angle Pitch | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AOANGY | Dither_Ang_Y -- Dither angle Yaw | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AOPHASEP | Dither_Coeff_P -- Dither phase Angle Pitch | 9.69627763e-5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AOPHASEY | Dither_Coeff_Y -- Dither phase Angle Yaw | 9.69627763e-5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AORATEP | Dither_Rate_P -- Dither rate Pitch | 4.7e-3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68-76 | 27 | AORATEY | Dither_Rate_Y -- Dither rate Yaw | 1.0e-2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 77-80 | 28 | AOMOMLIM | SET SYSTEM ANGULAR MOMENTUM LIMIT (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 77-80 | 28 | AOMOMLM1 | Set system angular momentum limit command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 77-80 | 28 | AOMOMLM2 | Set system angular momentum limit command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 77-80 | 28 | AOMOMLIM | Mom_Tot_Lim -- Total system momentum limit for angular momentum unloading | 2.79e1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 29 | AOMUNLMO | OBC SET ANGULAR MOMENTUM UNLOADING STATE MONITOR |  | AOUNLOAD | MON |  |  |  |  | NA | NA |  |  |  |  |
| 82-87 | 30 | AODESMOS | SET DESIRED SPACECRAFT ANGULAR MOMENTUM (Stored)--There are Real and Stored Versions of this command |  | AOSYMOM1 |  | AOSYMOM2 |  | AOSYMOM3 |  | NA | NA |  |  |  |  |
| 82-87 | 30 | AODESMS1 | Set Desired System Angular Momentum Command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 82-87 | 30 | AODESMS2 | Set Desired System Angular Momentum Command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 82-87 | 30 | AODESMS3 | Mom_Tot_Cmd(1) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 82-87 | 30 | AODESMS4 | Mom_Tot_Cmd(2) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 82-87 | 30 | AODESMS5 | Mom_Tot_Cmd(3) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 88 | 31 | AOSAMAUT | OBC SET SOLAR ARRAY MODE AUTONOMOUS |  | AOSAMDGD | AUTO |  |  |  |  | NA | NA |  |  |  |  |
| 89 | 32 | AOMUPSEL | SELECT THRUSTERS MUPS |  | AOFTHRST | MUPS |  |  |  |  | NA | NA |  |  |  |  |
| 90-93 | 33 | AODVBURN | SET DELTA V BURN DURATION (MULTI-PART) |  | AODVTIME |  |  |  |  |  | NA | NA |  |  |  |  |
| 90-93 | 33 | AODBURN1 | Set Delta-V Burn Time Command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 90-93 | 33 | AODBURN2 | Set Delta-V Burn Time Command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 90-93 | 33 | AOBTIME | DV_Duration -- Burn time duration | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 94 | 34 | AOSBMODE | OBC SET PCAD MODE STANDBY |  | AOPCADMD | STBY |  |  |  |  | NA | NA |  |  |  |  |
| 95 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 95 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 96 | 36 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 37 -- OO - Normal Sun Mode First Entry

Description:

This SCS enables all the sub-functions necessary for operation in Normal Sun Mode and Normal Maneuver Mode, initializes all commanded parameters necessary for Normal Sun Mode and Normal Maneuver Mode, and commands Normal Sun Mode entry.  It also initializes quite a few commanded parameters which are not strictly necessary for Normal Sun Mode or Normal Maneuver Mode operation. An attempt was made to initialize all commanded parameters in the PCAD OBC S/W in either SCS #: 36 -- Enter Standby Mode or SCS 37 even if they will be updated by the ground prior to their first use.  This is to prevent any accidental use of un-initialized parameters.

NOTE: this SCS is not to be used for safe mode recovery to OBC control. There exists an SCS command sequence that is used for this role that is loaded into mission SCS slot 141: OBC-A: AA_SCS37_141.CLD,  OBC-B: AB_SCS37_141.CLD. Refer to the safe mode recovery procedures for more information. Refer to the RTS files for the command sequence in human-readable format.

Main Steps in SCS:

- Enable Attitude Command Generation, Attitude Error Computation, Feed-Forward Torque Computation, Pointing Control Law, Sun Mode Control Law, Transfer Orbit Control Law, Angular Momentum Unloading Logic, Reaction Wheel Control Law, Solar Array Control Law, RCS Thruster Selection Logic, Reaction Wheel Command Processing, Solar Array Command Processing, and Thruster Command Processing Sub-functions.

- Disable Delta-V Command Processing and LAE Dome Temperature Monitor.

- Enable IRU Monitor, Sun Position Monitor, Attitude Error and Rate Error Monitor, S/C Momentum Monitor, Reaction Wheel Unloading Monitor, Solar Array Position Monitor, SADA Over-temperature Monitor.

- Disable Dithering

- Enable Gravity Gradient Torque Computation (Only used in NPM)

- Enable RW Momentum Bias

- Set Yaw Rate Biases used in NSM to zero for both Sun-Point and Attitude Hold sub-modes.

- Enable Autonomous Angular Momentum Unloading

- Enable MUPs Directives, Wheel Directives and Solar Array Drive Directives

- Disable LAE Directives and RCS Directives

- Disable Autonomous transition from NMM to NPM

- Set the Sun Mode Control Law Sub-mode to Autonomous Control

- Command IRUs 1 & 2 to Hi Range Operation (repeat to ensure commands are not dropped)

- Set the PCAD Mode to NSM

- Enable Maneuvers

- Initialize Position integration for all control laws (position integration used in NPM and PFM)

- Delay 9.8 seconds to allow NSM to finish initializing prior to enabling safing actions (in 118).

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is called by SCS #: 118 -- OBC Reset Reconfiguration Tasks.  It is used on orbit for re-initializing the OBC software in the event of an OBC reset (in which case 118 is called by SCS #: 80 -- OO - Standby State Timeout).

Constraints:

The only commands necessary for starting NSM (assuming that SCS’s 34, 35 & 36 have already been called) are those in steps 1, 2, 3, 6, 7, 8, 10, 12, 13, and 14.  If a slimmed-down version of SCS 37 is used, however, all necessary parameters for NMM will not be initialized.  For use with 118, do not remove the 9.8 second delay at the end of SCS 37.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | AOPCADSD | PCAD_Subfunction | 20 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 23 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | AOPCADSD | PCAD_Subfunction | 24 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 25 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 26 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 27 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | AOPCADSD | PCAD_Subfunction | 28 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 34 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 36 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | AOPCADSD | PCAD_Subfunction | 37 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | AODSDITH | DITHERING DISABLE |  | AODITHEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | AOGGTQEN | ENABLE GRAVITY GRADIENT TORQUE COMPUTATION |  | AOFGRAVG | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | AORWMOME | ENABLE RW MOMENTUM BIAS |  | AORWBIAS | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 26-30 | 26 | AOSETYAW | SET SUN MODE CONTROL LAW YAW BIASES (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26-30 | 26 | AOSETYW1 | Set Yaw Bias Cmd 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 26-30 | 26 | AOSETYW2 | Set Yaw Bias Cmd 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 26-30 | 26 | AOYAWHLD | Sun_Yaw_Bias_Hold -- Yaw Bias Rate for Hold Submode | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26-30 | 26 | AOYAWPNT | Sun_Yaw_Bias_Point -- Yaw Bias Rate for Point Submode | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 27 | AOMUNLEN | OBC AUTONOMOUS ANGULAR MOMENTUM UNLOADING ENABLE |  | AOAUTUNL | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | AODIRCTR | OBC DIRECTIVES ENABLE/DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | AODRCTR1 | Directive Type (Real) -- 000=MUPS 001=RCS 010=RW 011=SA 100=LAE | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | AODRCTR2 | AOFLR20 spare -- filler |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | AODRCTR3 | AODIRCTR Enable/Disable Flag -- Enable/Disable Directive Flag | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 29 | AODIRCTR | OBC DIRECTIVES ENABLE/DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 29 | AODRCTR1 | Directive Type (Real) -- 000=MUPS 001=RCS 010=RW 011=SA 100=LAE | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 29 | AODRCTR2 | AOFLR20 spare -- filler |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 29 | AODRCTR3 | AODIRCTR Enable/Disable Flag -- Enable/Disable Directive Flag | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | AODIRCTR | OBC DIRECTIVES ENABLE/DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | AODRCTR1 | Directive Type (Real) -- 000=MUPS 001=RCS 010=RW 011=SA 100=LAE | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | AODRCTR2 | AOFLR20 spare -- filler |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | AODRCTR3 | AODIRCTR Enable/Disable Flag -- Enable/Disable Directive Flag | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | AODIRCTR | OBC DIRECTIVES ENABLE/DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | AODRCTR1 | Directive Type (Real) -- 000=MUPS 001=RCS 010=RW 011=SA 100=LAE | 3 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | AODRCTR2 | AOFLR20 spare -- filler |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | AODRCTR3 | AODIRCTR Enable/Disable Flag -- Enable/Disable Directive Flag | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | AODIRCTR | OBC DIRECTIVES ENABLE/DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | AODRCTR1 | Directive Type (Real) -- 000=MUPS 001=RCS 010=RW 011=SA 100=LAE | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | AODRCTR2 | AOFLR20 spare -- filler |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | AODRCTR3 | AODIRCTR Enable/Disable Flag -- Enable/Disable Directive Flag | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 33 | AONM2NPD | AUTONOMOUS TRANSITION FROM NMM TO NPM DISABLE |  | AOAUTTXN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 34 | AOSUNMAU | SET SUN MODE CONTROL LAW SUB MODE TO AUTO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 35 | AIR1HRP1 | IRU-1 HIGH RANGE PRI (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 40 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 37 | AIR1HRP2 | IRU-1 HIGH RANGE PRI (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 42 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 39 | AIR1HRR1 | IRU-1 HIGH RANGE RDNT (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 44 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 41 | AIR1HRR2 | IRU-1 HIGH RANGE RDNT (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 46 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 43 | AIR2HRP1 | IRU-2 HIGH RANGE PRI (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 48 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 45 | AIR2HRP2 | IRU-2 HIGH RANGE PRI (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 50 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 47 | AIR2HRR1 | IRU-2 HIGH RANGE RDNT (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 52 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 49 | AIR2HRR2 | IRU-2 HIGH RANGE RDNT (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 54 | 50 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 50 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 10 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 51 | AIR1HRP1 | IRU-1 HIGH RANGE PRI (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 56 | 52 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 52 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 53 | AIR1HRP2 | IRU-1 HIGH RANGE PRI (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 58 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 59 | 55 | AIR1HRR1 | IRU-1 HIGH RANGE RDNT (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 60 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 57 | AIR1HRR2 | IRU-1 HIGH RANGE RDNT (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 62 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 59 | AIR2HRP1 | IRU-2 HIGH RANGE PRI (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 64 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 61 | AIR2HRP2 | IRU-2 HIGH RANGE PRI (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 66 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 67 | 63 | AIR2HRR1 | IRU-2 HIGH RANGE RDNT (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 68 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 65 | AIR2HRR2 | IRU-2 HIGH RANGE RDNT (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 70 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 71 | 67 | AONSMODE | OBC SET PCAD MODE NORMAL SUN |  | AOPCADMD | NSUN |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 68 | AOMNVREN | ENABLE MANEUVERS |  | AOMVRINH | NINH |  |  |  |  | NA | NA |  |  |  |  |
| 73 | 69 | AOINTAHD | SCS POSTN INTEG DISABLE ATT_HLD CNTL LAW |  | AOCINTAH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 70 | AOINTNMD | SCS POSTN INTEG DISA NORM_MAN CNTL LAW |  | AOCINTNM | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 75 | 71 | AOINTNPE | SCS POSTN INTEG ENAB NORM POINT CNTL LAW |  | AOCINTNP | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 72 | AOINTPFE | SCS POSTN INTEG ENABLE POW_FLT CNTL LAW |  | AOCINTPF | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 77 | 73 | AOINTRMD | SCS POSTN INTEG DISABLE RCS_MAN CNTL LAW |  | AOCINTRM | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 74 | AOINTSAD | SCS POSTN INTEG DISABLE SUN_ACQ CNTL LAW |  | AOCINTSA | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 79 | 75 | AOINTSPD | SCS POSTN INTEG DISABLE SUN_PT CNTL LAW |  | AOCINTSP | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 157 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 77 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 38 – Idle ACA Windows

Description:

As discussed in Flight Note 299, ACA searches may fail or time out due to images or monitor windows being retained by the ACA from a previous observation and not commanded over for a subsequent observation.

SCS 38 contains an event wait check which waits until F_ATT_CMD=Steady  (end of the maneuver).  Following the event wait check in SCS 38, 8 directed search commands are sent to the ACA to search at the same location with the minimum search box size designated and with the brightest dimness threshold selected (magnitude=-2). The 8 search commands are virtually guaranteed to fail thus resetting the ACA windows.

Main Steps in SCS:

Event Wait for F_ATT_CMD = Steady

ACA Directed Search Commands

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the on-orbit phase

Constraints:

This SCS is activated by the Daily Load SCS as part of normal observations.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AAC1CCSC | ACA CMD CHECKSUM AND COUNT PEA1--THE ACA COMMAND CHECKSUM AND COUNT IS A 16-BIT WORD THAT IS THE FIRST COMMAND OF A GROUP OF N ACA COMMANDS (N NOT TO EXCEED 63). THIS COMMAND CONTAINS A CHECKSUM AND WORD COUNT USED IN ERROR CHECKING. IF THE CHECKSUM FOR ANY GOUP OF ACA COMMAND WORDS IS INVALID, OR IF A SYNTAX ERROR IS DETECTED IN ANY COMMAND WITHIN THE GROUP, THE ERROR SHALL BE REPORTED AND THE ACA WILL NOT EXECUTE ANY COMMAND IN THE GROUP. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 3 | 3 | AACKSUM | AACKSUM Checksum -- The MSByte of this 16-bit command word contains a checksum; computed such that the least significant eight bits of the sum of all 8-bit bytes in the group of ACA command, including the checksum and count, is zero. | 156 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AACONSTN | AACONSTN Constant -- A constant always set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AAWRDCNT | Word Count -- The Word Count contains the number of 16-bit words in an ACA Command Group (packet) that follow the ACA Command Checksum and Count command. The count cannot exceed 63 since this field is 6 bits wide. | 24 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 4-6 | 4 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-6 | 4 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 7-9 | 5 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7-9 | 5 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 10-12 | 6 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10-12 | 6 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 13-15 | 7 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-15 | 7 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 16-18 | 8 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-18 | 8 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 19-21 | 9 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19-21 | 9 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 22-24 | 10 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22-24 | 10 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AAC1SCH | ACA SEARCH CMD PEA1--THE SEARCH COMMAND IS USED TO COMMAND A SEARCH IN THE FOV OR AT DIRECTED LOCATION FOR IMAGES.THE ACA SEARCH COMMAND CONSISTS OF THREE 16-BIT WORDS. |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 25-27 | 11 | AASCHFMT | ACA Search Command Format Word -- Constant (binary 001) that identifies command as a Search Command type. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASBRITE | AASBRITE Brightness Threshold -- Brightness threshold is the Star Magnitude, an 8-bit word with the LSB representing a value of 0.0625 mag and range of [-2.00, +13.94]. Zero represents -2.0 and 255 represents +13.94. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASCNVTF | Brightest image flag -- Specifies whether brightness (=1), as opposed to position (=0) is to be used as the best image selection criteria. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASFIDLF | AASFIDLF Fiducial light flag -- Will be set true (1) only if a fiducial light is expected to be the best available image for the search region defined. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASIMNUM | AASIMNUM Image number -- Specifies where data (which image data slot) is to be reported in the OBC and aspect telemetry data. | 7 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASIMIZR | Search Region Dimension -- Specifies the size of the search region. Unsigned integer. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASZANGL | Z angle of center of search region -- Z angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASCHCON | ACA Search Constant -- Constant set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASENDF | End flag -- Set true (1) only for the last command in a continuous sequence of search commands. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASHRESF | High resolution flag -- High resolution flag for Search Region Dimension; used with Search Region Dimension (D) to specify search region size. True (1) implies half-width of search region = 20 +5D arcsec; False (0) implies half-width of search region = 20 + 40D arcsec. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASIMSZC | AASIMSZC Image size code -- Image size code: binary (00) specifies 4 x 4 pixel image for aspect data telemetry, (01) specifies modified 6 x 6 image; (10) specifies 8 x 8 image; (11) is not used. | 01 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25-27 | 11 | AASYANGL | Y angle corrdinate -- Y angle coordinate of center of search region; a 2's compliment number with one LSB representing 6.40 arc seconds. | 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 12 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 39 -- Telescope OBA Heater Zone Shutdown

Description:

This SCS turns off the OBA heater zones control.

This command sequence works by disabling the OBA heater zones software task. This command results in the OBA heaters being left in the last state they were commanded to by the flight software. The next multipart command sets all the heater zones OFF. This shuts down ALL the heaters zones, both HRMA and OBA. On the next computation cycle for this software task, the HRMA heater zones, which have not been disabled, return to normal operation.

Main Steps in SCS:

- Disable OBA thermal control (command to OBC)

- Send the multipart command to set all heater zones (both OBA and HRMA) to OFF.

- End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This command sequence is used to shut down the OBA heater zones to reduce load power demand for long eclipse passage. This command sequence does not contain any hardware commands. The commands are only to the software process, therefore they do not need to be doubled. This also means the commands are also hardware independent.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4OOBTCDS | DISABLE OBA THERMAL CONTROL |  | 4OACOBAH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 2-6 | 2 | 4OSTHTRZ | SET TELESCOPE HEATER ZONE STATES (ST) |  | 4OTSHCM1 |  | 4OTSHCM1 |  | 4OTSHCM1 |  | NA | NA |  |  |  |  |
| 2-6 | 2 | 4STHTRZ1 | 4OSTHTRZ Header -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ2 | 4OSTHTRZ Number of Comms Following -- 5 HEATER ZONE PARAMETERS. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ3[01] | 4OSTHTRZ Param -- Heater Zone Parameters | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ3[02] | 4OSTHTRZ Param -- Heater Zone Parameters | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ3[03] | 4OSTHTRZ Param -- Heater Zone Parameters | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ3[04] | 4OSTHTRZ Param -- Heater Zone Parameters | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-6 | 2 | 4STHTRZ3[05] | 4OSTHTRZ Param -- Heater Zone Parameters | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 40 -- ACIS Instrument Shutdown

Description:

This SCS performs a controlled shutdown of the ACIS

Main Steps in SCS:

- Interrupt the current science run (stop science): ACIS parameter block: AA00000000

- Turn off and disable Detector Housing Bakeout Heaters, A and B side

- Turn off and disable Detector Housing Heaters, A and B side

- Turn off and disable focal plane bakeout heaters: ACIS Parameter block: WSFT-120

- Dump system configuration: ACIS Parameter block: RS-0000001

- Turn off video boards ACIS Parameter block: ChangeConfigSetting: WSVIDALLDN

- Turn off the FEPs: ACIS Parameter block: ChangeConfigSetting: WSFEPALLDN

- Turn off and disable the DEAs, A and B side

- Turn off and disable the DPAs, A and B side

- End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in phases where long eclipses are anticipated and ACIS shutdown is required to reduce loads. SCS 32, loadshed SCS, is edited to include a call to this SCS.

The default on-board SCS for both the launch load and the on-orbit load turns off all ACIS processors. If load power is not a constraint for long eclipses, then this SCS can be edited and patched to leave the DPA on, thereby keeping the flight software and all patches intact.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center

Commands are doubled to protect against SEU upset.

At least one second between ACIS hardware commands. Note longer delay commands between command packet commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1-3 | 1 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1-3 | 1 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | COACISL4[01] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | COACISL4[02] | ACIS DATA -- | 1539 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-3 | 1 | COACISL4[03] | ACIS DATA -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 64 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5-7 | 3 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5-7 | 3 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5-7 | 3 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5-7 | 3 | COACISL4[01] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5-7 | 3 | COACISL4[02] | ACIS DATA -- | 1539 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5-7 | 3 | COACISL4[03] | ACIS DATA -- | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 5 | 1HBOAOF | HOUSING B.O. OFF A--TURNS THE SIDE A DETECTOR HOUSING BAKE OUT OFF |  | 1DABOAON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 10 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 7 | 1HBOAOF | HOUSING B.O. OFF A--TURNS THE SIDE A DETECTOR HOUSING BAKE OUT OFF |  | 1DABOAON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 12 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 9 | 1HBOADS | HOUSING B.O. DISABLE A--DISABLES THE SIDE A DETECTOR HOUSING BAKE OUT |  | 1DABOAEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 14 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 11 | 1HBOADS | HOUSING B.O. DISABLE A--DISABLES THE SIDE A DETECTOR HOUSING BAKE OUT |  | 1DABOAEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 16 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 13 | 1HBOBOF | HOUSING B.O. OFF B--TURNS THE SIDE B DETECTOR HOUSING BAKE OUT OFF |  | 1DABOBON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 18 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 15 | 1HBOBOF | HOUSING B.O. OFF B--TURNS THE SIDE B DETECTOR HOUSING BAKE OUT OFF |  | 1DABOBON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 20 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 17 | 1HBOBDS | HOUSING B.O. DISABLE B--DISABLES THE SIDE B DETECTOR HOUSING BAKE OUT |  | 1DABOBEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 22 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 19 | 1HBOBDS | HOUSING B.O. DISABLE B--DISABLES THE SIDE B DETECTOR HOUSING BAKE OUT |  | 1DABOBEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 24 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 21 | 1HHTRAOF | HOUSING HTR OFF A--TURNS THE A SIDE HOUSING HEATER OFF |  | 1DAHTAON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 26 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 23 | 1HHTRAOF | HOUSING HTR OFF A--TURNS THE A SIDE HOUSING HEATER OFF |  | 1DAHTAON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 28 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 25 | 1HHTRADS | HOUSING HTR DISABLE A--DISABLES THE A SIDE HOUSING HEATER |  | 1DAHTAEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 30 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 27 | 1HHTRADS | HOUSING HTR DISABLE A--DISABLES THE A SIDE HOUSING HEATER |  | 1DAHTAEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 32 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 29 | 1HHTRBOF | HOUSING HTR OFF B--TURNS THE B SIDE HOUSING HEATER OFF |  | 1DAHTBON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 34 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 31 | 1HHTRBOF | HOUSING HTR OFF B--TURNS THE B SIDE HOUSING HEATER OFF |  | 1DAHTBON | OFF |  |  |  |  | SI | HLP |  |  |  |  |
| 36 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 33 | 1HHTRBDS | HOUSING HTR DISABLE B--DISABLES THE B SIDE HOUSING HEATER |  | 1DAHTBEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 38 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 35 | 1HHTRBDS | HOUSING HTR DISABLE B--DISABLES THE B SIDE HOUSING HEATER |  | 1DAHTBEN | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 40 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41-47 | 37 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[01] | ACIS DATA -- | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[02] | ACIS DATA -- | 105 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[04] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[05] | ACIS DATA -- | 128 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[06] | ACIS DATA -- | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[07] | ACIS DATA -- | 106 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[08] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41-47 | 37 | COACISL4[09] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 48 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49-55 | 39 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[01] | ACIS DATA -- | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[02] | ACIS DATA -- | 105 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[04] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[05] | ACIS DATA -- | 128 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[06] | ACIS DATA -- | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[07] | ACIS DATA -- | 106 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[08] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49-55 | 39 | COACISL4[09] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 56 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57-59 | 41 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57-59 | 41 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 57-59 | 41 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57-59 | 41 | COACISL4[01] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57-59 | 41 | COACISL4[02] | ACIS DATA -- | 66 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57-59 | 41 | COACISL4[03] | ACIS DATA -- | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 61-63 | 43 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61-63 | 43 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 61-63 | 43 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 61-63 | 43 | COACISL4[01] | ACIS DATA -- | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 61-63 | 43 | COACISL4[02] | ACIS DATA -- | 66 |  |  |  |  |  |  |  |  |  |  |  |  |
| 61-63 | 43 | COACISL4[03] | ACIS DATA -- | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 64 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65-68 | 45 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL4[01] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL4[02] | ACIS DATA -- | 1541 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL4[04] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 65-68 | 45 | COACISL4[05] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 69 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70-73 | 47 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL4[01] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL4[02] | ACIS DATA -- | 1541 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL4[04] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70-73 | 47 | COACISL4[05] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 74 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 160 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 75-78 | 49 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL4[01] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL4[02] | ACIS DATA -- | 1542 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL4[04] | ACIS DATA -- | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75-78 | 49 | COACISL4[05] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 79 | 50 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 79 | 50 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80-83 | 51 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL4[01] | ACIS DATA -- | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL4[02] | ACIS DATA -- | 1542 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL4[03] | ACIS DATA -- | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL4[04] | ACIS DATA -- | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80-83 | 51 | COACISL4[05] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 84 | 52 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 52 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 96 |  |  |  |  |  |  |  |  |  |  |  |  |
| 85 | 53 | 1DEPSBOF | DEA PWR SUPPLY OFF B--TURNS THE B SIDE POWER SUPPLY TO THE DEA OFF |  | 1DEPSB | OFF | 1DEDBBON | OFF |  |  | SI | HLP |  |  |  |  |
| 86 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 55 | 1DEPSBOF | DEA PWR SUPPLY OFF B--TURNS THE B SIDE POWER SUPPLY TO THE DEA OFF |  | 1DEPSB | OFF | 1DEDBBON | OFF |  |  | SI | HLP |  |  |  |  |
| 88 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 89 | 57 | 1DEPSBDS | DEA PWR SUPPLY DISABLE B--DISABLES THE B SIDE DEA POWER SUPPLY |  | 1DEPSBX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 90 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 90 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 91 | 59 | 1DEPSBDS | DEA PWR SUPPLY DISABLE B--DISABLES THE B SIDE DEA POWER SUPPLY |  | 1DEPSBX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 92 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 92 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 93 | 61 | 1DEPSAOF | DEA PWR SUPPLY OFF A--TURNS THE A SIDE POWER SUPPLY TO THE DEA OFF |  | 1DEPSA | OFF | 1DEDBAON | OFF |  |  | SI | HLP |  |  |  |  |
| 94 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 95 | 63 | 1DEPSAOF | DEA PWR SUPPLY OFF A--TURNS THE A SIDE POWER SUPPLY TO THE DEA OFF |  | 1DEPSA | OFF | 1DEDBAON | OFF |  |  | SI | HLP |  |  |  |  |
| 96 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 96 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 97 | 65 | 1DEPSADS | DEA PWR SUPPLY DISABLE A--DISABLES THE A SIDE DEA POWER SUPPLY |  | 1DEPSAX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 98 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 98 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 99 | 67 | 1DEPSADS | DEA PWR SUPPLY DISABLE A--DISABLES THE A SIDE DEA POWER SUPPLY |  | 1DEPSAX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 100 | 68 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 100 | 68 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 101 | 69 | 1DPPSBOF | DPA PWR SUPPLY OFF B--TURNS THE B SIDE POWER SUPPLY TO THE DPA OFF |  | 1DPPSB | OFF | 1DPDBBON | OFF |  |  | SI | HLP |  |  |  |  |
| 102 | 70 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 102 | 70 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 103 | 71 | 1DPPSBOF | DPA PWR SUPPLY OFF B--TURNS THE B SIDE POWER SUPPLY TO THE DPA OFF |  | 1DPPSB | OFF | 1DPDBBON | OFF |  |  | SI | HLP |  |  |  |  |
| 104 | 72 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 104 | 72 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 105 | 73 | 1DPPSBDS | DPA PWR SUPPLY DISABLE B--DISABLES THE B SIDE DPA POWER SUPPLY |  | 1DPPSBX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 106 | 74 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 106 | 74 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 107 | 75 | 1DPPSBDS | DPA PWR SUPPLY DISABLE B--DISABLES THE B SIDE DPA POWER SUPPLY |  | 1DPPSBX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 108 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 108 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 109 | 77 | 1DPPSAOF | DPA PWR SUPPLY OFF A--TURNS THE A SIDE POWER SUPPLY TO THE DPA OFF |  | 1DPPSA | OFF | 1DPDBAON | OFF |  |  | SI | HLP |  |  |  |  |
| 110 | 78 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 110 | 78 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 111 | 79 | 1DPPSAOF | DPA PWR SUPPLY OFF A--TURNS THE A SIDE POWER SUPPLY TO THE DPA OFF |  | 1DPPSA | OFF | 1DPDBAON | OFF |  |  | SI | HLP |  |  |  |  |
| 112 | 80 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 112 | 80 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 113 | 81 | 1DPPSADS | DPA PWR SUPPLY DISABLE A--DISABLES THE A SIDE DPA POWER SUPPLY |  | 1DPPSAX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 114 | 82 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 114 | 82 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 115 | 83 | 1DPPSADS | DPA PWR SUPPLY DISABLE A--DISABLES THE A SIDE DPA POWER SUPPLY |  | 1DPPSAX | DISA |  |  |  |  | SI | HLP |  |  |  |  |
| 116 | 84 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 41 -- HRC Instrument Shutdown

Description:

This SCS performs a controlled shutdown of the HRC

Main Steps in SCS:

- Turn off the HRC-S and HRC-I MCP high voltage power supplies

- Turn off A and B side Antico Shield high voltage power supplies

- Set HRC-S MCP high voltage plate levels to zero volts

- Set HRC-I MCP high voltage plate levels to zero volts

- Set A and B side Antico shield high voltage levels to zero volts

- Turn off A and B side +5 volt power supplies

- End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in phases where long eclipses are anticipated and HRC shutdown is required to reduce loads. SCS 32, loadshed SCS, is edited to include a call to this SCS.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

A one-second delay is required between HRC commands.

Commands are doubled to protect against SEU upset. Commands are doubled individually to maintain correct command order.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2SPHVOF | SPECT DET HV OFF--TURNS OFF SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2SPONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2SPHVOF | SPECT DET HV OFF--TURNS OFF SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2SPONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMHVOF | IMAGING DET HV OFF--TURNS OFF IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2IMONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 2IMHVOF | IMAGING DET HV OFF--TURNS OFF IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2IMONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 17 | 17 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 19 | 19 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 21 | 21 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 23 | 23 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 25 | 25 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 27 | 27 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 29 | 29 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 29 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 31 | 31 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 31 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 33 | 33 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 33 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 35 | 35 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 37 | 37 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 39 | 39 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 205VAOF | +5V LV PWR SUPPLY A OFF |  | 2PS5AON | OFF | 2P05VAVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | 205VAOF | +5V LV PWR SUPPLY A OFF |  | 2PS5AON | OFF | 2P05VAVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | 205VBOF | +5V LV PWR SUPPLY B OFF |  | 2PS5BON | OFF | 2P05VBVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 46 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | 205VBOF | +5V LV PWR SUPPLY B OFF |  | 2PS5BON | OFF | 2P05VBVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 48 | 48 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 42 -- Trim Heater Prime Disable

Description:

This SCS turns off select prime-side ISIM Trim Heaters

Main Steps in SCS:

The following ISIM heaters are turned off:

| 3SMZPTDS | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HTR DISA |
| --- | --- |
| 3AC1PTDS | ACIS 1 FITTING +Z PRIME TRIM HTR DISA |
| 3AC2PTDS | ACIS 2 FITTING +Y,-Z PRIME TRIM HTR DISA |
| 3AC3PTDS | ACIS 3 FITTING -Y-Z PRIME TRIM HTR DISA |
| 3SPYPTDS | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HTR DISA |
| 3SMYPTDS | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HTR DISA |
| 3HR1PTDS | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER DISABLE |
| 3HR2PTDS | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER DISABLE |
| 3HR3PTDS | HRC 3 FITTING +Z PRIME TRIM HEATER DISABLE |
| 3RCTPTDS | RCTU PRIME TRIM HEATER DISABLE |
| 3PSMPTDS | PSMC PRIME TRIM HEATER DISABLE |
| 3FLCPTDS | FLCA PRIME TRIM HEATER DISABLE |
| 3FA6PADS | FOCUS ASSEMBLY 6 PRIME ABORT HTR DISA |
| 3FA6RADS | FOCUS ASSEMBLY 6 RDNT ABORT HTR DISA |

The ISIM Flexure heaters are turned off (heaters A, B and C)

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in phases where long eclipses are anticipated and the prime ISIM trim heater shutdown is required to reduce loads.

Constraints:

The heater commands are doubled-up as a group to protect against SEU upset. One minor cycle between adjacent commands, and 16 mc between the groups.

The SIM Flexure Heaters are doubled up, however the time delay between these commands should have been set to a minimum of 65 seconds (2 major frames). There is a possibility that one or both SIM flexure commands could be rejected by the SIM SEA. Based on a pre-launch CCB meeting, the decision was made not to correct this SCS (and SCS 75, the ON version), and instead add commands to the Long Eclipse Procedure products. The Long Eclipse Procedure, where this SCS would be used, specifically contains instructions to command the flexure heaters OFF and ON independent of SCS 42 (OFF) and SCS #: 75 -- Trim Heater Prime Enable (ON). This increases the chance that the commands will get through to the SIM SEA.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3SMZPTDS | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HEATER DISABLE |  | 3ASMZTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 3AC1PTDS | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER DISABLE |  | 3A1THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 3AC2PTDS | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER DISABLE |  | 3A2THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 3AC3PTDS | ACIS 3 FITTING +Z PRIME TRIM HEATER DISABLE |  | 3A3THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 3SPYPTDS | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER DISABLE |  | 3ASPYTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 3SMYPTDS | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER DISABLE |  | 3ASMYTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 3HR1PTDS | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER DISABLE |  | 3H1THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 3HR2PTDS | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER DISABLE |  | 3H2THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 3HR3PTDS | HRC 3 FITTING +Z PRIME TRIM HEATER DISABLE |  | 3H3PZTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | 3RCTPTDS | RCTU PRIME TRIM HEATER DISABLE |  | 3SITHTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 3PSMPTDS | PSMC PRIME TRIM HEATER DISABLE |  | 3APSMTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | 3FLCPTDS | FLCA PRIME TRIM HEATER DISABLE |  | 3FLCTHTA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 3FA6PADS | FOCUS ASSEMBLY 6 PRIME ABORT HEATER DISABLE |  | 3AZF6HTA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 3FA6RADS | FOCUS ASSEMBLY 6 REDUNDANT ABORT HEATER DISABLE |  | 3AZF6HTB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 29 | 29 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 159 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 29 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 29 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 30 | 30 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 30 | 30 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 00 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 30 | 30 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0000000000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | 3SMZPTDS | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HEATER DISABLE |  | 3ASMZTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | 3AC1PTDS | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER DISABLE |  | 3A1THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | 3AC2PTDS | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER DISABLE |  | 3A2THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 37 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | 3AC3PTDS | ACIS 3 FITTING +Z PRIME TRIM HEATER DISABLE |  | 3A3THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 39 | 39 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | 3SPYPTDS | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER DISABLE |  | 3ASPYTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 41 | 41 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | 3SMYPTDS | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER DISABLE |  | 3ASMYTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 43 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | 3HR1PTDS | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER DISABLE |  | 3H1THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 45 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | 3HR2PTDS | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER DISABLE |  | 3H2THTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 47 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | 3HR3PTDS | HRC 3 FITTING +Z PRIME TRIM HEATER DISABLE |  | 3H3PZTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 49 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 50 | 3RCTPTDS | RCTU PRIME TRIM HEATER DISABLE |  | 3SITHTRA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 51 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 52 | 3PSMPTDS | PSMC PRIME TRIM HEATER DISABLE |  | 3APSMTHA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 53 | 53 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | 3FLCPTDS | FLCA PRIME TRIM HEATER DISABLE |  | 3FLCTHTA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 55 | 55 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 55 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | 3FA6PADS | FOCUS ASSEMBLY 6 PRIME ABORT HEATER DISABLE |  | 3AZF6HTA | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 57 | 57 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | 3FA6RADS | FOCUS ASSEMBLY 6 REDUNDANT ABORT HEATER DISABLE |  | 3AZF6HTB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 59 | 59 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 59 | 59 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 60 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 60 | 60 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 159 |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 60 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 60 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 61 | 61 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 61 | 61 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 00 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 61 | 61 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0000000000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 63 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 43 -- Trim Heater Redundant Disable

Description:

This SCS turns off select redundant-side ISIM Trim Heaters

Main Steps in SCS:

The following ISIM heaters are turned off:

| Command Mnemonic | Description |
| --- | --- |
| 3SMZRTDS | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER DISABLE |
| 3AC1RTDS | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |
| 3AC2RTDS | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |
| 3AC3RTDS | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |
| 3SPYRTDS | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER DISABLE |
| 3SMYRTDS | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER DISABLE |
| 3HR1RTDS | HRC 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |
| 3HR2RTDS | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |
| 3HR3RTDS | HRC 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |
| 3RCTRTDS | RCTU REDUNDANT TRIM HEATER DISABLE |
| 3PSMRTDS | PSMC REDUNDANT TRIM HEATER DISABLE |
| 3FLCRTDS | FLCA REDUNDANT TRIM HEATER DISABLE |

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in phases where long eclipses are anticipated and the redundant ISIM trim heater shutdown is required to reduce loads.

Constraints:

The heater commands are doubled-up as a group to protect against SEU upset. One minor cycle between adjacent commands, and 16 mc between the groups.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3SMZRTDS | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER DISABLE |  | 3ASMZTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 3AC1RTDS | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3A1THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 3AC2RTDS | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3A2THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 3AC3RTDS | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |  | 3A3THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 3SPYRTDS | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER DISABLE |  | 3ASPYTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 3SMYRTDS | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER DISABLE |  | 3ASMYTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 3HR1RTDS | HRC 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3H1THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 3HR2RTDS | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3H2THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 3HR3RTDS | HRC 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |  | 3H3PZTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | 3RCTRTDS | RCTU REDUNDANT TRIM HEATER DISABLE |  | 3SITHTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 3PSMRTDS | PSMC REDUNDANT TRIM HEATER DISABLE |  | 3APSMTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | 3FLCRTDS | FLCA REDUNDANT TRIM HEATER DISABLE |  | 3FLCTHTB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 3SMZRTDS | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER DISABLE |  | 3ASMZTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 3AC1RTDS | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3A1THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 3AC2RTDS | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3A2THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | 3AC3RTDS | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |  | 3A3THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 3SPYRTDS | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER DISABLE |  | 3ASPYTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | 3SMYRTDS | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER DISABLE |  | 3ASMYTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 3HR1RTDS | HRC 1 FITTING -Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3H1THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | 3HR2RTDS | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER DISABLE |  | 3H2THTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 3HR3RTDS | HRC 3 FITTING +Z REDUNDANT TRIM HEATER DISABLE |  | 3H3PZTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | 3RCTRTDS | RCTU REDUNDANT TRIM HEATER DISABLE |  | 3SITHTRB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | 3PSMRTDS | PSMC REDUNDANT TRIM HEATER DISABLE |  | 3APSMTHB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 46 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | 3FLCRTDS | FLCA REDUNDANT TRIM HEATER DISABLE |  | 3FLCTHTB | DISA |  |  |  |  | SI | LCC |  |  |  |  |
| 48 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 44 -- ESA and ESA Heater Prime Disable

Description:

This SCS turns off the prime ESA and prime ESA heaters

Main Steps in SCS:

Turn off the Prime Earth Sensor

Turn off the Prime Earth Sensor Heaters.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn off the ESA and ESA heater circuits. The ESA and ESA heaters are no longer used during the mission following SSD opening and successful operation of the Aspect Determination System. However, these can be used for “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Do not use this SCS prior SSD opening to prevent interruption of PCAD operations.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 1 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AESAAOF | ESA-A PWR OFF |  | AESAA | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AESAAOF | ESA-A PWR OFF |  | AESAA | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | EESP1HOF | HTR BUS 9: ESA/ESE PRI DISA (CH0) |  | TESAPHT1 | DISA | TESAPHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | EESP1HOF | HTR BUS 9: ESA/ESE PRI DISA (CH0) |  | TESAPHT1 | DISA | TESAPHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | EESP2HOF | HTR BUS 9: ESA/ESE PRI DISA (CH1) |  | TESAPHT1 | DISA | TESAPHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | EESP2HOF | HTR BUS 9: ESA/ESE PRI DISA (CH1) |  | TESAPHT1 | DISA | TESAPHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 45 -- ESA and ESA Heater Redundant Disable

Description:

This SCS turns off the redundant ESA and redundant ESA heaters.

Main Steps in SCS:

Turn off the Redundant Earth Sensor

Turn off the Redundant Earth Sensor Heaters.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn off the ESA and ESA heater circuits. The ESA and ESA heaters are no longer used during the mission following SSD opening and successful operation of the Aspect Determination System. However, these can be used for “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Do not use this SCS prior SSD opening to prevent interruption of PCAD operations.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 1 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AESABOF | ESA-B PWR OFF |  | AESAB | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AESABOF | ESA-B PWR OFF |  | AESAB | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | EESR1HOF | HTR BUS 18: ESA/ESE RDNT DISA (CH0) |  | TESARHT1 | DISA | TESARHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | EESR1HOF | HTR BUS 18: ESA/ESE RDNT DISA (CH0) |  | TESARHT1 | DISA | TESARHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | EESR2HOF | HTR BUS 18: ESA/ESE RDNT DISA (CH1) |  | TESARHT1 | DISA | TESARHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | EESR2HOF | HTR BUS 18: ESA/ESE RDNT DISA (CH1) |  | TESARHT1 | DISA | TESARHT2 | DISA |  |  | EP | SD | 3 | 4 | 32 | K12A |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 46 -- Fuel Tank Heater Prime and Redundant Disable

Description:

This SCS turns off the prime and redundant Fuel Tank Heaters

Main Steps in SCS:

Commands to disable prime Tank Heater

Commands to disable redundant Tank Heater

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to shed Fuel Tank Heater loads during long earth eclipses.

Constraints:

Commands are doubled-up to prevent against SEU.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PFTPHDS | FUEL TANK HTR PRI DISA |  | EFTHTRPR | DISA |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PFTPHDS | FUEL TANK HTR PRI DISA |  | EFTHTRPR | DISA |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PFTRHDS | FUEL TANK HTR RDNT DISA |  | EFTHTRRD | DISA |  |  |  |  | EP | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PFTRHDS | FUEL TANK HTR RDNT DISA |  | EFTHTRRD | DISA |  |  |  |  | EP | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 47 -- Transmitter and Power Amp Prime Disable

Description:

This SCS turns off the prime transmitter and power amp

Main Steps in SCS:

Commands to turn off the prime Transmitter

Commands to turn of the prime Power Amplifier

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to shed transmitter and power amp loads during long earth eclipses where ground contact is not planned.

Constraints:

Do not include this SCS in SCS 32 or SCS 33 if ground contact is anticipated during the eclipse. The daily load is used to manipulate the transmitter commands.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

Transmitter must be turned off prior to Power Amp, so keep doubled-up transmitter disable commands ahead of Power Amp disable commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CTXAOF | TX-A OFF |  | CTXAX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CTXAOF | TX-A OFF |  | CTXAX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CPAAOF | PA-A OFF |  | CPA1 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CPAAOF | PA-A OFF |  | CPA1 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 48 -- Transmitter and Power Amp Redundant Disable

Description:

This SCS turns off the redundant transmitter and power amp.

Main Steps in SCS:

Commands to turn off the redundant Transmitter

Commands to turn of the redundant Power Amplifier

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to shed transmitter and power amp loads during long earth eclipses where ground contact is not planned.

Constraints:

Do not include this SCS in SCS 32 or SCS 33 if ground contact is anticipated during the eclipse. The daily load is used to manipulate the transmitter commands.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

Transmitter must be turned off prior to Power Amp, so keep doubled-up transmitter disable commands ahead of Power Amp disable commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CTXBOF | TX-B OFF |  | CTXBX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CTXBOF | TX-B OFF |  | CTXBX | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CPABOF | PA-B OFF |  | CPA2 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CPABOF | PA-B OFF |  | CPA2 | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 49 -- FLCA Prime Disable

Description:

This SCS turns off the Prime Fiducial Light Controller Assembly.

Main Steps in SCS:

FID light control command to turn off all FID lights.

Turn off the FID Light Controller Assembly

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to shed FLCA loads for long earth eclipse passage.

Constraints:

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 1 | 1 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AFLCAAOF | FLCA - A OFF |  | AFLCAAX | OFF |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AFLCAAOF | FLCA - A OFF |  | AFLCAAX | OFF |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 50 -- FLCA Redundant Disable

Description:

This SCS turns off the Redundant Fiducial Light Controller Assembly.

Main Steps in SCS:

FID light control command to turn off all FID lights.

Turn off the FID Light Controller Assembly

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to shed FLCA loads for long earth eclipse passage.

Constraints:

FLCA Off Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 1 | 1 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AFLCABOF | FLCA - B OFF |  | AFLCABX | OFF |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | AFLCABOF | FLCA - B OFF |  | AFLCABX | OFF |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 51 -- RCS Catbed Heaters Prime Disable

Description:

This SCS turns off the Prime RCS Catbed Heaters.

Main Steps in SCS:

Commands to Turn off Prime Catbed Heaters

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The RCS Catbed heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Command is doubled-up to protect against SEU upset.

16 minor cycles between doubled commands.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PCBPHOF | RCS CATBED HTR PRI OFF |  | PRCSCHPR | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PCBPHOF | RCS CATBED HTR PRI OFF |  | PRCSCHPR | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 52 -- RCS Catbed Heaters Redundant Disable

Description:

This SCS turns off the Redundant RCS Catbed Heaters.

Main Steps in SCS:

Commands to Turn off Redundant Catbed Heaters

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The RCS Catbed heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Command is doubled-up to protect against SEU upset.

16 minor cycles between doubled commands.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PCBRHOF | RCS CATBED HTR RDNT OFF |  | PRCSCHRD | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PCBRHOF | RCS CATBED HTR RDNT OFF |  | PRCSCHRD | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 53 -- LAE Heaters Prime Disable

Description:

This SCS turns off the prime LAE Injector Heaters for all four engines.

Main Steps in SCS:

Commands for Injector Heater #1 disable

Commands for Injector Heater #2 disable

Commands for Injector Heater #3 disable

Commands for Injector Heater #4 disable

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The LAE Injector heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Commands are doubled-up to protect against SEU upset.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

CAUTION: only one set of injector heaters, prime or redundant, is to be powered at any time.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PL1IHPOF | LAE 1 INJ HTR OFF PRI |  | PL1IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PL1IHPOF | LAE 1 INJ HTR OFF PRI |  | PL1IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PL2IHPOF | LAE 2 INJ HTR OFF PRI |  | PL2IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PL2IHPOF | LAE 2 INJ HTR OFF PRI |  | PL2IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | PL3IHPOF | LAE 3 INJ HTR OFF PRI |  | PL3IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | PL3IHPOF | LAE 3 INJ HTR OFF PRI |  | PL3IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | PL4IHPOF | LAE 4 INJ HTR OFF PRI |  | PL4IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | PL4IHPOF | LAE 4 INJ HTR OFF PRI |  | PL4IHPR | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 54 -- LAE Heaters Redundant Disable

Description:

This SCS turns off the redundant LAE Injector Heaters for all four engines.

Main Steps in SCS:

Commands for Injector Heater #1 disable

Commands for Injector Heater #2 disable

Commands for Injector Heater #3 disable

Commands for Injector Heater #4 disable

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The LAE Injector heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Commands are doubled-up to protect against SEU upset.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

CAUTION: only one set of injector heaters, prime or redundant, is to be powered at any time.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PL1IHROF | LAE 1 INJ HTR OFF RDNT |  | PL1IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PL1IHROF | LAE 1 INJ HTR OFF RDNT |  | PL1IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PL2IHROF | LAE 2 INJ HTR OFF RDNT |  | PL2IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PL2IHROF | LAE 2 INJ HTR OFF RDNT |  | PL2IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | PL3IHROF | LAE 3 INJ HTR OFF RDNT |  | PL3IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | PL3IHROF | LAE 3 INJ HTR OFF RDNT |  | PL3IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | PL4IHROF | LAE 4 INJ HTR OFF RDNT |  | PL4IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | PL4IHROF | LAE 4 INJ HTR OFF RDNT |  | PL4IHRD | OFF |  |  |  |  | EP | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 55 – MCE-B LETG Insert Nudge

Description:

This SCS contains the MCE-B LETG Enable Execute relay command and Disable Execute relay command separated by a time delay.  Inserting or retracting the gratings uses a combination of one large move and several small moves.  Large moves get the grating close to the bumper, and small nudge moves incrementally close in on the end-of-travel position.  Limit switch status is checked after each nudge move to detect the grating reaching the end of travel.  Small moves are implemented by the Flight Software activating this SCS.  SMALL_MOVE_SEQ is used by OTG_SUPPORT_PROC to perform the OTG small moves.  This procedure checks whether the end-of-travel limit switch corresponding 27 March, 2001 77 OTG Flight Software Patch Design Document to the move in progress is actuated. If not, an SCS is activated to briefly enable the execute relay. Time between LS checks/SCS activations can be expanded in 8 m.c. increments by storing a value in Small_Move_Delay. The maximum number of small moves allowed during an OTG move operation is limited by KT.Max_Small_Moves.

Main Steps in SCS:

MCE-B Enable LETG Insertion/Retraction

2 minor cycle time delay

MCE-B Disable LETG Insertion/Retraction

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated by the Flight Software during software controlled LETG Insertions.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4EXLGBEN | MCE B: EXEC LETG INSERTION/RETRACTION--Command to Initiate OTG Transistion |  | 4LEXRBX | ENAB |  |  |  |  | TS | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4EXLGBDS | MCE B:DISA LETG INSERTION/RETRACTION |  | 4LEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 56 – MCE-B HETG Insert Nudge

Description:

This SCS contains the MCE-B HETG Enable Execute relay command and Disable Execute relay command separated by a time delay.  Inserting or retracting the gratings uses a combination of one large move and several small moves.  Large moves get the grating close to the bumper, and small nudge moves incrementally close in on the end-of-travel position.  Limit switch status is checked after each nudge move to detect the grating reaching the end of travel.  Small moves are implemented by the Flight Software activating this SCS.  SMALL_MOVE_SEQ is used by OTG_SUPPORT_PROC to perform the OTG small moves.  This procedure checks whether the end-of-travel limit switch corresponding 27 March, 2001 77 OTG Flight Software Patch Design Document to the move in progress is actuated. If not, an SCS is activated to briefly enable the execute relay. Time between LS checks/SCS activations can be expanded in 8 m.c. increments by storing a value in Small_Move_Delay. The maximum number of small moves allowed during an OTG move operation is limited by KT.Max_Small_Moves.

Main Steps in SCS:

MCE-B Enable HETG Insertion/Retraction

1 minor cycle time delay

MCE-B Disable HETG Insertion/Retraction

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated by the Flight Software during software controlled HETG Insertions.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4EXHGBEN | MCE B: EXEC HETG INSERTION/RETRACTION--COMMAND TO INITIATE OTG TRANSISTION |  | 4HEXRBX | ENAB |  |  |  |  | TS | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4EXHGBDS | MCE B: DISA HETG INSERTION/RETRACTION |  | 4HEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 57 -- MCE-B LETG Retract Nudge

Description:

This SCS contains the MCE-B LETG Enable Execute relay command and Disable Execute relay command separated by a time delay.  Inserting or retracting the gratings uses a combination of one large move and several small moves.  Large moves get the grating close to the bumper, and small nudge moves incrementally close in on the end-of-travel position.  Limit switch status is checked after each nudge move to detect the grating reaching the end of travel.  Small moves are implemented by the Flight Software activating this SCS.  SMALL_MOVE_SEQ is used by OTG_SUPPORT_PROC to perform the OTG small moves.  This procedure checks whether the end-of-travel limit switch corresponding 27 March, 2001 77 OTG Flight Software Patch Design Document to the move in progress is actuated. If not, an SCS is activated to briefly enable the execute relay. Time between LS checks/SCS activations can be expanded in 8 m.c. increments by storing a value in Small_Move_Delay. The maximum number of small moves allowed during an OTG move operation is limited by KT.Max_Small_Moves.

Main Steps in SCS:

MCE-B Enable LETG Insertion/Retraction

2 minor cycle time delay

MCE-B Disable LETG Insertion/Retraction

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated by the Flight Software during software controlled LETG Retractions.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4EXLGBEN | MCE B: EXEC LETG INSERTION/RETRACTION--Command to Initiate OTG Transistion |  | 4LEXRBX | ENAB |  |  |  |  | TS | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4EXLGBDS | MCE B:DISA LETG INSERTION/RETRACTION |  | 4LEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 58 --  MCE-B HETG Retract Nudge

Description:

This SCS contains the MCE-B HETG Enable Execute relay command and Disable Execute relay command separated by a time delay.  Inserting or retracting the gratings uses a combination of one large move and several small moves.  Large moves get the grating close to the bumper, and small nudge moves incrementally close in on the end-of-travel position.  Limit switch status is checked after each nudge move to detect the grating reaching the end of travel.  Small moves are implemented by the Flight Software activating this SCS.  SMALL_MOVE_SEQ is used by OTG_SUPPORT_PROC to perform the OTG small moves.  This procedure checks whether the end-of-travel limit switch corresponding 27 March, 2001 77 OTG Flight Software Patch Design Document to the move in progress is actuated. If not, an SCS is activated to briefly enable the execute relay. Time between LS checks/SCS activations can be expanded in 8 m.c. increments by storing a value in Small_Move_Delay. The maximum number of small moves allowed during an OTG move operation is limited by KT.Max_Small_Moves.

Main Steps in SCS:

MCE-B Enable HETG Insertion/Retraction

1 minor cycle time delay

MCE-B Disable HETG Insertion/Retraction What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated by the Flight Software during software controlled HETG Retractions.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4EXHGBEN | MCE B: EXEC HETG INSERTION/RETRACTION--COMMAND TO INITIATE OTG TRANSISTION |  | 4HEXRBX | ENAB |  |  |  |  | TS | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4EXHGBDS | MCE B: DISA HETG INSERTION/RETRACTION |  | 4HEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 59 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 60 -- PC RCTU Monitor Fault

Description:

This SCS is activated when the PC RCTU Monitor trips.  This monitor protects against a failed PC RCTU, or if the RCTU has been shut down by an SEU.

Main Steps in SCS:

- (See attached flow chart)  Check to see which RCTU is on.  If Prime is on, cycle Prime RCTU converter power, else cycle the redundant power

- Reinitialize the following PCAD subfunctions:

Reaction Wheel Monitors

SADA position Monitor

Dome Temperature Monitor

- Disable LAE Directives in case an SEU shut down the PC RCTU while the LAEs were firing.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during all Mission Phases.

Constraints:

If this SCS is edited, be sure that the RCTU is brought back on line within one second of the failure.  Many other protected SCSs are designed with this one second value in mind.  Commands that go through this RCTU are doubled up with one second delays between them in the event that the RCTU is shut down by an SEU.

When the PC RCTU Monitor trips, the PC Cmd Wrap error (0e1e) will be observed in the OBC Error Log, and OBC Health and Status will activate SCS 60.

This SCS defaults to disabled upon OBC reset, and is automatically enabled by SCS #: 80 -- OO - Standby State Timeout.

Figure SCS 60-1 PC RCTU Wrap Test

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | CPCPOF | RCTU-PC PRI CONV PWR OFF |  | CTUPCA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | CPCPOF | RCTU-PC PRI CONV PWR OFF |  | CTUPCA | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | CPCPON | RCTU-PC PRI CONV PWR ON |  | CTUPCA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | CPCPON | RCTU-PC PRI CONV PWR ON |  | CTUPCA | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 9 | 9 | COSBRCH | SCS SET STEP# (I.E.UNCONDITIONAL BRANCH) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSBRCH1 | COSBRCH - SCS STEP -- SCS Step Number | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | CPCROF | RCTU-PC RED CONV PWR OFF |  | CTUPCB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | CPCROF | RCTU-PC RED CONV PWR OFF |  | CTUPCB | OFF |  |  |  |  | LR | HLP |  |  |  |  |
| 13 | 13 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | CPCRON | RCTU-PC RED CONV PWR ON |  | CTUPCB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 15 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | CPCRON | RCTU-PC RED CONV PWR ON |  | CTUPCB | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 17 | 17 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | AOPCADSE | PCAD Subfunction for EN | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | AOPCADSE | PCAD Subfunction for EN | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | AOPCADSE | PCAD Subfunction for EN | 37 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | AODRLAED | OBC DIRECTIVES LAE DISABLE |  | AOLAEDEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 61 -- ESA and ESA Heater Prime Enable

Description:

This SCS turns ON the prime ESA and prime ESA heaters

Main Steps in SCS:

Turn on the Prime Earth Sensor

Turn on the Prime Earth Sensor Heaters.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn on the ESA and ESA heater circuits. The ESA and ESA heaters are no longer used during the mission following SSD opening and successful operation of the Aspect Determination System. However, these can be used for “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Do not use this SCS prior SSD opening to prevent interruption of PCAD operations.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 1 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AESAAON | ESA-A PWR ON |  | AESAA | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AESAAON | ESA-A PWR ON |  | AESAA | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | EESP1HON | HTR BUS 9: ESA/ESE PRI ENAB (CH0) |  | TESAPHT1 | ENAB | TESAPHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | EESP1HON | HTR BUS 9: ESA/ESE PRI ENAB (CH0) |  | TESAPHT1 | ENAB | TESAPHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | EESP2HON | HTR BUS 9: ESA/ESE PRI ENAB (CH1) |  | TESAPHT1 | ENAB | TESAPHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | EESP2HON | HTR BUS 9: ESA/ESE PRI ENAB (CH1) |  | TESAPHT1 | ENAB | TESAPHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 62 -- ESA and ESA Heater Redundant Enable

Description:

This SCS turns ON the redundant ESA and redundant  ESA heaters

Main Steps in SCS:

Turn on the redundant Earth Sensor

Turn on the redundant Earth Sensor Heaters.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn on the ESA and ESA heater circuits. The ESA and ESA heaters are no longer used during the mission following SSD opening and successful operation of the Aspect Determination System. However, these can be used for “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Do not use this SCS prior SSD opening to prevent interruption of PCAD operations.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 1 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AESABON | ESA-B PWR ON |  | AESAB | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AESABON | ESA-B PWR ON |  | AESAB | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | EESR1HON | HTR BUS 18: ESA/ESE RDNT ENAB (CH0) |  | TESARHT1 | ENAB | TESARHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | EESR1HON | HTR BUS 18: ESA/ESE RDNT ENAB (CH0) |  | TESARHT1 | ENAB | TESARHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | EESR2HON | HTR BUS 18: ESA/ESE RDNT ENAB (CH1) |  | TESARHT1 | ENAB | TESARHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | EESR2HON | HTR BUS 18: ESA/ESE RDNT ENAB (CH1) |  | TESARHT1 | ENAB | TESARHT2 | ENAB |  |  | EP | SD | 2 | 5 | 32 | K12B |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 63 -- Transmitter and Power Amp Prime Enable

Description:

This SCS turns ON the prime transmitter and power amp

Main Steps in SCS:

Commands to turn on the prime Power Amplifier

Commands to turn on the prime Transmitter

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn on transmitter and power amp loads. This command sequence does not include any link configuration commands.

Constraints:

Do not include this SCS in SCS 32 or SCS 33 if ground contact is anticipated during the eclipse. The daily load is used to manipulate the transmitter commands.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

Power Amp must be turned on prior to Transmitter, so keep doubled-up Power Amp enable commands ahead of Transmitter enable commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CPAAON | PA-A ON |  | CPA1 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CPAAON | PA-A ON |  | CPA1 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CTXAON | TX-A ON |  | CTXAX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CTXAON | TX-A ON |  | CTXAX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 64 -- Transmitter and Power Amp Redundant Enable

Description:

This SCS turns ON the redundant transmitter and power amp

Main Steps in SCS:

Commands to turn on the redundant Power Amplifier

Commands to turn on the redundant Transmitter

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to turn on transmitter and power amp loads. This command sequence does not include any link configuration commands.

Constraints:

Do not include this SCS in SCS 32 or SCS 33 if ground contact is anticipated during the eclipse. The daily load is used to manipulate the transmitter commands.

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

Power Amp must be turned on prior to Transmitter, so keep doubled-up Power Amp enable commands ahead of Transmitter enable commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | CPABON | PA-B ON |  | CPA2 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CPABON | PA-B ON |  | CPA2 | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | CTXBON | TX-B ON |  | CTXBX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CTXBON | TX-B ON |  | CTXBX | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 65 -- Fuel Tank Heater Prime and Redundant Enable

Description:

This SCS turns on the prime and redundant Fuel Tank Heaters

Main Steps in SCS:

Commands to enable prime Tank Heater

Commands to enable redundant Tank Heater

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to restore Fuel Tank Heater loads following exit from long earth eclipses.

Constraints:

Commands are doubled-up to prevent against SEU.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PFTPHEN | FUEL TANK HTR PRI ENAB |  | EFTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PFTPHEN | FUEL TANK HTR PRI ENAB |  | EFTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PFTRHEN | FUEL TANK HTR RDNT ENAB |  | EFTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PFTRHEN | FUEL TANK HTR RDNT ENAB |  | EFTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 66 -- FLCA Prime Enable

Description:

This SCS turns on the Prime Fiducial Light Controller Assembly.

Main Steps in SCS:

Turn on the FID Light Controller Assembly

FID light control command to turn off all FID lights.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to restore FLCA loads following exit from a long earth eclipse passage.

Constraints:

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AFLCAAON | FLCA - A ON |  | AFLCAAX | ON |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AFLCAAON | FLCA - A ON |  | AFLCAAX | ON |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 5 | 5 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 7 | 7 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 67 -- FLCA Redundant Enable

Description:

This SCS turns on the Redundant Fiducial Light Controller Assembly.

Main Steps in SCS:

Turn on the FID Light Controller Assembly

FID light control command to turn off all FID lights.

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to restore FLCA loads following exit from a long earth eclipse passage.

Constraints:

Commands are doubled-up to protect against SEU upset.

16 minor cycles between doubled commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AFLCABON | FLCA - B ON |  | AFLCABX | ON |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AFLCABON | FLCA - B ON |  | AFLCABX | ON |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 5 | 5 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | AFIDP | FID LIGHT CONTROL PRIME (FLCA-A)--CONTAINS AN FLCA COMMAND WORD WITH: RESET, DMUX ADDRESS, DMUX CHANNEL, CURRENT LEVEL There is only one command which operates both sides, set the side you want to operate on/off with AFLCAA/BON/OF |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 7 | 7 | AFIDP01 | AFIDP01 Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP02 | Reset -- Zero's all current levels when reset and disables Dmux addressing. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP03 | Driver Dmux Address -- Chooses the dmux being commanded. DMux driver 1 - 00 DMux driver 2 - 01 DMux driver 3 - 10 DMux driver 4 - 11 | 00 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP04 | Dmux channel Enable -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP05 | Dmux Channel Select -- 0 - Channel 1, 1 - Channel 2, 2 - Channel 3, 3 - Channel 4, 4 - Channel 5, 5 - Channel 6, 6 - Channel 7, 7 - Channel 8 | 000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AFIDP06 | Current Level Command -- 0,1 - Off, residual current only 2..255 I(FLA)=((0.1432milliamp)/Count)*Current level Command - 0.221 milliamps | 00000000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 68 -- Telescope OBA Heater Zone Enable

Description:

This SCS turns on the OBA heater zones control.

Main Steps in SCS:

Command Re-initialize Telescope thermal control. This command resets any error flags, and resets the health and safety timers to start counting down. This command does NOT select the IP or database to use.

Command Enable OBA Thermal Control

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This command sequence is used to restore OBA heater zone control after exit from a long eclipse. This command sequence does not contain any hardware commands. The commands are only to the software process, therefore they do not need to be doubled–up. This also means the commands are also hardware independent.

The health and safety counters by default are set to 15 hours for the OBA and 90 hours for the HRMA. These allow time for the thermal control system to stabilize before reporting thermal faults.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | 4OOBTCEN | ENABLE OBA THERMAL CONTROL |  | 4OACOBAH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 69 -- HRC Turn On (into Standby)

Description:

This SCS performs a controlled turn on the HRC instrument into a standby mode.

Main Steps in SCS:

- Turn on +5v power supply A.

- Turn off Spectroscopy Detector HV power supply.

- Set HRC-S Top Plate to zero volts

- Set HRC-S Bottom Plate to zero volts

- Enable HRC-S HV Current Limit

- Turn off Antico Shield A HV power supply

- Set Antico Shield A HV to zero volts

- Turn off Imaging Detector HV power supply

- Set HRC-I Top Plate to zero volts

- Set HRC-I Bottom Plate to zero volts

- Enable HRC-I HV Current Limit

- Turn off Antico Shield B HV power supply

- Set Antico Shield B HV to zero volts

- Disable Motor Drive

- Reset Motion Control

- De-select all motors

- Turn on +15V power supply

- Turn on +24V power supply

- Antico Shield PMT 1 select preamp A

- Antico Shield PMT 2 select preamp B

- Select Next In Line Mode

- Reset DATA FIFO

- End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used for powering up the HRC following a long earth eclipse or an unplanned event during a long eclipse season. SCS 33, configured for long eclipse season, would contain the call to this SCS.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

A one-second delay is required between HRC commands.

Commands are doubled to protect against SEU upset. Commands are doubled individually to maintain correct command order.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 205VAON | +5V LV PWR SUPPLY A ON |  | 2PS5AON | ON | 2P05VAVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 205VAON | +5V LV PWR SUPPLY A ON |  | 2PS5AON | ON | 2P05VAVL | NONE | 2C05PALV |  | SI | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 2SPHVOF | SPECT DET HV OFF--TURNS OFF SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2SPONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2SPHVOF | SPECT DET HV OFF--TURNS OFF SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2SPONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 13 | 13 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 15 | 15 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 25 | 25 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 27 | 27 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 2IMHVOF | IMAGING DET HV OFF--TURNS OFF IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2IMONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 31 | 2IMHVOF | IMAGING DET HV OFF--TURNS OFF IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2IMONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 33 | 33 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 33 | 33 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 35 | 35 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 37 | 37 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 39 | 39 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | 43 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 46 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | 47 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 48 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 49 | 49 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 49 | 49 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 50 | 50 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 50 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | 51 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 51 | 51 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | 51 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 52 | 52 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 52 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | 2MDRVADI | MOTOR DRIVE DISABLE-- APPLIES POWER TO SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2MDRVAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 54 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | 2MDRVADI | MOTOR DRIVE DISABLE-- APPLIES POWER TO SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2MDRVAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 56 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 57 | 57 | 2MCMRASL | MOTION CONTROL MODE RESET--PREVENTS MOTION CONTROL MODES 2MVPSAEX, 2MVLAAEX, 2MVLBAEX, 2NSTAAEX, AND 2NSTBAEX FROM BEING EXECUTED. BITS 19-26 ARE THE COMMAND NUMBER (6F HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MCMDARS | RSET |  |  |  |  | SI | SD |  |  |  |  |
| 58 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 2MCMRASL | MOTION CONTROL MODE RESET--PREVENTS MOTION CONTROL MODES 2MVPSAEX, 2MVLAAEX, 2MVLBAEX, 2NSTAAEX, AND 2NSTBAEX FROM BEING EXECUTED. BITS 19-26 ARE THE COMMAND NUMBER (6F HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MCMDARS | RSET |  |  |  |  | SI | SD |  |  |  |  |
| 60 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 61 | 2ALMTADS | ALL MOTORS DESELECT--DESELECTS ALL MOTORS. BITS 19-26 ARE THE COMMAND NUMBER (70 HEX), BITS 27-34 ARE DONT CARE. |  | 2ALMTAST | NSEL |  |  |  |  | SI | SD |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 63 | 2ALMTADS | ALL MOTORS DESELECT--DESELECTS ALL MOTORS. BITS 19-26 ARE THE COMMAND NUMBER (70 HEX), BITS 27-34 ARE DONT CARE. |  | 2ALMTAST | NSEL |  |  |  |  | SI | SD |  |  |  |  |
| 64 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 65 | 215PCAON | +15V LV PWR SUPPLY ON--TURNS ON +15V LVPS. BITS 19-26 ARE THE COMMAND NUMBER (10 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 215PCAST | ON | 2P15VAVL | NONE | 2C15PALV |  | SI | SD |  |  |  |  |
| 66 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 67 | 67 | 215PCAON | +15V LV PWR SUPPLY ON--TURNS ON +15V LVPS. BITS 19-26 ARE THE COMMAND NUMBER (10 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 215PCAST | ON | 2P15VAVL | NONE | 2C15PALV |  | SI | SD |  |  |  |  |
| 68 | 68 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 68 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 69 | 224PCAON | +24V LV PWR SUPPLY ON--TURNS ON +24V LVPS. BITS 19-26 ARE THE COMMAND NUMBER (12 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 224PCAST | ON | 2P24VAVL | NONE | 2C24PALV |  | SI | SD |  |  |  |  |
| 70 | 70 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 70 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 71 | 71 | 224PCAON | +24V LV PWR SUPPLY ON--TURNS ON +24V LVPS. BITS 19-26 ARE THE COMMAND NUMBER (12 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 224PCAST | ON | 2P24VAVL | NONE | 2C24PALV |  | SI | SD |  |  |  |  |
| 72 | 72 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 72 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1405 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 73 | 73 | 2PRA1SL | SHIELD PMT 1 SEL, PREAMP A |  | 2ELEASS | PMT1 |  |  |  |  | SI | HLP |  |  |  |  |
| 74 | 74 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 74 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 75 | 75 | 2PRA1SL | SHIELD PMT 1 SEL, PREAMP A |  | 2ELEASS | PMT1 |  |  |  |  | SI | HLP |  |  |  |  |
| 76 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 77 | 77 | 2PRB2SL | SHIELD PMT 2 SEL, PREAMP B |  | 2ELEBSS | PMT2 |  |  |  |  | SI | HLP |  |  |  |  |
| 78 | 78 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 78 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 79 | 79 | 2PRB2SL | SHIELD PMT 2 SEL, PREAMP B |  | 2ELEBSS | PMT2 |  |  |  |  | SI | HLP |  |  |  |  |
| 80 | 80 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 80 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 81 | 2NXILASL | NEXT-IN-LINE MODE SELECT-- SETS THE TELEMETRY OUTPUT FOR OBSERVING AS THE NEXT IN LINE SCIENCE INSTRUMENT. BITS 19-26 ARE THE COMMAND NUMBER (1A HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2OBNLASL | NEXT |  |  |  |  | SI | SD |  |  |  |  |
| 82 | 82 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 82 | 82 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 83 | 83 | 2NXILASL | NEXT-IN-LINE MODE SELECT-- SETS THE TELEMETRY OUTPUT FOR OBSERVING AS THE NEXT IN LINE SCIENCE INSTRUMENT. BITS 19-26 ARE THE COMMAND NUMBER (1A HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2OBNLASL | NEXT |  |  |  |  | SI | SD |  |  |  |  |
| 84 | 84 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 84 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 85 | 85 | 2FIFOAOF | DATA FIFO RESET-- HOLDS PRIMARY DATA FIFO IN RESET MODE. BITS 19-26 ARE THE COMMAND NUMBER (45 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2FIFOAVR | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 86 | 86 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 86 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 87 | 87 | 2FIFOAOF | DATA FIFO RESET-- HOLDS PRIMARY DATA FIFO IN RESET MODE. BITS 19-26 ARE THE COMMAND NUMBER (45 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2FIFOAVR | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 88 | 88 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 88 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 89 | 89 | 2FIFOAON | DATA FIFO ENABLE-- RELEASES DATA FIFO TO OPERATIONAL MODE. BITS 19-26 ARE THE COMMAND NUMBER (45 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2FIFOAVR | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 90 | 90 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 90 | 90 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 91 | 91 | 2FIFOAON | DATA FIFO ENABLE-- RELEASES DATA FIFO TO OPERATIONAL MODE. BITS 19-26 ARE THE COMMAND NUMBER (45 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2FIFOAVR | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 92 | 92 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 70 -- ACIS Turn-on into Standby

Description:

This SCS performs a controlled turn on the ACIS instrument into a standby mode.

Main Steps in SCS:

- Enable B-side Detector Housing heater

- Turn On B-side Detector Housing Heater

- Enable A-side DPA Power Supply

- Turn On A-side DPA

- Enable B-side DPA Power Supply

- Turn On B-side DPA

- Enable A-side DEA Power Supply

- Turn on A-side DEA Power Supply

- Start DEA Housekeeping run, ACIS Parameter block: startDEA: XDZ0000001

- Set DPA Warm Boot flag

- Command DPA reset (parameter = 1), Halt BEP

- Command DPA reset (parameter = 0), Restart BEP

- Start DEA Housekeeping run, ACIS parameter block: startDEA: XDZ0000001

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in phases where long eclipses are anticipated and ACIS shutdown is required to reduce loads. SCS 32, loadshed SCS, is edited to include a call to this SCS.

The default on-board SCS for both the launch load and the on-orbit load turns off all ACIS processors. If load power is not a constraint for long eclipses, then SCS 40 can be edited and patched to leave the DPA on, thereby keeping the flight software and all patches intact. This SCS may in turn have to be modified to not send the DPA power command, since it will already be on.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Commands are NOT doubled per request by CXC.

At least one second between ACIS hardware commands. Note longer delay commands between command packet commands

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 1HHTRBEN | HOUSING HTR ENABLE B--ENABLES THE B SIDE HOUSING HEATER |  | 1DAHTBEN | ENAB |  |  |  |  | SI | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 1HHTRBON | HOUSING HTR ON B--TURNS THE B SIDE HOUSING HEATER ON |  | 1DAHTBON | ON |  |  |  |  | SI | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 1DPPSAEN | DPA PWR SUPPLY ENABLE A--ENABLES THE A SIDE DPA POWER SUPPLY |  | 1DPPSAX | ENAB |  |  |  |  | SI | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 1DPPSAON | DPA PWR SUPPLY ON A--TURNS THE A SIDE POWER SUPPLY TO THE DPA ON |  | 1DPPSA | ON | 1DPDBAON | ON |  |  | SI | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 1DPPSBEN | DPA PWR SUPPLY ENABLE B--ENABLES THE B SIDE DPA POWER SUPPLY |  | 1DPPSBX | ENAB |  |  |  |  | SI | HLP |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 1DPPSBON | DPA PWR SUPPLY ON B--TURNS THE B SIDE POWER SUPPLY TO THE DPA ON |  | 1DPPSB | ON | 1DPDBBON | ON |  |  | SI | HLP |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 1DEPSAEN | DEA PWR SUPPLY ENABLE A--ENABLES THE A SIDE DEA POWER SUPPLY |  | 1DEPSAX | ENAB |  |  |  |  | SI | HLP |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 1DEPSAON | DEA PWR SUPPLY ON A--TURNS THE A SIDE POWER SUPPLY TO THE DEA ON |  | 1DEPSA | ON | 1DEDBAON | ON |  |  | SI | HLP |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17-20 | 17 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17-20 | 17 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-20 | 17 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-20 | 17 | COACISL4[01] | ACIS DATA -- | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-20 | 17 | COACISL4[02] | ACIS DATA -- | 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-20 | 17 | COACISL4[03] | ACIS DATA -- | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-20 | 17 | COACISL4[04] | ACIS DATA -- | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1920 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 19 | 1WRMBTSB | DPA Warm Boot--Sets BEP Status Register bit WARM_BOOT to value = D(0). This bit defaults to 0 upon power up). D(o)=1 indicates that the S/C requires taht the DPA enter a low current mode. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 22 | 19 | 1WRMBTS1 | BEP STATUS REGISTER BIT WARM_BOOT -- SETS BEP STATUS REGISTER BIT WARM_BOOT TO VALUE=D(0). THIS BIT DEFAULTS TO 0 UPON POWER-UP. D(0)=1 INDICATES THAT THE S/C REQUIRES THAT THE DPA ENTER A LOW-CURRENT MODE. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 21 | 1RSETIRT | DPA CMD RESET |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 24 | 21 | 1RSETIRT_FLD1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 21 | 1RSETIR1 | RESET -- ASSERTS RESET. D(0)=1 HOLDS THE BOARD IN A RESET STATE (EXCEPT FOR THE HW COMMAND DECODER). D(0)=0 DEASSERTS. THIS BIT DEFAULTS TO 0 UPON POWER-UP. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 23 | 1RSETIRT | DPA CMD RESET |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 26 | 23 | 1RSETIRT_FLD1 | FILLER -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 23 | 1RSETIR1 | RESET -- ASSERTS RESET. D(0)=1 HOLDS THE BOARD IN A RESET STATE (EXCEPT FOR THE HW COMMAND DECODER). D(0)=0 DEASSERTS. THIS BIT DEFAULTS TO 0 UPON POWER-UP. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 64 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISLD | ACIS LOAD |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL1 | COACISLD - HEADER -- |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL2 | Number of 16 bit ACIS data -- Number of Serial Digital Commands | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL4[01] | ACIS DATA -- | 4 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL4[02] | ACIS DATA -- | 10 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL4[03] | ACIS DATA -- | 18 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28-31 | 25 | COACISL4[04] | ACIS DATA -- | 0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 26 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 71 -- RCS Catbed Heaters Prime Enable

Description:

This SCS turns On the Prime RCS Catbed Heaters.

Main Steps in SCS:

Commands to Turn on Prime Catbed Heaters

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The RCS Catbed heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Command is doubled-up to protect against SEU upset.

16 minor cycles between doubled commands.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PCBPHON | RCS CATBED HTR PRI ON |  | PRCSCHPR | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PCBPHON | RCS CATBED HTR PRI ON |  | PRCSCHPR | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 72 -- RCS Catbed Heaters Redundant Enable

Description:

This SCS turns On the Redundant RCS Catbed Heaters.

Main Steps in SCS:

Commands to Turn on Redundant Catbed Heaters

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The RCS Catbed heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Command is doubled-up to protect against SEU upset.

16 minor cycles between doubled commands.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PCBRHON | RCS CATBED HTR RDNT ON |  | PRCSCHRD | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PCBRHON | RCS CATBED HTR RDNT ON |  | PRCSCHRD | ON |  |  |  |  | LR | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 73 -- LAE Injector Heaters Prime Enable (all 4 engines)

Description:

This SCS turns On the prime LAE Injector Heaters for all four engines.

Main Steps in SCS:

Commands for Injector Heater #1 enable

Commands for Injector Heater #2 enable

Commands for Injector Heater #3 enable

Commands for Injector Heater #4 enable

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The LAE Injector heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Commands are doubled-up to protect against SEU upset.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

CAUTION: only one set of injector heaters, prime or redundant, is to be powered at any time.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PL1IHPON | LAE 1 INJ HTR ON PRI |  | PL1IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PL1IHPON | LAE 1 INJ HTR ON PRI |  | PL1IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PL2IHPON | LAE 2 INJ HTR ON PRI |  | PL2IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PL2IHPON | LAE 2 INJ HTR ON PRI |  | PL2IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | PL3IHPON | LAE 3 INJ HTR ON PRI |  | PL3IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | PL3IHPON | LAE 3 INJ HTR ON PRI |  | PL3IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | PL4IHPON | LAE 4 INJ HTR ON PRI |  | PL4IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | PL4IHPON | LAE 4 INJ HTR ON PRI |  | PL4IHPR | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 74 -- LAE Injector Heaters Redundant Enable (all 4 engines)

Description:

This SCS turns On the redundant LAE Injector Heaters for all four engines.

Main Steps in SCS:

Commands for Injector Heater #1 enable

Commands for Injector Heater #2 enable

Commands for Injector Heater #3 enable

Commands for Injector Heater #4 enable

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The LAE Injector heaters are used during transfer orbit operations. Following IPS deactivation, these heaters can be used as “power ballast” in short earth eclipse conditions where additional loads are required.

Constraints:

Commands are doubled-up to protect against SEU upset.

Do not use this SCS during transfer orbit to prevent interruption of propulsion operations.

16 minor cycles between doubled commands, at least 2 minor cycles between adjacent non-like commands.

CAUTION: only one set of injector heaters, prime or redundant, is to be powered at any time.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | PL1IHRON | LAE 1 INJ HTR ON RDNT |  | PL1IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | PL1IHRON | LAE 1 INJ HTR ON RDNT |  | PL1IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | PL2IHRON | LAE 2 INJ HTR ON RDNT |  | PL2IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | PL2IHRON | LAE 2 INJ HTR ON RDNT |  | PL2IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | PL3IHRON | LAE 3 INJ HTR ON RDNT |  | PL3IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | PL3IHRON | LAE 3 INJ HTR ON RDNT |  | PL3IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | PL4IHRON | LAE 4 INJ HTR ON RDNT |  | PL4IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | PL4IHRON | LAE 4 INJ HTR ON RDNT |  | PL4IHRD | ON |  |  |  |  | EP | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 75 -- Trim Heater Prime Enable

Description:

This SCS turns ON the prime trim heaters and the three flexure heaters.

Main Steps in SCS:

The following heaters are turned ON:

| 3AC1PTEN | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |
| --- | --- |
| 3AC2PTEN | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |
| 3AC3PTEN | ACIS 3 FITTING +Z PRIME TRIM HEATER ENABLE |
| 3HR1PTEN | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |
| 3HR2PTEN | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |
| 3HR3PTEN | HRC 3 FITTING +Z PRIME TRIM HEATER ENABLE |
| 3PSMPTEN | PSMC PRIME TRIM HEATER ENABLE |
| 3FLCPTEN | FLCA PRIME TRIM HEATER ENABLE |
| 3RCTPTEN | RCTU PRIME TRIM HEATER ENABLE |
| 3SPYPTEN | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER ENABLE |
| 3SMYPTEN | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER ENABLE |
| 3SMZPTEN | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HEATER ENABLE |
| 3FA6PAEN | FOCUS ASSEMBLY 6 PRIME ABORT HEATER ENABLE |

The ISIM Flexure heaters are turned ON (heaters A, B and C)

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS re-enables all the prime trim heaters that would be disabled for a long eclipse passage. Along with the latching relay commands are the serial digital commands to enable the three flexure heater zones.

Constraints:

The heater commands are doubled-up as a group to protect against SEU upset. One minor cycle between adjacent commands, and 16 mc between the groups.

The SIM Flexure Heaters are doubled up, however the time delay between these commands should have been set to a minimum of 65 seconds (2 major frames). There is a possibility that one or both SIM flexure commands could be rejected by the SIM SEA. Based on a pre-launch CCB meeting, the decision was made not to correct this SCS (and SCS 42, the OFF version), and instead add commands to the Long Eclipse Procedure products. The Long Eclipse Procedure, where this SCS would be used, specifically contains instructions to command the flexure heaters OFF and ON independent of SCS 75 (ON) and SCS #: 42 -- Trim Heater Prime Disable (OFF). This increases the chance that the commands will get through to the SIM SEA.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3AC1PTEN | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3A1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 3AC2PTEN | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3A2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 3AC3PTEN | ACIS 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3A3THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 3HR1PTEN | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3H1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 3HR2PTEN | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3H2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 3HR3PTEN | HRC 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3H3PZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 3PSMPTEN | PSMC PRIME TRIM HEATER ENABLE |  | 3APSMTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 3FLCPTEN | FLCA PRIME TRIM HEATER ENABLE |  | 3FLCTHTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 3RCTPTEN | RCTU PRIME TRIM HEATER ENABLE |  | 3SITHTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | 3SPYPTEN | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER ENABLE |  | 3ASPYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 3SMYPTEN | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER ENABLE |  | 3ASMYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | 3SMZPTEN | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HEATER ENABLE |  | 3ASMZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 3FA6PAEN | FOCUS ASSEMBLY 6 PRIME ABORT HEATER ENABLE |  | 3AZF6HTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 27 | 27 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 213 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 28 | 28 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 01 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 28 | 28 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 29 | 29 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 29 | 29 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 10 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 29 | 29 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 30 | 30 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 30 | 30 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 11 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 30 | 30 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | 3AC1PTEN | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3A1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | 3AC2PTEN | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3A2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | 3AC3PTEN | ACIS 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3A3THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 37 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | 3HR1PTEN | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3H1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 39 | 39 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | 3HR2PTEN | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3H2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 41 | 41 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | 3HR3PTEN | HRC 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3H3PZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 43 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | 3PSMPTEN | PSMC PRIME TRIM HEATER ENABLE |  | 3APSMTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 45 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | 3FLCPTEN | FLCA PRIME TRIM HEATER ENABLE |  | 3FLCTHTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 47 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | 3RCTPTEN | RCTU PRIME TRIM HEATER ENABLE |  | 3SITHTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 49 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 50 | 3SPYPTEN | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER ENABLE |  | 3ASPYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 51 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 52 | 3SMYPTEN | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER ENABLE |  | 3ASMYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 53 | 53 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | 3SMZPTEN | ACIS SUPPORT STRUCTURE - Z PRIME TRIM HEATER ENABLE |  | 3ASMZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 55 | 55 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 55 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | 3FA6PAEN | FOCUS ASSEMBLY 6 PRIME ABORT HEATER ENABLE |  | 3AZF6HTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 57 | 57 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 58 | 58 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 213 |  |  |  |  |  |  |  |  |  |  |  |  |
| 58 | 58 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 58 | 58 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 59 | 59 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 01 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 59 | 59 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 60 | 60 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 60 | 60 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 10 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 60 | 60 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 61 | 61 | 3SEASETH | SIM SEA SET FA HTR ZONE TEMP--The Heater Control command controls the heater power latching relay and the temperature for each FA mounting flexure. Three zones or flexures may be specified and controlled with this command. A set point temperature range of -64 to +63 degrees Celsius may be specified. When the binary value (00) is specified in the Zone field of the command, the SEA will ignore the Temperature field in the command and set the heater power latching relay to its OFF state, which switches off power to heaters on all three flexures. When any oter zone is specifed in the command the SEA will set the heater power relay to its ON state, if it is not already in that state. The SEA software will accept multiple heater control commands within one SEA command group or packet, but it may assume that no more than one command within a single group will cause a change in state of the heater power latching relay. After execution of a command that changes the state of the heater power relay, any subsequent command within the same group that also changes the heater power relay state will be ignored by the SEA software. |  | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 61 | 61 | 3SEASTH1 | SIM Heater Control Zone -- This field is used to specify the zone or FA mounting flexure which is to be controlled. Binary (01) specifies zone 1 or flexure A, binary (10) specifies zone 2 or flexure B, binary (11) specifies zone 3 or flexure C. Binary (00) set the heater power latching relay to its OFF state which switches off power to heaters in all three zones or flexures. | 11 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 61 | 61 | 3SEASTH2 | SIM Heater Control Set Temperature -- This field is a 10 bit signed integer used to specify the temperature set point in degrees C within the specified zone. The allowable range is -64 to +63 degrees C. | 0001010000 | 3SFLXAST | NONE | 3SFLXBST | NONE | 3SFLXCST | NONE | SI | SD |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 63 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 76 -- Trim Heater Redundant Enable

Description:

This SCS turns ON the redundant trim heaters.

Main Steps in SCS:

The following heaters are turned ON:

| 3AC1RTEN | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER ENABLE |
| --- | --- |
| 3AC2RTEN | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |
| 3AC3RTEN | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |
| 3HR1RTEN | HRC 1 FITTING -Y,-Z REDUNDANT TRIM HEATER ENABLE |
| 3HR2RTEN | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |
| 3HR3RTEN | HRC 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |
| 3PSMRTEN | PSMC REDUNDANT TRIM HEATER ENABLE |
| 3FLCRTEN | FLCA REDUNDANT TRIM HEATER ENABLE |
| 3RCTRTEN | RCTU REDUNDANT TRIM HEATER ENABLE |
| 3SPYRTEN | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER ENABLE |
| 3SMYRTEN | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER ENABLE |
| 3SMZRTEN | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER ENABLE |

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS re-enables all the redundant trim heaters that would be disabled for a long eclipse passage.

Constraints:

The heater commands are doubled-up as a group to protect against SEU upset. One minor cycle between adjacent commands, and 16 mc between the groups.

NOTE: The redundant trim heaters are to be enabled 12 hours after the prime trim heaters following a long eclipse. This requirement is implemented by placing a 12 hour time delay in SCS 33 between calls to SCS 75 and SCS 76.

| Count | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3AC1RTEN | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3A1THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 3AC2RTEN | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3A2THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 3AC3RTEN | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |  | 3A3THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 3HR2RTEN | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3H2THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 3HR3RTEN | HRC 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |  | 3H3PZTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 3PSMRTEN | PSMC REDUNDANT TRIM HEATER ENABLE |  | 3APSMTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 3FLCRTEN | FLCA REDUNDANT TRIM HEATER ENABLE |  | 3FLCTHTB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 3RCTRTEN | RCTU REDUNDANT TRIM HEATER ENABLE |  | 3SITHTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 3SPYRTEN | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER ENABLE |  | 3ASPYTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | 3SMYRTEN | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER ENABLE |  | 3ASMYTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 3SMZRTEN | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER ENABLE |  | 3ASMZTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | 3AC1RTEN | ACIS 1 FITTING -Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3A1THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 3AC2RTEN | ACIS 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3A2THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 3AC3RTEN | ACIS 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |  | 3A3THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 3HR2RTEN | HRC 2 FITTING +Y,-Z REDUNDANT TRIM HEATER ENABLE |  | 3H2THTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | 3HR3RTEN | HRC 3 FITTING +Z REDUNDANT TRIM HEATER ENABLE |  | 3H3PZTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 3PSMRTEN | PSMC REDUNDANT TRIM HEATER ENABLE |  | 3APSMTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | 3FLCRTEN | FLCA REDUNDANT TRIM HEATER ENABLE |  | 3FLCTHTB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 3RCTRTEN | RCTU REDUNDANT TRIM HEATER ENABLE |  | 3SITHTRB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | 3SPYRTEN | ACIS SUPPORT STRUCTURE +Y REDUNDANT TRIM HEATER ENABLE |  | 3ASPYTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 3SMYRTEN | ACIS SUPPORT STRUCTURE -Y REDUNDANT TRIM HEATER ENABLE |  | 3ASMYTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | 3SMZRTEN | ACIS SUPPORT STRUCTURE - Z REDUNDANT TRIM HEATER ENABLE |  | 3ASMZTHB | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 77 -- OO - Halt OBC Safing Action

Description:

This is a “common” SCS that is called by a number of Safing Actions to accomplish halting the processor.

Main Steps in SCS:

Halt the OBC

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

This SCS is CALLED by the following SCSs:

SCS #: 5 -- OO - CCDM RCTU Command Wrap Test

SCS #: 7 -- OO - IRU Monitor Fault Safing Action

SCS #: 10 -- OO - Attitude Reference in Eclipse Monitor

SCS #: 11 -- OO - EPS Sunlight Overload Fault

SCS #: 12 -- OO - EPS Eclipse Overload Fault

SCS #: 13 -- OO - PCAD Sensor Processing Fault

Constraints:

If this SCS is edited, be sure that the final action is to Halt the Processor.  Many Safing Actions rely on this SCS to halt the processor.

This SCS defaults to enabled upon OBC reset.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSOHALT | SCS HALT OBC |  |  |  |  |  |  |  | LR | OBC |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 78 -- OO - Battery Connection / Halt OBC Safing Action

Description:

This SCS is a “common” SCS called by a number of Safing Actions to accomplish connecting the batteries, turning off the VDE, and halting the processor.

Main Steps in SCS:

- Call SCS #: 30 -- Battery Connection to Bus Safing Action to connect the batteries to the bus

- Turn off VDE A

- Halt the processor.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS, as described herein, is used in the On-Orbit Phase.

This SCS is CALLED by the following SCSs:

SCS #: 6 -- OO - Attitude/Rate Error Monitor Fault

SCS #: 8 -- OO - Sun Position Monitor Fault Safing Action

SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action

Constraints:

If this SCS is edited, be sure that no commands are deleted.  Many Safing Actions rely on this SCS to perform the functions identified above.

This SCS defaults to enabled upon OBC reset.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | AVDEAOF | VDE-A PWR OFF |  | AVDEAX | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COSOHALT | SCS HALT OBC |  |  |  |  |  |  |  | LR | OBC |  |  |  |  |
| 5 | 5 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 79 -- OO - NSM Transition

Description:

This SCS is a “common” SCS called by a number of Safing Actions to perform transition PCAD to Normal Sun Mode, and to safe the instruments.

Main Steps in SCS:

- Set IRU 1 and 2 to High Range

- Set Yaw Bias to zero

- Set OBC solar array mode to Autonomous

- Set Sun Mode control law to Auto

- Disable reaction momentum bias

- Transition to NSM

- Terminate SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands

- Terminate SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands

- Activate SCS #: 107 -- Main SI Safing.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase.

This SCS is ACTIVATED by the following SCSs:

SCS #: 16 -- Attitude Reference in Sunlight Monitor

SCS #: 23 -- OO - SADA Position or Temperature Monitor Fault

SCS #: 24 -- Unexpected Connection of the Batteries

SCS #: 98 -- Bright Star Normal Sun Mode

Constraints:

If this SCS is edited, be sure that no commands are deleted.  Many Safing Actions rely on this SCS to perform the functions identified above.

This SCS defaults to enabled upon OBC reset.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AIR1HRP1 | IRU-1 HIGH RANGE PRI (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AIR1HRP2 | IRU-1 HIGH RANGE PRI (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 15 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | AIR1HRR1 | IRU-1 HIGH RANGE RDNT (CHAN 0) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | AIR1HRR2 | IRU-1 HIGH RANGE RDNT (CHAN 1) |  | AIRU1R1X | HIGH | AIRU1R1Y | HIGH | AIRU1R2X | HIGH | EP | SD | 4 | 7 | 64 | K16 |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | AIR2HRP1 | IRU-2 HIGH RANGE PRI (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | AIR2HRP2 | IRU-2 HIGH RANGE PRI (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | AIR2HRR1 | IRU-2 HIGH RANGE RDNT (CHAN 0) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | AIR2HRR2 | IRU-2 HIGH RANGE RDNT (CHAN 1) |  | AIRU2R1X | HIGH | AIRU2R1Y | HIGH | AIRU2R2X | HIGH | EP | SD | 5 | 5 | 64 | K24 |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) – Relative Time Delay (minor cycles) | 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-21 | 17 | AOSETYAW | SET SUN MODE CONTROL LAW YAW BIASES (MULTI-PART) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17-21 | 17 | AOSETYW1 | Set Yaw Bias Cmd 1 -- 1st command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-21 | 17 | AOSETYW2 | Set Yaw Bias Cmd 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-21 | 17 | AOYAWHLD | Sun_Yaw_Bias_Hold -- Yaw Bias Rate for Hold Submode | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17-21 | 17 | AOYAWPNT | Sun_Yaw_Bias_Point -- Yaw Bias Rate for Point Submode | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 18 | AOSAMAUT | OBC SET SOLAR ARRAY MODE AUTONOMOUS |  | AOSAMDGD | AUTO |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 19 | AOSUNMAU | SET SUN MODE CNTL LAW (SUB MODE) TO AUTO |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 20 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 21 | AONSMSAF | Transition to Normal Sun Mode Safing |  | AOPCADMD | NSUN |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 22 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 22 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 87 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 23 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 23 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 88 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 24 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 24 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 24 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 25 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 80 -- OO - Standby State Timeout

Description:

This SCS is activated when the OBC transitions to Standby Online State (see Figure SCS 80-1).  This monitor protects against an OBC reset in the event that an SEU causes the IU to power-cycle.  As a result of an IU power-cycle, the Online OBC will be reset and will transition to Standby Online State.  This SCS enables the Observatory to continue operating in Normal Sun Mode (no science), and prevents a Safe Mode transition. Reference Flow SCS 80-1

Main Steps in SCS:

- Turn off VDE A in case thrusters were firing prior to the reset.

- Transition OBC to Normal Online State (see Figure SCS 80-1).

- Enable RCTU wrap tests, corresponding SCSs (25-27, 60, 5), and enable Reaction Wheel Safing SCSs (17-22).

- Reinitialize ADE and WDE EPIC counters

- Initialize/Activate PCAD via SCS #: 34 -- Configure PCAD, SCS #: 35 -- Activate Sensor Processing, SCS #: 36 -- Enter Standby Mode.

- Re-initialize Telescope Thermal Control

- Disable battery thermal and peak power control

- Disable OTG Motion

- Enable Telescope Thermal Control Process

- Enable OBA and HRMA Thermal Control, Select Primary Data Base

- Initialize EPS Manager and set state to Normal

- Call SCS #: 118 -- OBC Reset Reconfiguration Tasks

- Turn on VDE A to re-establish thruster capability

- Select OTG Primary Data Source

- Call SCS #: 107 -- Main SI Safing

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the On-Orbit Phase.

Constraints:

If this SCS is edited, be sure that no commands are deleted.  These commands are necessary to ensure that the Observatory is safed in the event of an OBC reset, and that operations continue on “A-side” hardware.

This SCS defaults to enabled upon OBC reset.  Disabling this SCS has no effect since the only time it is used is during an OBC reset, and at that time, it will be re-enabled.

If SCS 80 is “deleted” or incapacitated, an OBC reset will result in a Safe Mode transition.  Upon reset, the OBC will transition to Standby Online State, and will then time-out after 4-6 Major Frames, causing it to Halt.  This will trip the sequencer, and result in Safe Mode.

Figure SCS 80-1.   OBC State Transition Diagram

Flow SCS 80-1.   SCS 80 Flow Diagram

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AVDEAOF | VDE-A PWR OFF |  | AVDEAX | OFF |  |  |  |  | PC | LCC |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COOFPNM | NORMAL OFP STATE SELECT |  | CONLOFP | NRML |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COWRAPED | Set RCTU Command Wrap Enable/Disable |  |  |  |  |  |  |  | LR | SD |  |  |  |  |
| 4 | 4 | EP_RCTU | EP RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | PC_RCTU | PC RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | TS_RCTU | TE RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | SI_RCTU | SI RCTU -- 0 = Disable Wrap Test 1=Enable Wrap Test | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 25 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 26 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 27 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 60 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 20 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 22 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17-18 | 17 | ADEAO3IN | ADE-A INIT, CT3, SELECT 4.096 MHZ (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_1 | ADEAO3IN Data Bits D13 to D0 of Data Field -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_3 | ADEAO3IN Least Significant Word and First Command Word -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_4 | ADEAO3IN Filler bit -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_5 | ADEAO3IN Address Part of Data Field -- Address part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_6 | ADEAO3IN Channel Part of Data Field -- Channel part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_7 | ADEAO3IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 17-18 | 17 | ADEAO3_8 | ADEAO3IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4IN | ADE-A INIT, CT3, DIVIDE BY 166 (24.67 KHZ) (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_1 | ADEAO4IN Data Bits D13 to D0 of Data Field -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_3 | ADEAO4IN Least Significant Word and First Command Word -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_4 | ADEAO4IN Filler bit -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_5 | ADEAO4IN Address Part of Data Field -- Address part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_6 | ADEAO4IN Channel Part of Data Field -- Channel part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_7 | ADEAO4IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 19-20 | 18 | ADEAO4_8 | ADEAO4IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 21 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22-23 | 20 | ADEAO3IN | ADE-A INIT, CT3, SELECT 4.096 MHZ (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_1 | ADEAO3IN Data Bits D13 to D0 of Data Field -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_3 | ADEAO3IN Least Significant Word and First Command Word -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_4 | ADEAO3IN Filler bit -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_5 | ADEAO3IN Address Part of Data Field -- Address part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_6 | ADEAO3IN Channel Part of Data Field -- Channel part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_7 | ADEAO3IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 22-23 | 20 | ADEAO3_8 | ADEAO3IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4IN | ADE-A INIT, CT3, DIVIDE BY 166 (24.67 KHZ) (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_1 | ADEAO4IN Data Bits D13 to D0 of Data Field -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_3 | ADEAO4IN Least Significant Word and First Command Word -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_4 | ADEAO4IN Filler bit -- |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_5 | ADEAO4IN Address Part of Data Field -- Address part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_6 | ADEAO4IN Channel Part of Data Field -- Channel part of the data field |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_7 | ADEAO4IN Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 24-25 | 21 | ADEAO4_8 | ADEAO4IN Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOADAC3A |  | AOADAC3C |  | AOADAC3E |  | PC | SD |  |  |  |  |
| 26 | 22 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 22 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 34 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 23 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 23 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 24 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 24 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 36 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 25 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 27 | 4OBATCDS | DISABLE BATTERY THERMAL CONTROL |  | 4OACBATH | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 28 | 4OBAPKDS | DISABLE BATTERY PEAK POWER CONTROL |  | 4OPPMEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 29 | 4OOTGDS | DISABLE OTG MOTION |  | 4OOTGMEF | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 30 | 4OTTCPEN | TEL THERMAL CONTROL PROCESS ENABLE |  | 4OTCPEN | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 5 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 32 | 4OOBTCEN | ENABLE OBA THERMAL CONTROL |  | 4OACOBAH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 33 | 4OHMTCEN | ENABLE HRMA THERMAL CONTROL |  | 4OACHRMH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 34 | 4OTTHCDB | TELE THERM CONTROL DATA BASE SELECT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 34 | 4OTTHCD1 | 4OTTHCDB- Filler -- |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 34 | 4OTTHCD2 | 4OTTHCDB - Data Base to select -- 0-Primary Database 1-Secondary Database 2-Tertiary Database | 00 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 35 | EOINISET | Set initialization flag to true |  | EGCTTEL3 | OVRT |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 36 | EOEMGSTN | EPS Manager State (B4) Normal--Build 4 |  | EGCTTEL1 | NORM |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 37 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 37 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 118 |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | 38 | AVDEAON | VDE-A PWR ON |  | AVDEAX | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 43 | 39 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 39 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 40 | AVDEAON | VDE-A PWR ON |  | AVDEAX | ON |  |  |  |  | PC | LCC |  |  |  |  |
| 45 | 41 | 4OOTGPT | SELECT OTG PRIMARY DATA SOURCE |  | 4OOTGDAS | PRI |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 42 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 42 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | 43 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 81 -- SIM Move to Safe Position

Description:

This SCS positions the SIM so that the x-ray focal point is between the ACIS and HRC detectors.

Main Steps in SCS:

SIMGOTO serial digital command with parameter value [000101101100101]. This is +23336 steps, absolute position. To use this position, divide by 8 to get 2917, then encode to binary.

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Placing the x-ray focal point between the instruments provides protection against sun radiation impinging on the instruments.

The SCS is called by SCS #: 107 -- Main SI Safing

Constraints:

The SEA that is ON will respond to the command (e.g. no A or B side command sequences required)

All commands require the SIM SEA serial digital header properly filled out.

Two commands minimum - header command and data command.

The SIMGOTO commands are doubled-up to protect against SEU upset. The commands are separated by 1024 minor cycles (65.6 seconds, or two major frames) because of SIM sync requirements.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 1 | 1 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 188 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | 3TSCMBEN | SIM TSC MOTOR ENABLE--The TSC Motor Enable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply power to either motor in response to this command, only to the motor driver. The Goto Position command powers on the motor. The TSC Motor Enable command must be issued to select a motor and apply power to the motor driver prior to issuing the Goto Position command. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. |  | 3SMOTPEN | ON | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 3 | 3 | 3TSCGOTO | SIM GO TO POSITION--The SIM Go To Position command causes the SEA software to initiate movement of one of the drive motors. This command will have no effect unless power has already been applied to the motor driver by a previous Motor Enable command. The SEA software will hold off execution of this command until any motor motion already in progress is completed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 3TSCGOTO | SIM GOTO Mechanism Position Value -- This field is a signed 15 bit integer used to specify a mechanism position relative to the origin. For the TSC, one LSB equals 160 degrees of motor rotation. For the FA, one LSB equals 20 degrees of motor rotation. The TSC or FA motor is moved depending on which one has been selected with the Motor Enable command. | 000101101100101 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | 3TSCMBDS | SIM TSC MOTOR DISABLE--The TSC Motor Disable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply or disconnect power to either motor in response to this command, only to the motor driver. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. Therefore, it cannot be used to stop a motion in progress. The Motor Stop command is used for that purpose. |  | 3SMOTPEN | OFF | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1024 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 6 | 6 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 188 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 3TSCMBEN | SIM TSC MOTOR ENABLE--The TSC Motor Enable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply power to either motor in response to this command, only to the motor driver. The Goto Position command powers on the motor. The TSC Motor Enable command must be issued to select a motor and apply power to the motor driver prior to issuing the Goto Position command. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. |  | 3SMOTPEN | ON | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 8 | 8 | 3TSCGOTO | SIM GO TO POSITION--The SIM Go To Position command causes the SEA software to initiate movement of one of the drive motors. This command will have no effect unless power has already been applied to the motor driver by a previous Motor Enable command. The SEA software will hold off execution of this command until any motor motion already in progress is completed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | 3TSCGOTO | SIM GOTO Mechanism Position Value -- This field is a signed 15 bit integer used to specify a mechanism position relative to the origin. For the TSC, one LSB equals 160 degrees of motor rotation. | 000101101100101 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 3TSCMBDS | SIM TSC MOTOR DISABLE--The TSC Motor Disable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply or disconnect power to either motor in response to this command, only to the motor driver. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. Therefore, it cannot be used to stop a motion in progress. The Motor Stop command is used for that purpose. |  | 3SMOTPEN | OFF | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 82 -- OTG Emergency Halt

Description:

This SCS halts the motion of either the LETG or the HETG using MCE hardware commands in the event that they are in motion when a safing event occurs.  The commanding first disables OTG motion and power supplies using MCE-B commands, then repeats the commanding using MCE-A commands.

Main Steps in SCS:

Refer to Flow SCS 82-1 for the steps in moving the OTGs.

Flow SCS 82-1 Emergency OTG Halt Sequence

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS is used to halt OTG motion in the event that the daily loads are stopped.

This SCS is called by SCS #: 107 -- Main SI Safing

Constraints:

The commands in the sequence will disable any OTG motion that is in process.

Each command is doubled up individually with a separation of 16 mc (1 second).

NOTE: This SCS uses both MCE-B and MCE-A side commands to control the OTGs.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4EXHGBDS | MCE B: DISA HETG INSERTION/RETRACTION |  | 4HEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | 4EXHGBDS | MCE B: DISA HETG INSERTION/RETRACTION |  | 4HEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | 4EXLGBDS | MCE B:DISA LETG INSERTION/RETRACTION |  | 4LEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 4EXLGBDS | MCE B:DISA LETG INSERTION/RETRACTION |  | 4LEXRBX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 4MC28BDS | MCE B: DISA 28 VOLT DC/DC CONV |  | 4M28IRBX | DISA | 4MP28BV | 0/.6 |  |  | TS | HLP |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 4MC28BDS | MCE B: DISA 28 VOLT DC/DC CONV |  | 4M28IRBX | DISA | 4MP28BV | 0/.6 |  |  | TS | HLP |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 4MC5BDS | MCE B: DISA 5 VOLT DC/DC CONV |  | 4M5IRBX | DISA | 4MP5BV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | 4MC5BDS | MCE B: DISA 5 VOLT DC/DC CONV |  | 4M5IRBX | DISA | 4MP5BV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 4EXHGADS | MCE A: DISA HETG INSERTION/RETRACTION |  | 4HEXRAX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | 4EXHGADS | MCE A: DISA HETG INSERTION/RETRACTION |  | 4HEXRAX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 4EXLGADS | MCE A:DISA LETG INSERTION/RETRACTION |  | 4LEXRAX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | 4EXLGADS | MCE A:DISA LETG INSERTION/RETRACTION |  | 4LEXRAX | DISA |  |  |  |  | TS | HLP |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 4MC28ADS | MCE A: DISA 28 VOLT DC/DC CONV |  | 4M28IRAX | DISA | 4MP28AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | 4MC28ADS | MCE A: DISA 28 VOLT DC/DC CONV |  | 4M28IRAX | DISA | 4MP28AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 4MC5ADS | MCE A: DISA 5 VOLT DC/DC CONV |  | 4M5IRAX | DISA | 4MP5AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | 4MC5ADS | MCE A: DISA 5 VOLT DC/DC CONV |  | 4M5IRAX | DISA | 4MP5AV | 0/.5 |  |  | TS | HLP |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 109 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 110 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COENASX | ENABLE SCS |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 36 | COENAS1 | SCS Number | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | COACTS1 | SCS Number | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | COACTS2 | Repeat Count | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 83 – No-op SCS

Description:

This SCS was formerly the ACIS High Radiation Command, and a Spare SCS  It is now designated a No-op SCS that will contain only a End SCS Command.  This SCS is called in the EPS Flight Software Unexpected Connection Fault Handling code and is intended to act as a No-op.  See the New Eclipse Handling Plan for rationale.

Main Steps in SCS:

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated in the event that the Unexpected Connection Fault Handling code executes.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 84 – Command Normal Sun Mode

Description:

This SCS is activated by SCS #: 107 -- Main SI Safing, and will only run in the event that SCS 84 has been enabled.

Prior to the introduction of the Propulsion Temperature Safing Monitor in July 2006, the purpose of SCS 84 was to protect the propulsion lines from an extended period of cold temperatures.  If SCS 107 executed, the mission load would stop, possibly leaving the spacecraft at an unfavorable thermal attitude that would allow the lines to get too cold.   With SCS 84 commanding a Normal Sun attitude, this would be averted.

With the Propulsion Temperature Safing Monitor in place, SCS 84 has been left in a disabled state and is no longer used operationally to provide thermal protection for the propulsion lines and valves.  As such, it can be considered as a “spare” SCS, or be used to support the handling plans for other performance issues or concerns that may arise in the future.

Main Steps in SCS:

1. AONSMSAF -- command Normal Sun Mode as a safing action

2. End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is activated by SCS 107.

Constraints:

In the case of an unexpected OBC reset (such as those experienced in the 2008 and 2010 IU resets), SCS 84 is enabled by default as part of the OBC startup.  In this case, a clean-up action must be taken operationally to disable SCS 84 at the earliest opportunity.

Considering the implementation of the Science Only Safing Action capability, SCS 84 should continue to remain in a disabled state so as not to disrupt Vehicle mission loads for events that only require science instrument safing (for example, a high radiation event).  For events where both the Vehicle and Observing loads must be stopped (for example, a Bright Star Hold event), appropriate commanding has been placed in those safing SCSs to accomplish this task; however, SCS 84 must remain in a disabled state for these cases as well so as not to disrupt an intended transition to Bright Star Hold.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | AONSMSAF | Transition to Normal Sun Mode Safing |  | AOPCADMD | NSUN |  |  |  |  | NA | NA | 21 | AONSMSAF | Transition to Normal Sun Mode Safing |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 85 -- Spare SCS

Description:

This SCS is not used.  This SCS was formerly the HRC Radiation High Command sequence, and is now a spare.

Main Steps in SCS:

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 86 -- Spare SCS

Description:

This SCS is not used.  This SCS is formerly the HRC Radiation Low Command sequence. It was actually never defined, and has been empty since before launch.

Main Steps in SCS:

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands

Description:

This SCS reduces the HRC-I MCP top and bottom plate voltages to safe levels.

Main Steps in SCS:

- Disable HRC-I current limiting

- Set HRC-I Top Plate voltage to level 42

- Set HRC-I Bottom Plate voltage to level 53

- Wait 32 minor cycles

- Enable HRC-I current limiting.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS sets the HRC-I MCP top and bottom plates to levels that will not harm the instrument when AXAF is not in a dither state. This sequence would normally be called by a daily load command as part of normal observation scheduling.

This SCS is TERMINATED by SCS SCS #: 79 -- OO - NSM Transition

This SCS is CALLED by the following SCSs:

SCS #: 91 -- HRC Dither Control

SCS #: 104 -- HRC Safing Part 1

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Commands are doubled-up individually to protect against SEUs.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 42 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 42 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 53 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 53 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands

Description:

This SCS reduces the HRC-S MCP top and bottom plate voltages to safe levels.

Main Steps in SCS:

- Disable HRC-S current limiting

- Set HRC-S Top Plate voltage to level 43

- Set HRC-S Bottom Plate voltage to level 54

- Wait 32 minor cycles

- Enable HRC-S current limiting.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS sets the HRC-S MCP top and bottom plates to levels that will not harm the instrument when AXAF is not in a dither state. This sequence would normally be called by a daily load command as part of normal observation scheduling.

This SCS is TERMINATED by SCS SCS #: 79 -- OO - NSM Transition

This SCS is CALLED by the following SCSs:

SCS #: 91 -- HRC Dither Control

SCS #: 104 -- HRC Safing Part 1

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Commands are doubled-up individually to protect against SEUs.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 43 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 43 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 54 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 54 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 89 -- HRC Scheduled/Dither HRC-I HV Ramp Up Commands

Description:

This SCS performs a controlled ramp-up of HRC-I MCP high voltages for observations.

This SCS was modified via patch during the OAC period to change the last step voltage levels.

Main Steps in SCS:

Refer to Flow SCS 89-1 for the main sequence of commands. Time delays are not shown.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to step up the HRC-I MCP high voltage for an observation.

This SCS is CALLED by SCS #: 91 -- HRC Dither Control

This SCS is TERMINATED by SCS #: 104 -- HRC Safing Part 1

This SCS is DISABLED by SCS #: 104 -- HRC Safing Part 1

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Command are doubled-up individually to protect against SEUs.

Flow SCS 89-1 HRC-I MCP HV Ramp Up

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2IMTBHV1 | Filler -- |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 53 | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 53 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2IMTTHV1 | Filler -- |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 42 | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 42 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 21 | 21 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 61 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 23 | 23 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 61 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 25 | 25 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 50 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 27 | 27 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 50 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 31 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 37 | 37 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 68 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 39 | 39 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 68 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 41 | 41 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 41 | 41 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 57 |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | 43 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 43 | 43 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | 43 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 57 |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 46 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | 47 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 48 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 50 | 50 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 50 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | 51 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 52 | 52 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 52 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 53 | 53 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 53 | 53 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 76 |  |  |  |  |  |  |  |  |  |  |  |  |
| 54 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 55 | 55 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 76 |  |  |  |  |  |  |  |  |  |  |  |  |
| 56 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 57 | 57 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 57 | 57 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 65 |  |  |  |  |  |  |  |  |  |  |  |  |
| 58 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 59 | 59 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 65 |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 61 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 63 | 63 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 64 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 65 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 66 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 67 | 67 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 68 | 68 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 68 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 69 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 69 | 69 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 69 | 69 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 83 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70 | 70 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 70 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 71 | 71 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 71 | 71 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 71 | 71 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 83 |  |  |  |  |  |  |  |  |  |  |  |  |
| 72 | 72 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 72 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 73 | 73 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 73 | 73 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 73 | 73 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 72 |  |  |  |  |  |  |  |  |  |  |  |  |
| 74 | 74 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 74 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75 | 75 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 75 | 75 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 75 | 75 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 72 |  |  |  |  |  |  |  |  |  |  |  |  |
| 76 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 77 | 77 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 78 | 78 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 78 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 79 | 79 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 80 | 80 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 80 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 81 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 82 | 82 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 82 | 82 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 83 | 83 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 84 | 84 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 84 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 85 | 85 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 85 | 85 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 85 | 85 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 89 |  |  |  |  |  |  |  |  |  |  |  |  |
| 86 | 86 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 86 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 87 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 87 | 87 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 87 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 89 |  |  |  |  |  |  |  |  |  |  |  |  |
| 88 | 88 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 88 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 89 | 89 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 89 | 89 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 89 | 89 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 90 | 90 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 90 | 90 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 91 | 91 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 91 | 91 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 91 | 91 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 92 | 92 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 92 | 92 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 93 | 93 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 94 | 94 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 94 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 95 | 95 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 96 | 96 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 96 | 96 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 97 | 97 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 90 -- HRC Scheduled/Dither HRC-S HV Ramp Up Commands

Description:

This SCS performs a controlled ramp-up of HRC-S MCP high voltages for observations.

Main Steps in SCS:

Refer to Flow SCS 90-1 for the main sequence of commands. Time delays are not shown.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used to step up the HRC-S MCP high voltage for an observation.

This SCS is CALLED by SCS #: 91 -- HRC Dither Control

This SCS is TERMINATED by SCS #: 104 -- HRC Safing Part 1

This SCS is DISABLED by SCS #: 104 -- HRC Safing Part 1

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Command are doubled-up individually to protect against SEUs.

Flow SCS 90-1 HRC-S MCP HV Ramp Up

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 57 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 57 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 46 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 46 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 21 | 21 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 67 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 23 | 23 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 67 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 25 | 25 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 56 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 27 | 27 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 27 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 56 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 | 31 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | 35 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 37 | 37 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | 37 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 39 | 39 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 39 | 39 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 77 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40 | 40 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 41 | 41 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 41 | 41 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 66 |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | 42 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 42 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | 43 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 43 | 43 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | 43 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 66 |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | 44 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 44 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 46 | 46 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 46 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | 47 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 48 | 48 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 48 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 50 | 50 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 50 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | 51 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 52 | 52 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 52 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 53 | 53 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 53 | 53 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 87 |  |  |  |  |  |  |  |  |  |  |  |  |
| 54 | 54 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 54 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 55 | 55 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 55 | 55 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 87 |  |  |  |  |  |  |  |  |  |  |  |  |
| 56 | 56 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 56 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 57 | 57 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 57 | 57 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 76 |  |  |  |  |  |  |  |  |  |  |  |  |
| 58 | 58 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 58 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 59 | 59 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | 59 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 76 |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 60 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 60 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 61 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 62 | 62 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 62 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 63 | 63 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 64 | 64 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 64 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 65 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 66 | 66 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 66 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 67 | 67 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 68 | 68 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 68 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 69 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 69 | 69 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 69 | 69 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 97 |  |  |  |  |  |  |  |  |  |  |  |  |
| 70 | 70 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 70 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 71 | 71 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 71 | 71 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 71 | 71 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 97 |  |  |  |  |  |  |  |  |  |  |  |  |
| 72 | 72 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 72 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 73 | 73 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 73 | 73 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 73 | 73 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 86 |  |  |  |  |  |  |  |  |  |  |  |  |
| 74 | 74 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 74 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 75 | 75 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 75 | 75 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 75 | 75 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 86 |  |  |  |  |  |  |  |  |  |  |  |  |
| 76 | 76 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 76 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 77 | 77 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 78 | 78 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 78 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 79 | 79 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 80 | 80 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 80 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 469 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 81 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 82 | 82 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 82 | 82 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 83 | 83 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 84 | 84 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 84 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 85 | 85 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 85 | 85 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 85 | 85 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 105 |  |  |  |  |  |  |  |  |  |  |  |  |
| 86 | 86 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 86 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 87 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 87 | 87 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 87 | 87 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 105 |  |  |  |  |  |  |  |  |  |  |  |  |
| 88 | 88 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 88 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 89 | 89 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 89 | 89 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 89 | 89 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 93 |  |  |  |  |  |  |  |  |  |  |  |  |
| 90 | 90 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 90 | 90 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 91 | 91 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 91 | 91 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 91 | 91 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 93 |  |  |  |  |  |  |  |  |  |  |  |  |
| 92 | 92 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 92 | 92 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 93 | 93 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 94 | 94 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 94 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 95 | 95 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 96 | 96 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 96 | 96 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 97 | 97 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 91 -- HRC Dither Control

Description:

This SCS controls the HRC High Voltage levels during an observation based on whether Chandra is dithering or not.

The SCS contains “event waits”, pauses in the execution of the SCS until a condition is met. The first event wait watches for the event “F_Dither_On= 1 (TRUE)”. If the event is satisfied, the SCS calls the two on-board SCSs that ramp up the HRC MCP high voltages (SCS #: 89 -- HRC Scheduled/Dither HRC-I HV Ramp Up Commands, SCS #: 90 -- HRC Scheduled/Dither HRC-S HV Ramp Up Commands) and the observation is started. The SCS that is enabled by the daily load command sequence is the one that actually executes, the one that controls the active detector for the immediate observation. The SCS sequence stops at the next event wait, which is “F_Dither_On= 0 (FALSE)”.  When the event is satisfied (AXAF is no longer dithering), the SCS continues, calling the on-board SCS that ramp down the HRC MCP HV (SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands, SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands).

Post-OAC changes were made to provide continuous dithering capability. The change that affects the running of this SCS is as follows:  Patch PCAD Subfunction "PCAD Scheduling" to change the flag F_Dither_On:

from:

F_Dither_On = (PCAD Mode=NPM) AND (ACA Sequence=Kalman) AND (F_Dither=Enabled)

to:

F_Dither_On = ( (PCAD Mode=NPM) OR (PCAD Mode=NMM) ) AND (F_Dither=Enabled)

Main Steps in SCS:

Refer to Flow SCS 91-1 for the major steps in this SCS.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the normal observation phase. At the beginning of each HRC observation, SCS 91 is activated.

Constraints:

All commands are software commands, so command doubling is not necessary.

The ground is responsible for enabling the correct MCP HV ramp-up SCSs for a particular observation. This is part of HRC observation scheduling.

SCS 91 must be activated for each individual HRC observation to provide the proper dither protection.

Flow SCS 91-1 HRC Dither Control SCS

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSEVTWT | EVENT WAIT (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSEVTW1 | COSEVTWT -Pointer into K-Constant Event Table -- Event Number in K Constant Table | 28 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 89 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 90 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSEVTWT | EVENT WAIT (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSEVTW1 | COSEVTWT -Pointer into K-Constant Event Table -- Event Number in K Constant Table | 27 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 87 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 88 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 92 -- HRC-I MCP HV On

Description:

This SCS turns on and prepares the HRC-I MCP for an observation.

Main Steps in SCS:

Refer to Flow SCS 92-1 for the main steps in the sequence. Time delays are not shown.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used for normal HRC observations. It is not accessed by any on-board protected SCS.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Commands are doubled up individually to protect against SEUs.

Flow SCS 92-1, HRC-I MCP HV On

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2IMCLDS | IMAGING HV CURRENT LIMIT DISABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2IMCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2IMTTHV | IMAGING DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2IMTPAST | NONE | 2IMHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2IMTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2IMTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2IMTBHV | IMAGING DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2IMBPAST | NONE | 2IMHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2IMTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2IMTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF IM BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2IMHVON | IMAGING DET HV ON--TURNS ON IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 2IMONST | ON |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2IMHVON | IMAGING DET HV ON--TURNS ON IM HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 2IMONST | ON |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2IMCLEN | IMAGING HV CURRENT LIMIT ENABLE--DISABLES IM HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2IMCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 93 -- HRC-S MCP HV On

Description:

This SCS turns on and prepares the HRC-S MCP for an observation.

Main Steps in SCS:

Refer to Flow SCS 93-1 for the main steps in the sequence. Time delays are not shown.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used for normal HRC observations. It is not accessed by any on-board protected SCS.

Constraints:

This SCS should only be modified and approved for use by the Chandra X-ray Science Center.

Commands are doubled up individually to protect against SEUs.

Flow SCS 93-1, HRC-S MCP HV On

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 2SPCLDS | SPECT HV CURRENT LIMIT DISABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 DISABLES THE LIMITER. |  | 2SPCLST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 5 | 5 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2SPTTHV | SPECT DET TOP PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. |  | 2SPTPAST | NONE | 2SPHBLV | NONE |  |  | SI | SD |  |  |  |  |
| 7 | 7 | 2SPTTHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 2SPTTHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP TOP CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (02 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -40 VOLTS PER COUNT. EXAMPLES: 0200 HEX = 0 VOLTS, 0220H=-640 VOLTS, 027FH=-5080 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 9 | 9 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTBHV | SPECT DET BOTTOM PLATE HV SETTING-- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. |  | 2SPBPAST | NONE | 2SPHVLV | NONE |  |  | SI | SD |  |  |  |  |
| 11 | 11 | 2SPTBHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | 11 | 2SPTBHV2 | VOLTAGE STEPS -- SETS VOLTAGE AT TOP OF SP BOTTOM CHANNEL PLATE. BITS 19-26 ARE THE COMMAND NUMBER (03 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT -20 VOLTS PER COUNT. EXAMPLES: 0300 HEX = 0 VOLTS, 0320H=-320 VOLTS, 037FH=-2540 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 13 | 2SPHVON | SPECT DET HV ON--TURNS ON SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 2SPONST | ON |  |  |  |  | SI | SD |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 15 | 2SPHVON | SPECT DET HV ON--TURNS ON SP HVPS. BITS 19-26 ARE THE COMMAND NUMBER (01 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 TURNS ON THE SUPPLY. |  | 2SPONST | ON |  |  |  |  | SI | SD |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 17 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | 2SPCLEN | SPECT HV CURRENT LIMIT ENABLE--DISABLES SP HV OUTPUT CURRENT LIMITER. BITS 19-26 ARE THE COMMAND NUMBER (04 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 ENABLES THE LIMITER. |  | 2SPCLST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 94 -- OBA Heater Enable

Description:

This SCS enables OBA heater control.

A consequence of long eclipse events is that OBA thermal control must be managed. The object is to assure the OBA heaters are not restarted during the eclipse event, but also make sure they do get restarted before or after the event. This is discussed below:

SCS #: 26 -- TS RCTU Monitor or Telescope Thermal Control Fault is the TS-RCTU wrap test SCS action, and SCS 26 and SCS 94 together is the telescope thermal control safing action. SCS 94 is called from SCS 26. OBA thermal control during long eclipse events is controlled by the ability to enable or disable SCS 94 from other SCSs.

The Eclipse ATS and SCS 32 for long eclipse will contain the commands to disable SCS 94, and SCS 33 will contain the commands to re-enable SCS 94. Therefore, going into the eclipse, either by design or by fault, SCS 94 is prevented from running and restarting OBA thermal control if SCS 26 is triggered. Upon exit from eclipse, SCS 33 restarts OBA thermal control, but also re-enables SCS 94, so that subsequent calls to SCS 26 and hence SCS 94 will execute.

If SCS 32 were to execute by a subsequent fault between the long eclipses, and disable SCS 94, CHANDRA will detect that it is in sunlight, disconnect the batteries, and SCS 33 will run, thereby restarting thermal control and re-enabling SCS 94. Refer to Figure SCS 94-1 for a diagram depicting use of SCS 94.

Main Steps in SCS:

Reset Telescope Thermal Control

Enable OBA Thermal Control

End SCS

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is for on-orbit use.

Constraints:

Figure SCS 94-1 OBA Thermal Control Management for Long Eclipses

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4OTELTCR | REINITIALIZE TELESCOPE THERMAL CONTROL |  | 4ORINITC | TRUE |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | 4OOBTCEN | ENABLE OBA THERMAL CONTROL |  | 4OACOBAH | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 95 -- EPHIN Failure

Description:

This SCS is activated by the FSW in the event the IEPHIN instrument is detected failed.

Main Steps in SCS:

Disable Radiation Monitor Function

Call SCS #: 107 -- Main SI Safing

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The same action that is taken in a high radiation environment is taken when the IEPHIN has been detected failed.

Constraints:

Software commands only, therefore command doubling is not required.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OORMPDS | RADIATION MONITOR PROCESS DISABLE |  | CORADMEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 96 – PEA Reset

Description:

This SCS performs a function if the sixth-bit of the ACA global status word indicates that the PEA has experienced a reset.

At this time there is not action to be taken, but this SCS is a placeholder.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS would be used in the on-orbit phase.

Constraints:

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 97 -- Spare SCS

Description:

This SCS is not used.  This SCS was formerly the ACA Processing Initialization. It was cleared out as part of patch request PR93 when it no longer was being used by anyone.

Main Steps in SCS:

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 98 -- Bright Star Normal Sun Mode

Description:

This SCS is used as part of Bright Star/Commanded Attitude Monitor response. It is called by SCS #: 28 -- Bright Star or Commanded Attitude Monitor.

This SCS is normally disabled whenever observation attitudes are such that the sun is within the Fine Sun Sensor FOV. Whenever it is planned to observe a target at an attitude where the sun is NOT in the Fine Sun Sensor FOV, then this SCS is enabled. It provides extra protection to the Observatory by transiting to Normal Sun Mode instead of Bright Star Mode when observing very close to sun exclusion limits.

If executed, this SCS activates SCS #: 79 -- OO - NSM Transition and disables SCS #: 99 -- Bright Star SI Safing to keep it from running when it is subsequently called by SCS 28.

Main Steps in SCS:

Four Minor Cycle relative time delay

Activate SCS 79

Disable SCS 99

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the on-orbit phase.

Constraints:

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 79 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | CODISASX | CODISASX - SCS NUMBER -- SCS Number | 99 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 99 -- Bright Star SI Safing

Description:

This SCS is used as part of Bright Star/Commanded Attitude Monitor response. It is called by SCS #: 28 -- Bright Star or Commanded Attitude Monitor.

When this SCS is executed, it is because the Bright Star/Commanded Attitude Monitor tripped, and the Observatory is going to sit where it is on the stars that it sees, even though it may not know where it is. SCS 99 activates SCS #: 107 -- Main SI Safing to safe the instruments. SCS 99 is executed only when SCS #: 98 -- Bright Star Normal Sun Mode is disabled (also called by SCS 28) and that only occurs when an observation attitude is such that the sun is within the Fine Sun Sensor FOV.

Main Steps in SCS:

Activate SCS 107

End SCS

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the on-orbit phase.

Constraints:

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 100 – Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 101 – Checksum CPE Patches

Description:

This SCS is used to patch the CPE, making it possible to achieve the result of installing all checksummed patches upon Safe Mode entry, without complications due to checksum differences.  This SCS contains all CPE checksummed patches, so that it can be assured that all patches will be installed correctly, and the proper order.

SCS 101 is enabled and activated only from SCS #: 31 -- Safe Mode Reconfiguration in the event of Safe Mode entry.

This SCS is to be updated when future CPE checksum code modifications are made.

CPE patches included in this SCS are as follows:

- Update of Momentum Auto-unload Deadzone K-constant which was directly uplinked to the CPE via PR-178 in June, 2004.

- Update of Momentum Auto-unload Threshold K-constant which was directly uplinked to the CPE via PR-319 in August, 2012

Main Steps in SCS:

The steps for this SCS are to:

- Set Subformat to EPS (necessary to patch CPE)

- Patch CPE with Momentum Auto-unload System K-constant patches

- Set Subformat to Normal

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in the on-orbit phase.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OFMTSEPS | OBC TLM SMODE SLCT EPS DATA--OBC Telemetry Sub-Mode Format Select - EPS calculated or processed data |  | COTLRDSF | EPS |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | ACMEMLCL | CPE CLEAR MEMORY LOAD BUFFER |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 4 | 4 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | ACPMMLD0 | CPE Ram Load Command Header--This command specifies the first serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 5 | 5 | ACPECN02 | CPE Memory Load Header Constant -- This field is defined with a constant, a value of binary (0000 0000) - essentially a space filler since the CPE requires word pairs. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | ACPMMLD1 | CPE Ram Load Command Word Count--This command specifies the second serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 7 | 7 | ACPECB12 | CPE Memory Load Checksum Bypass Flag -- This flag, when set, alerts the CPE firmware that the contents of the buffer are modifying a defined checksummed region of CPE RAM memory. A new expected checksum must be loaded in the sequence if load is performed within a checksummed region of CPE RAM memory. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | ACPESQ13 | CPE Memory Load Sequence Flag -- This flag, when set, indicates that the current load buffer is the last in a sequence of load buffers or the only load buffer in a sequence. | 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | ACPEWL14 | CPE Memory Load Word Count -- This field is used to specifiy the number of data (byte pairs) or word that follow in the load sequence. 0 represents 64 data byte pairs follow. Each data byte pair is a sequence of two commands carring the 8 MSBs and the 8 LSBs of a single CPE data word. | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | ACPMMLD2 | CPE Ram Load Command MSB Start Address--This command specifies the third serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 9 | 9 | ACPEAD22 | CPE Memory Load MSByte Start Address -- This field is used to specify the most significant byte of a 16-bit start address at which the data load begins. | 96 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | ACPMMLD3 | CPE Ram Load Command LSB Start Address--This command specifies the fourth serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 11 | 11 | ACPEAD32 | CPE Memory Load LSByte Start Address -- This field is used to specify the least significant byte of a 16-bit start address at which the data load begins. | 191 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | ACPMMLD4 | CPE Ram Load Command MSB Data--This command specifies the fifth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 13 | 13 | ACPEDT42 | CPE Memory Load MSByte Of Data -- This field is used to specify the most significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 80 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | ACPMMLD5 | CPE Ram Load Command LSB Data--This command specifies the sixth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 15 | 15 | ACPEDT52 | CPE Memory Load LSByte Of Data -- This field is used to specify the least significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 16 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | ACPMMLD4 | CPE Ram Load Command MSB Data--This command specifies the fifth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 17 | 17 | ACPEDT42 | CPE Memory Load MSByte Of Data -- This field is used to specify the most significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | ACPMMLD5 | CPE Ram Load Command LSB Data--This command specifies the sixth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 19 | 19 | ACPEDT52 | CPE Memory Load LSByte Of Data -- This field is used to specify the least significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | ACPMMLD4 | CPE Ram Load Command MSB Data--This command specifies the fifth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 21 | 21 | ACPEDT42 | CPE Memory Load MSByte Of Data -- This field is used to specify the most significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 100 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | ACPMMLD5 | CPE Ram Load Command LSB Data--This command specifies the sixth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 23 | 23 | ACPEDT52 | CPE Memory Load LSByte Of Data -- This field is used to specify the least significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 24 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | ACPMMLD4 | CPE Ram Load Command MSB Data--This command specifies the fifth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 25 | 25 | ACPEDT42 | CPE Memory Load MSByte Of Data -- This field is used to specify the most significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | ACPMMLD5 | CPE Ram Load Command LSB Data--This command specifies the sixth serial digital h/w command in a CPE RAM Load sequence and may repeat up to 64 times in a load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 27 | 27 | ACPEDT52 | CPE Memory Load LSByte Of Data -- This field is used to specify the least significant byte of a 16-bit data word. A single CPE Load Command sequence may consist of 64 data byte pairs. | 6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 28 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | ACPMMLD6 | Ram Load Command MSB CPE Memory Checksum-- Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 29 | 29 | ACPECS62 | CPE Memory Load MSByte of CPE Memory Checksum -- This field is used to specify the most significant byte of a 16-bit memory load checksum. | 96 |  |  |  |  |  |  |  |  |  |  |  |  |
| 30 | 30 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | ACPMMLD7 | Ram Load Command LSB CPE Memory Checksum-- Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 31 | 31 | ACPECS72 | CPE Memory Load LSByte of CPE Memory Checksum -- This field is used to specify the least significant byte of a 16-bit memory load checksum. | 93 |  |  |  |  |  |  |  |  |  |  |  |  |
| 32 | 32 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | ACPMMLD8 | Ram Load Command MSB Buffer Checksum--This command specifies the second to the last serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 33 | 33 | ACPECS82 | CPE Memory Load MSByte of Memory Buffer Checksum -- This field is used to specify the most significant byte of a 16-bit memory load buffer checksum. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 34 | 34 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | ACPMMLD9 | Ram Load Command LSB Buffer Checksum--This command specifies the last serial digital h/w command in a CPE RAM Load sequence. Additional information may be found in the CPE DM05 section 3.2.2.3.2 CPE RAM Memory Load. |  |  |  |  |  |  |  | NA |  |  |  |  |  |
| 35 | 35 | ACPECS92 | CPE Memory Load LSByte of Memory Buffer Checksum -- This field is used to specify the least significant byte of a 16-bit memory load buffer checksum. | 94 |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | 36 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | ACMEMLD | CPE COMPLETE MEMORY LOAD |  |  |  |  |  |  |  | PC | SD |  |  |  |  |
| 38 | 38 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | OFMTSNRM | OBC TLM SMODE SLCT NORM DATA--OBC Telemetry Sub-Mode Format Select - EPS calculated or processed data |  | COTLRDSF | NORM |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 102 – Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 103 – Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 104 -- HRC Safing Part 1

Description:

This SCS was created as part of the SI safing enhancement and was later modified to take out all HRC mechanism commanding. This SCS is called by SCS #: 107 -- Main SI Safing.  This SCS terminates HRC SCSs that may be running before ramping down the HV and turning off the A&B Shield HVPS.

Main Steps in SCS:

- Terminate the following SCSs:

SCS #: 89 -- HRC Scheduled/Dither HRC-I HV Ramp Up Commands

SCS #: 90 -- HRC Scheduled/Dither HRC-S HV Ramp Up Commands

SCS #: 91 -- HRC Dither Control

- Call SCS #: 87 -- HRC Scheduled/No Dither HRC-I HV Ramp Down Commands

- Call SCS #: 88 -- HRC Scheduled/No Dither HRC-S HV Ramp Down Commands

- Disable SCS #: 89 -- HRC Scheduled/Dither HRC-I HV Ramp Up Commands

- Disable SCS #: 90 -- HRC Scheduled/Dither HRC-S HV Ramp Up Commands

- Turn off A&B Shield HVPS and set levels to zero volts

- End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used for on-orbit SI Safing.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 89 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 90 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 91 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 87 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 88 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 89 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 90 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | 10 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | 12 | 2S1HVOF | SHIELD HVPS A OFF--TURNS OFF SHIELD HVPS A. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S1ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 13 | 13 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | 14 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 15 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | 2S2HVOF | SHIELD HVPS B OFF--TURNS OFF SHIELD HVPS B. BITS 19-26 ARE THE COMMAND NUMBER (05 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 TURNS OFF THE SUPPLY. |  | 2S2ONST | OFF |  |  |  |  | SI | SD |  |  |  |  |
| 17 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 18 | 18 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 18 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | 2S1STHV | SHIELD HVPS A STEP-- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S1HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 20 | 20 | 2S1STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 20 | 2S1STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT A BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 22 | 22 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 22 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 23 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | 2S2STHV | SHIELD HVPS B STEP-- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DONT CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. |  | 2S2HVST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 24 | 24 | 2S2STHV1 | Filler -- |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 24 | 2S2STHV2 | VOLTAGE STEPS -- SETS VOLTAGE ACROSS PMT B BLEEDER STRING. BITS 19-26 ARE THE COMMAND NUMBER (06 HEX), BIT 27 IS A DON'T CARE, AND BITS 28-34 SET THE VOLTAGE AT 16 VOLTS PER COUNT. EXAMPLES: 0600 HEX = 0 VOLTS, 0620H=48 VOLTS, 067FH=2032 VOLTS. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 25 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 26 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 80 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 105 -- HRC Safing Part 2, Door Partially Close

Description:

This SCS was created as part of the SI safing enhancement. This SCS is called by SCS #: 104 -- HRC Safing Part 1, which is originally called by SCS #: 107 -- Main SI Safing. This SCS is part 2 of a 2-part HRC safing response.

This SCS has been modified from the original version of the HRC Part 2 SCS. This version no longer opens the door all the way to the snubbers. This SCS now only partially closes the HRC door.

A summary of the patch request change is as follows:

All commanding associated with opening the door is eliminated

In the door "mostly" close commanding there are 3 changes (6 command changes):

1) Primary close limit switch changed from disable to enable

2) Number of step high-byte load changed to 35

3) Number of step low-byte load changed to 40

The net result of all the changes should be to move 9000 steps toward the closed limit switch from wherever it happens to be without first opening the door. With both the primary and secondary closed limit switches enabled we are protected from running hard against the closed position in the event of a single limit switch failure.

Main Steps in SCS:

Mostly close HRC door.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used for on-orbit SI safing

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | 2MCMRASL | MOTION CONTROL MODE RESET--PREVENTS MOTION CONTROL MODES 2MVPSAEX, 2MVLAAEX, 2MVLBAEX, 2NSTAAEX, AND 2NSTBAEX FROM BEING EXECUTED. BITS 19-26 ARE THE COMMAND NUMBER (6F HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MCMDARS | RSET |  |  |  |  | SI | SD |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | 2MCMRASL | MOTION CONTROL MODE RESET--PREVENTS MOTION CONTROL MODES 2MVPSAEX, 2MVLAAEX, 2MVLBAEX, 2NSTAAEX, AND 2NSTBAEX FROM BEING EXECUTED. BITS 19-26 ARE THE COMMAND NUMBER (6F HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MCMDARS | RSET |  |  |  |  | SI | SD |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | 2DRMTASL | DOOR MOTOR SELECT--SELECTS DOOR MOTOR FOR CONTROL. BITS 19-26 ARE THE COMMAND NUMBER (71 HEX), BITS 27-34 ARE DONT CARE. |  | 2DRMTAST | SEL |  |  |  |  | SI | SD |  |  |  |  |
| 7 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | 2DRMTASL | DOOR MOTOR SELECT--SELECTS DOOR MOTOR FOR CONTROL. BITS 19-26 ARE THE COMMAND NUMBER (71 HEX), BITS 27-34 ARE DONT CARE. |  | 2DRMTAST | SEL |  |  |  |  | SI | SD |  |  |  |  |
| 9 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | 2STFLADI | CLEAR STOP FLAGS-- CLEARS LATCHING INDICATORS FOR SECONDARY LIMIT SWITCHES. BITS 19-26 ARE THE COMMAND NUMBER (54 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2SFLGAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 11 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 12 | 2STFLADI | CLEAR STOP FLAGS-- CLEARS LATCHING INDICATORS FOR SECONDARY LIMIT SWITCHES. BITS 19-26 ARE THE COMMAND NUMBER (54 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2SFLGAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 13 | 13 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 13 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 14 | 2STFLAEN | ENABLE STOP FLAGS-- ENABLES LATCHING INDICATORS FOR SECONDARY LIMIT SWITCHES. BITS 19-26 ARE THE COMMAND NUMBER (54 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2SFLGAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 15 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 16 | 2STFLAEN | ENABLE STOP FLAGS-- ENABLES LATCHING INDICATORS FOR SECONDARY LIMIT SWITCHES. BITS 19-26 ARE THE COMMAND NUMBER (54 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2SFLGAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 17 | 17 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 17 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 18 | 2SMOIADI | SELECTED MTR OVERCURRENT PROTECTION DISABLE-- DISABLES MOTOR OVERCURRENT PROTECTION. BITS 19-26 ARE THE COMMAND NUMBER (49 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2DROIAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 19 | 19 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 19 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 20 | 2SMOIADI | SELECTED MTR OVERCURRENT PROTECTION DISABLE-- DISABLES MOTOR OVERCURRENT PROTECTION. BITS 19-26 ARE THE COMMAND NUMBER (49 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2DROIAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 21 | 21 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 21 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 22 | 2SMOTAEN | SELECTED MTR OVERTEMP PROTECTION ENABLE-- ENABLES MOTOR OVERTEMPERATURE PROTECTION. BITS 19-26 ARE THE COMMAND NUMBER (4A HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2DROTAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 23 | 23 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 23 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 24 | 2SMOTAEN | SELECTED MTR OVERTEMP PROTECTION ENABLE-- ENABLES MOTOR OVERTEMPERATURE PROTECTION. BITS 19-26 ARE THE COMMAND NUMBER (4A HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2DROTAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 25 | 25 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 25 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 26 | 2CHPLAEN | CLOSE / HOME PRI LIMIT SWITCH ENABLE-- ENABLES CLOS/HOME POSITION PRIMARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (50 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2CPLSAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 27 | 27 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 27 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 28 | 2CHPLAEN | CLOSE / HOME PRI LIMIT SWITCH ENABLE-- ENABLES CLOS/HOME POSITION PRIMARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (50 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2CPLSAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 29 | 29 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 29 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 30 | 2CHSLAEN | CLOSE / HOME SECONDARY LIMIT SWITCH ENABLE--ENABLES CLOS/HOME POSITION SECONDARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (51 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2CSLSAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 31 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 32 | 2CHSLAEN | CLOSE / HOME SECONDARY LIMIT SWITCH ENABLE--ENABLES CLOS/HOME POSITION SECONDARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (51 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2CSLSAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 33 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 33 | COSRTDLY | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 34 | 2OMPLADI | OPEN/MAX PRI LIMIT SWITCH DIS-- DISABLES OPEN/MAX POSITION PRIMARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (52 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2OPLSAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 35 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 36 | 2OMPLADI | OPEN/MAX PRI LIMIT SWITCH DIS-- DISABLES OPEN/MAX POSITION PRIMARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (52 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2OPLSAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 37 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 38 | 2OMSLADI | OPEN/MAX SECONDARY LIMIT SWITCH DISA-- DISABLES OPEN/MAX POSITION SECONDARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (53 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2OSLSAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 39 | 39 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 39 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 40 | 2OMSLADI | OPEN/MAX SECONDARY LIMIT SWITCH DISA-- DISABLES OPEN/MAX POSITION SECONDARY LIMIT SWITCH FOR SELECTED MOTOR. BITS 19-26 ARE THE COMMAND NUMBER (53 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2OSLSAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 41 | 41 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 41 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | 42 | 2MDRVAEN | MOTOR DRIVE ENABLE-- REMOVES POWER FROM SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MDRVAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 43 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | 44 | 2MDRVAEN | MOTOR DRIVE ENABLE-- REMOVES POWER FROM SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=1 SETS THIS MODE. |  | 2MDRVAST | ENAB |  |  |  |  | SI | SD |  |  |  |  |
| 45 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 46 | 46 | 2PSHBALD | MOT CTRL POS WORD HI BYTE LOAD-- SETS VALUE OF THE MOTOR CONTROL POSITION WORD HIGH BYTE. BITS 19-26 ARE THE COMMAND NUMBER (18 HEX), AND BITS 27-34 SET THE VALUE. |  | 2SCTHAST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 46 | 46 | 2PSHBAL1 | MOT CTRL POS WORD HI STEPS -- SETS VALUE OF THE MOTOR CONTROL POSITION WORD (NUMBER OF STEPS) HIGH BYTE. BITS 19-26 ARE THE COMMAND NUMBER (18 HEX), AND BITS 27-34 SET THE VALUE. | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 48 | 48 | 2PSHBALD | MOT CTRL POS WORD HI BYTE LOAD-- SETS VALUE OF THE MOTOR CONTROL POSITION WORD HIGH BYTE. BITS 19-26 ARE THE COMMAND NUMBER (18 HEX), AND BITS 27-34 SET THE VALUE. |  | 2SCTHAST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 48 | 48 | 2PSHBAL1 | MOT CTRL POS WORD HI STEPS -- SETS VALUE OF THE MOTOR CONTROL POSITION WORD (NUMBER OF STEPS) HIGH BYTE. BITS 19-26 ARE THE COMMAND NUMBER (18 HEX), AND BITS 27-34 SET THE VALUE. | 35 |  |  |  |  |  |  |  |  |  |  |  |  |
| 49 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 50 | 50 | 2PSLBALD | MOT CTRL POS WORD LO BYTE LOAD-- SETS VALUE OF THE MOTOR CONTROL POSITION WORD LOW BYTE. BITS 19-26 ARE THE COMMAND NUMBER (19 HEX), AND BITS 27-34 SET THE VALUE. |  | 2SCTHAST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 50 | 50 | 2PSLBAL1 | MOT CTRL POS WORD LO STEPS -- SETS VALUE OF THE MOTOR CONTROL POSITION WORD (NUMBER OF STEPS) LOW BYTE. BITS 19-26 ARE THE COMMAND NUMBER (19 HEX), AND BITS 27-34 SET THE VALUE. | 40 |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 52 | 52 | 2PSLBALD | MOT CTRL POS WORD LO BYTE LOAD-- SETS VALUE OF THE MOTOR CONTROL POSITION WORD LOW BYTE. BITS 19-26 ARE THE COMMAND NUMBER (19 HEX), AND BITS 27-34 SET THE VALUE. |  | 2SCTHAST | NONE |  |  |  |  | SI | SD |  |  |  |  |
| 52 | 52 | 2PSLBAL1 | MOT CTRL POS WORD LO STEPS -- SETS VALUE OF THE MOTOR CONTROL POSITION WORD (NUMBER OF STEPS) LOW BYTE. BITS 19-26 ARE THE COMMAND NUMBER (19 HEX), AND BITS 27-34 SET THE VALUE. | 40 |  |  |  |  |  |  |  |  |  |  |  |  |
| 53 | 53 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 53 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 54 | 54 | 2NSTAAEX | MOVE N STEPS TOWARD CLOSE/HOME LS -- THIS COMMAND IS INTENDED FOR USE IN STOWING THE DOOR AND SHUTTERS BEFORE LAUNCH BY DRIVING PAST THE PRIMARY LIMIT SWITCHES TO THE SECONDARY SWITCHES. ---------- MOVES TOWARD LIMIT SWITCH A (HOME) BY THE AMOUNT OF STEPS HELD IN THE POSITION COUNTER. |  | 2MCNAAMD | CMD |  |  |  |  | SI | SD |  |  |  |  |
| 55 | 55 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 55 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 56 | 56 | 2NSTAAEX | MOVE N STEPS TOWARD CLOSE/HOME LS -- THIS COMMAND IS INTENDED FOR USE IN STOWING THE DOOR AND SHUTTERS BEFORE LAUNCH BY DRIVING PAST THE PRIMARY LIMIT SWITCHES TO THE SECONDARY SWITCHES. ---------- MOVES TOWARD LIMIT SWITCH A (HOME) BY THE AMOUNT OF STEPS HELD IN THE POSITION COUNTER. |  | 2MCNAAMD | CMD |  |  |  |  | SI | SD |  |  |  |  |
| 57 | 57 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 57 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1920 |  |  |  |  |  |  |  |  |  |  |  |  |
| 58 | 58 | 2MDRVADI | MOTOR DRIVE DISABLE-- APPLIES POWER TO SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2MDRVAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 59 | 59 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 59 | 59 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 60 | 60 | 2MDRVADI | MOTOR DRIVE DISABLE-- APPLIES POWER TO SELECTED MOTOR CIRCUIT. BITS 19-26 ARE THE COMMAND NUMBER (68 HEX), BITS 27-33 ARE DONT CARE, AND BIT 34=0 SETS THIS MODE. |  | 2MDRVAST | DISA |  |  |  |  | SI | SD |  |  |  |  |
| 61 | 61 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 61 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 62 | 62 | 2ALMTADS | ALL MOTORS DESELECT--DESELECTS ALL MOTORS. BITS 19-26 ARE THE COMMAND NUMBER (70 HEX), BITS 27-34 ARE DONT CARE. |  | 2ALMTAST | NSEL |  |  |  |  | SI | SD |  |  |  |  |
| 63 | 63 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 63 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 64 | 64 | 2ALMTADS | ALL MOTORS DESELECT--DESELECTS ALL MOTORS. BITS 19-26 ARE THE COMMAND NUMBER (70 HEX), BITS 27-34 ARE DONT CARE. |  | 2ALMTAST | NSEL |  |  |  |  | SI | SD |  |  |  |  |
| 65 | 65 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 65 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 66 | 66 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 106 – ACIS Safing

Description:

This SCS was created as part of the SI safing enhancement. This SCS is called by SCS #: 107 -- Main SI Safing.

This patch was not created using the SCS tool, since it utilized ACIS command packets. These packets are supplied by the CXC, and are not resident in the Command Data Base.

Main Steps in SCS:

AA00000000, Stop Science

1 Second Delay

AA00000000, Stop Science

10 Second Delay

WSPOW00000, Power down Video Boards and FEPs

20 Second Delay

RS_0000001, Dump System Configuration

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

SCS in hex format:

| Step | Command Hex | Command Description |
| --- | --- | --- |
| 1 | D800003 | ACIS Command Packet |
| 2 | 3060 | ACIS Command Packet |
| 3 | 3001300 | ACIS Command Packet |
| 4 | 9800010 | COSRTDLY, COSRTDLY=16 |
| 5 | D800003 | ACIS Command Packet |
| 6 | 3060 | ACIS Command Packet |
| 7 | 3001300 | ACIS Command Packet |
| 8 | 98000A0 | COSRTDLY, COSRTDLY=160 |
| 9 | D800007 | ACIS Command Packet |
| 10 | 7030 | ACIS Command Packet |
| 11 | 5002000 | ACIS Command Packet |
| 12 | 0 | ACIS Command Packet |
| 13 | 10000 | ACIS Command Packet |
| 14 | 9800140 | COSRTDLY, COSRTDLY=320 |
| 15 | D800003 | ACIS Command Packet |
| 16 | 3004 | ACIS Command Packet |
| 17 | 2002100 | ACIS Command Packet |
| 18 | C800000 | OBC_END_SCS |

# SCS #: 107 -- Main SI Safing

Description:

SCS 107 is the Main SI Safing SCS. It was created to replace the set of safing actions that were in place at launch and through OAC. Early in the mission it was discovered that the radiation belts were having a deleterious affect on the ACIS instrument, specifically the FI chips. It was found that moving the ACIS instrument out of the HRMA FOV, into the Next In Line location, stopped the degradation to the FI chips. The next step was to change the on-board safing actions to make sure the ACIS was removed to the NIL position. Additional changes were also made to consolidate all the safing actions into one main SCS.

Refer to Table 4 Safe Modes Summary Flow Chart

Main Steps in SCS:

- Disable Radmon Process

- Call SCS #: 123 -- Terminate and Disable Observing SCSs 131 - 135

- Disable Angular Momentum Unloading Logic (Subfunction 21)

- Disable VDE A&B MUPS Hi-Side Valve Power

- Disable S/C Momentum Monitor Safing Action (SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action)

- Disable RW Momentum Bias

- Activate SCS #: 82 -- OTG Emergency Halt, OTG Retraction

- Call SCS #: 108 – SIM Move to HRC-S

- Call SCS #: 106 – ACIS Safing

- Call SCS #: 104 -- HRC Safing Part 1 (+ SCS #: 105 -- HRC Safing Part 2, Door Partially Close)

- 432-Second Time Delay.  This was originally included in the SCS to allow time for the OTGs to Retract, but this is no longer done since SCS 82 has been modified to halt OTG motion.  Now this time delay is intended to give the SIM TSC enough time to move before enabling the momentum monitor safing action.  The longest move takes about 300 seconds.  This time delay provides adequate pad time for commands to be issued by the SEA and for overcurrents that could slow TSC moves.

- Enable Angular Momentum Unloading Logic (Subfunction 21)

- Enable S/C Momentum Monitor Safing Action (SCS 9)

- Enable RW Momentum Bias

- Activate SCS #: 84 – Command Normal Sun Mode

- Disable SCS 107

- Turn off FID lights

Timing of SCS 107 Actions:

| Description of Action | Timing (~sec) |
| --- | --- |
| Disable Radmon Process | 1.025 |
| Call SCS 123 (Disable SCSs 131 to 135) |  |
| Disable Angular Momentum Unloading Logic (Subfunction 21) |  |
| Disable VDE A&B MUPS Hi-Side Valve Power |  |
| Disable S/C Momentum Monitor Safing Action (SCS #: 9 -- OO - Spacecraft Momentum Monitor Fault Safing Action) |  |
| Disable RW Momentum Bias |  |
| Activate SCS #: 82 – Halt OTG motion |  |
| Call SCS #: 108 - SIM Move to HRC-S | 0 (All 16 seconds run in parallel with step 8) |
| Call SCS #: 106 - ACIS Safing | 65.66 |
| Stop Science (AA00000000) |  |
| 1 second delay | - |
| Stop Science (AA00000000) | 1.025 |
| 10 Second Delay | - |
| Power down video boards and FEPs (WSPOW00000) | 10.25 |
| 20 Second Delay | - |
| Dump System Config (RS_0000001) | 20.5 |
| Call SCS #: 104 -- HRC Safing Part 1 | - |
| Terminate SCSs 89, 90, and 91 |  |
| Call SCS 87 – Ramp down HRC-I HV | - |
| SCS 104 Delay | 9.29 |
| Call SCS 88 – Ramp down HRC-S HV | 1.025 |
| Disable SCSs 89, 90 | 10.25 |
| 1 second delay | - |
| SCS 104 – Safe HRC | 1.025 |
| 7-Minute Time Delay to allow the SIM to move to HRC-S before re-enabling the Momentum Monitor | 13.325 |
| Enable Angular Momentum Unloading Logic (Subfunction 21) | 432 (6744 mc) |
| Enable S/C Momentum Monitor Safing Action (SCS 9) | - |
| Enable RW Momentum Bias |  |
| Activate SCS 84 |  |
| Disable SCS 107 |  |
| FLCA Configuration Reset (turn off all FID lights) |  |
| TOTAL TIME |  |
|  | 565 (9.42 minutes) |

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in all phases.

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OORMPDS | RADIATION MONITOR PROCESS DISABLE |  | CORADMEN | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 123 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSD | PCAD_Subfunction | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-5 | 4 | AVAMPOOF | VDE-A VLV PWR SWITCHING CMDS, PBO, MUPS PWR OFF (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB1 | AVAMPOOF Data Bits D13 to D0 of Data Field -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB3 | AVAMPOOF Least Significant Word and First Command Word -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB4 | AVAMPOOF Filler bit -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB5 | AVAMPOOF Address Part of Data Field -- Address part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB6 | AVAMPOOF Channel Part of Data Field -- Channel part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB7 | AVAMPOOF Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB8 | AVAMPOOF Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOOF | VDE-B VLV PWR SWITCHING CMDS, PBO, MUPS PWR OFF (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH1 | AVBMPOOF Data Bits D13 to D0 of Data Field -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH3 | AVBMPOOF Least Significant Word and First Command Word -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH4 | AVBMPOOF Filler bit -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH5 | AVBMPOOF Address Part of Data Field -- Address part of the data field |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH6 | AVBMPOOF Channel Part of Data Field -- Channel part of the data field |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH7 | AVBMPOOF Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 5 | AVBMPOH8 | AVBMPOOF Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 8 | 6 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 6 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-10 | 7 | AVAMPOOF | VDE-A VLV PWR SWITCHING CMDS, PBO, MUPS PWR OFF (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB1 | AVAMPOOF Data Bits D13 to D0 of Data Field -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB3 | AVAMPOOF Least Significant Word and First Command Word -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB4 | AVAMPOOF Filler bit -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB5 | AVAMPOOF Address Part of Data Field -- Address part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB6 | AVAMPOOF Channel Part of Data Field -- Channel part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB7 | AVAMPOOF Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 7 | AVAMPOB8 | AVAMPOOF Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOOF | VDE-B VLV PWR SWITCHING CMDS, PBO, MUPS PWR OFF (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH1 | AVBMPOOF Data Bits D13 to D0 of Data Field -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 0 | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH3 | AVBMPOOF Least Significant Word and First Command Word -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH4 | AVBMPOOF Filler bit -- |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH5 | AVBMPOOF Address Part of Data Field -- Address part of the data field |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH6 | AVBMPOOF Channel Part of Data Field -- Channel part of the data field |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH7 | AVBMPOOF Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 11-12 | 8 | AVBMPOH8 | AVBMPOOF Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVBMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 13 | 9 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 9 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 9 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 10 | AORWMOMD | DISABLE RW MOMENTUM BIAS |  | AORWBIAS | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 11 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 11 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 82 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 11 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 12 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 12 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 108 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 13 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 13 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 106 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 14 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 14 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 104 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 15 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 15 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 6744 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 16 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 16 | AOPCADSE | PCAD Subfunction for EN | 21 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 17 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 17 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 18 | AORWMOME | ENABLE RW MOMENTUM BIAS |  | AORWBIAS | ENAB |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 19 | COACTSX | ACTIVATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 19 | COACTS1 | COACTSX - SCS NUMBER -- SCS Number | 84 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 19 | COACTS2 | COACTSX - REPEAT COUNT -- Repeat Count. If this is 0, then SCS is executed once. | 0 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 20 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 20 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 107 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 21 | AFLCRSET | FLCA Configuration Reset (turn off all FID lights) |  |  |  |  |  |  |  | SI | S |  |  |  |  |
| 26 | 22 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 108 – SIM Move to HRC-S

Description:

This SCS is used to move the SIM translation table to place HRC-S in the HRMA FOV, and move the ACIS into the NIL (Next in Line) position. This is used to “safe” ACIS from the deleterious effects of the radiation belts.

This SCS is identical to SCS #: 81 -- SIM Move to Safe Position, the original SIM move to the safe (midpoint) position, except for the absolute location.

Main Steps in SCS:

SIMGOTO serial digital command with parameter value (translation coordinate) –99612 steps, absolute position. To use this position, divide by 8 then encode to binary. Note Mod 215 since only 15 bits are used for the position.

End SCS command.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

The SCS is called by SCS #: 107 -- Main SI Safing

Constraints:

The SIM SEA that is ON will respond to the command (e.g. no A or B side command sequences required)

All commands require the SIM SEA serial digital header properly filled out.

Two commands minimum - header command and data command.

The SIMGOTO commands are doubled-up to protect against SEU upset. The commands are separated by 1024 minor cycles (65.6 seconds, or two major frames) because of SIM sync requirements.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 1 | 1 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 129 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 1 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 2 | 3TSCMBEN | SIM TSC MOTOR ENABLE--The TSC Motor Enable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply power to either motor in response to this command, only to the motor driver. The Goto Position command powers on the motor. The TSC Motor Enable command must be issued to select a motor and apply power to the motor driver prior to issuing the Goto Position command. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. |  | 3SMOTPEN | ON | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 3 | 3 | 3TSCGOTO | SIM GO TO POSITION--The SIM Go To Position command causes the SEA software to initiate movement of one of the drive motors. This command will have no effect unless power has already been applied to the motor driver by a previous Motor Enable command. The SEA software will hold off execution of this command until any motor motion already in progress is completed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | 3TSCGOTO | SIM GOTO Mechanism Position Value -- This field is a signed 15 bit integer used to specify a mechanism position relative to the origin. For the TSC, one LSB equals 160 degrees of motor rotation. | 20316 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 4 | 3TSCMBDS | SIM TSC MOTOR DISABLE--The TSC Motor Disable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply or disconnect power to either motor in response to this command, only to the motor driver. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. Therefore, it cannot be used to stop a motion in progress. The Motor Stop command is used for that purpose. |  | 3SMOTPEN | OFF | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1024 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | 3SIMHD | SIM SEA SERIAL COMMAND HEADER--The SEA will only accept commands in groups or packets preceeded by this SEA Header command. The SEA Header command is the first command in a group or packet sent to the SEA. The SEA Header command contains an 8 bit checksum which is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group or packet, including the two bytes of the Header command, is zero. The Header command also contains field to specify the number of 16 bit command in the group or packet that follow the Header. The maximum number of commands that may be sent in one group, following the header, is 63. The SEA will not execute any command in a group until the entire group has been received and verified to be correct. An error in the checksum, word count, or an illegal value for any individual command will cause the SEA to reject the entire command group or packet and set the invalid command flag in output telemetry. |  |  |  |  |  |  |  | SI | SD |  |  |  |  |
| 6 | 6 | 3SIMHD1 | SIM SEA Header Checksum -- This field is used to specify an 8 bit checksum of all command bytes within a command group transmitted to the SIM. The checksum is computed such that the low order 8 bits of the sum of all 8 bit bytes in the command group, including the header word, is zero. | 129 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | 3SIMHD2 | SIM SEA Header Fill -- Fill bits, set to binary (00). |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | 6 | 3SIMHD3 | SIM SEA Header No of Commands -- This field is used to specify the number of 16 bit commands in a command group that follow the header. The maximum number of 16 bit commands in a command group is limited to 63. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | 7 | 3TSCMBEN | SIM TSC MOTOR ENABLE--The TSC Motor Enable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply power to either motor in response to this command, only to the motor driver. The Goto Position command powers on the motor. The TSC Motor Enable command must be issued to select a motor and apply power to the motor driver prior to issuing the Goto Position command. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. |  | 3SMOTPEN | ON | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 8 | 8 | 3TSCGOTO | SIM GO TO POSITION--The SIM Go To Position command causes the SEA software to initiate movement of one of the drive motors. This command will have no effect unless power has already been applied to the motor driver by a previous Motor Enable command. The SEA software willhold off execution of this command until any motor motion already in progress is completed. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | 8 | 3TSCGOTO | SIM GOTO Mechanism Position Value -- This field is a signed 15 bit integer used to specify a mechanism position relative to the origin. For the TSC, one LSB equals 160 degrees of motor rotation. | 20316 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 3TSCMBDS | SIM TSC MOTOR DISABLE--The TSC Motor Disable command causes the SEA software to operate latching relays that control which motor is to be driven, and that control the application of power to the motor driver. The SEA software will not apply or disconnect power to either motor in response to this command, only to the motor driver. Execution of this command will be held off by the SEA software until any motor motion already in progress is completed. Therefore, it cannot be used to stop a motion in progress. The Motor Stop command is used for that purpose. |  | 3SMOTPEN | OFF | 3SMOTSEL | TSC |  |  | SI | SD |  |  |  |  |
| 10 | 10 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 109 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 110 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 111 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 112 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 113 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 114 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 115 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 116 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 117 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 118 -- OBC Reset Reconfiguration Tasks

Description:

This SCS is called by SCS 80 upon an OBC reset in order to activate the proper PCAD control mode function and MUPS momentum control.  In addition, important safing SCSs that default to disabled after an OBC reset are enabled and selected heater functions are enabled.  It calls SCS 37 in order to enter Normal Sun Mode.

Main Steps in SCS:

- Enable kinematic integration process

- Enable MUPS momentum control

- Enable MUPS valve power

- Delay 1 minute, then set PCAD to normal sun mode 1st entry, Call to SCS #: 37 -- OO - Normal Sun Mode First Entry

- Enable safing SCS’s and safe mode monitors (SCS’s 6-9, 11-14, 23-27, 29, 30)

- Enable heater systems (ox tank, fuel tank, FA6 SIM abort, SIM trim heaters)

- Enable SCS 32 (fault load shed) & SCS 33 (power recovery)

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This is used in all phases.  It is called by SCS #: 80 -- OO - Standby State Timeout.

Constraints:

All hardware commands contain 64 ms command spacing and are doubled up with 1.025 s spacing between sets to overcome SEU’s.

No time delays were inserted between OBC commands (i.e. commands with 2nd character = “O”)

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COOFPNM | NORMAL OFP STATE SELECT |  | CONLOFP | NRML |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | AOPCADSE | PCAD Subfunction for EN | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | AOMUPSEL | SELECT THRUSTERS MUPS |  | AOFTHRST | MUPS |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6-7 | 6 | AVAMPOON | VDE-A VLV PWR SWITCHING CMDS, PBO, MUPS PWR ON (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB1 | AVAMPOON Data Bits D13 to D0 of Data Field -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB3 | AVAMPOON Least Significant Word and First Command Word -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB4 | AVAMPOON Filler bit -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB5 | AVAMPOON Address Part of Data Field -- Address part of the data field |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB6 | AVAMPOON Channel Part of Data Field -- Channel part of the data field |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB7 | AVAMPOON Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 6-7 | 6 | AVAMPOB8 | AVAMPOON Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 8 | 7 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 7 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-10 | 8 | AVAMPOON | VDE-A VLV PWR SWITCHING CMDS, PBO, MUPS PWR ON (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB1 | AVAMPOON Data Bits D13 to D0 of Data Field -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB3 | AVAMPOON Least Significant Word and First Command Word -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB4 | AVAMPOON Filler bit -- |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB5 | AVAMPOON Address Part of Data Field -- Address part of the data field |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB6 | AVAMPOON Channel Part of Data Field -- Channel part of the data field |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB7 | AVAMPOON Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 9-10 | 8 | AVAMPOB8 | AVAMPOON Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVAMPWR | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 11 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 937 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 10 | COSCALL | SCS CALL SCS |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 12 | 10 | COSCALL1 | COSCALL - SCS NUMBER -- SCS Number | 37 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 13 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 12 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 14 | 12 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 | 13 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 13 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 7 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 | 14 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 14 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | 15 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 15 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 | 16 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 16 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 | 17 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 19 | 17 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 12 |  |  |  |  |  |  |  |  |  |  |  |  |
| 20 | 18 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 20 | 18 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 21 | 19 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 21 | 19 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 14 |  |  |  |  |  |  |  |  |  |  |  |  |
| 22 | 20 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 22 | 20 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 23 |  |  |  |  |  |  |  |  |  |  |  |  |
| 23 | 21 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 23 | 21 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 24 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | 22 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 24 | 22 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 25 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 | 23 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 25 | 23 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 26 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 | 24 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 26 | 24 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 27 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 | 25 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 27 | 25 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 | 26 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 28 | 26 | COENAS1 | COENASX - SCS NUMBER -- SCS Number | 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 | 27 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 29 | 27 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 30 | 28 | ASMMONEN | CPE ENABLE SAFE MODE STATUS MONITOR--IOC Command, Serial interface |  | AIOESWD3 | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 31 | 29 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 31 | 29 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 32 | 30 | ASMMONEN | CPE ENABLE SAFE MODE STATUS MONITOR--IOC Command, Serial interface |  | AIOESWD3 | ENAB |  |  |  |  | PC | SD |  |  |  |  |
| 33 | 31 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 33 | 31 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 34 | 32 | PTOXHPEN | OX TANK HTR PRI ENAB |  | PXTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 35 | 33 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 35 | 33 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 36 | 34 | PTOXHREN | OX TANK HTR RDNT ENAB |  | PXTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 37 | 35 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 37 | 35 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 38 | 36 | PFTPHEN | FUEL TANK HTR PRI ENAB |  | EFTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 39 | 37 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 39 | 37 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 40 | 38 | PFTRHEN | FUEL TANK HTR RDNT ENAB |  | EFTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 41 | 39 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 41 | 39 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 42 | 40 | 3FA6PAEN | FOCUS ASSEMBLY 6 PRIME ABORT HEATER ENABLE |  | 3AZF6HTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 43 | 41 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 43 | 41 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 44 | 42 | 3SPYPTEN | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER ENABLE |  | 3ASPYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 45 | 43 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 45 | 43 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 46 | 44 | 3SMYPTEN | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER ENABLE |  | 3ASMYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 47 | 45 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 47 | 45 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 48 | 46 | 3PSMPTEN | PSMC PRIME TRIM HEATER ENABLE |  | 3APSMTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 49 | 47 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 49 | 47 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 50 | 48 | 3FLCPTEN | FLCA PRIME TRIM HEATER ENABLE |  | 3FLCTHTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 51 | 49 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 51 | 49 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 52 | 50 | 3RCTPTEN | RCTU PRIME TRIM HEATER ENABLE |  | 3SITHTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 53 | 51 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 53 | 51 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 54 | 52 | 3AC1PTEN | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3A1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 55 | 53 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 55 | 53 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 56 | 54 | 3AC2PTEN | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3A2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 57 | 55 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 57 | 55 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 58 | 56 | 3AC3PTEN | ACIS 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3A3THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 59 | 57 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 59 | 57 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 60 | 58 | 3HR1PTEN | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3H1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 61 | 59 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 61 | 59 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 62 | 60 | 3HR2PTEN | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3H2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 63 | 61 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 63 | 61 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 64 | 62 | 3HR3PTEN | HRC 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3H3PZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 65 | 63 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 65 | 63 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 16 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 66 | 64 | PTOXHPEN | OX TANK HTR PRI ENAB |  | PXTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 67 | 65 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 67 | 65 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 68 | 66 | PTOXHREN | OX TANK HTR RDNT ENAB |  | PXTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 69 | 67 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 69 | 67 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 70 | 68 | PFTPHEN | FUEL TANK HTR PRI ENAB |  | EFTHTRPR | ENAB |  |  |  |  | LR | HLP |  |  |  |  |
| 71 | 69 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 71 | 69 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 72 | 70 | PFTRHEN | FUEL TANK HTR RDNT ENAB |  | EFTHTRRD | ENAB |  |  |  |  | EP | HLP |  |  |  |  |
| 73 | 71 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 73 | 71 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 74 | 72 | 3FA6PAEN | FOCUS ASSEMBLY 6 PRIME ABORT HEATER ENABLE |  | 3AZF6HTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 75 | 73 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 75 | 73 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 76 | 74 | 3SPYPTEN | ACIS SUPPORT STRUCTURE +Y PRIME TRIM HEATER ENABLE |  | 3ASPYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 77 | 75 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 77 | 75 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 78 | 76 | 3SMYPTEN | ACIS SUPPORT STRUCTURE -Y PRIME TRIM HEATER ENABLE |  | 3ASMYTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 79 | 77 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 79 | 77 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 80 | 78 | 3PSMPTEN | PSMC PRIME TRIM HEATER ENABLE |  | 3APSMTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 81 | 79 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 81 | 79 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 82 | 80 | 3FLCPTEN | FLCA PRIME TRIM HEATER ENABLE |  | 3FLCTHTA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 83 | 81 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 83 | 81 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 84 | 82 | 3RCTPTEN | RCTU PRIME TRIM HEATER ENABLE |  | 3SITHTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 85 | 83 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 85 | 83 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 86 | 84 | 3AC1PTEN | ACIS 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3A1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 87 | 85 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 87 | 85 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 88 | 86 | 3AC2PTEN | ACIS 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3A2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 89 | 87 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 89 | 87 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 90 | 88 | 3AC3PTEN | ACIS 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3A3THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 91 | 89 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 91 | 89 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 92 | 90 | 3HR1PTEN | HRC 1 FITTING -Y,-Z PRIME TRIM HEATER ENABLE |  | 3H1THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 93 | 91 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 93 | 91 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 94 | 92 | 3HR2PTEN | HRC 2 FITTING +Y,-Z PRIME TRIM HEATER ENABLE |  | 3H2THTRA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 95 | 93 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 95 | 93 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 96 | 94 | 3HR3PTEN | HRC 3 FITTING +Z PRIME TRIM HEATER ENABLE |  | 3H3PZTHA | ENAB |  |  |  |  | SI | LCC |  |  |  |  |
| 97 | 95 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 97 | 95 | COENAS1 | COENASX – SCS NUMBER -- SCS Number | 32 |  |  |  |  |  |  |  |  |  |  |  |  |
| 98 | 96 | COENASX | ENABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 98 | 96 | COENAS1 | COENASX – SCS NUMBER -- SCS Number | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 99 | 97 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 119 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 120 – Momentum Unload Cutoff Monitor

Description:

This SCS provides a means to limit the duration of a momentum unload that could possibly be overextended from anomalous thruster behavior.  It is intended that this SCS be activated with a repeat count of 255 for continuous execution of the SCS.

Main Steps in SCS:

1.  If no unload is detected at the beginning of this SCS (i.e., F_Unload_State, which is event number 33 in the OFP Event Table, equals MONITOR), the SCS drops down to the 8 second delay step

2.  If a momentum unload is detected (F_Unload_State equals GROUND or AUTO), there is a 400 second (6240 minor cycles) wait period to allow an unload to complete before the subsequent commands are executed to stop any unload from continuing.  The 400 second value is based on the worst-case time estimate to execute an autounload from the trip threshold of 40 ft-lb-sec.

a.  The cutoff sequence consists of the following:

- Disable the PCAD angular momentum unloading subfunction (number 21)

- Disable the Valve Drive Electronics (VDE) A MUPS valve power

- Disable the VDE-A thruster monitor

- Set the momentum unloading state to monitor

- Set the desired angular momentum to zero

b.  After the cutoff actions are complete, an additional delay of one hour (56224 minor cycles) is initiated to prevent ‘back to back’ momentum unloads which would be thermally unfavorable to the MUPS thruster valves.  After this delay, the angular momentum unloading sub-function is re-enabled.  The SCS then drops down to the 8 second delay step.

3.  Delay for 8 seconds (127 minor cycles) and end the check for, and response to, an active momentum unload event.  If the SCS was activated with a repeat count of 255, SCS execution will loop back to the start of the SCS.  This 8 second delay serves to control the number of times the monitor will run in a major frame.

Figure SCS 120-1.  Momentum Unload Cutoff Monitor

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used during the On-Orbit Phase.  A patch may be required for this SCS if VDE-B becomes the primary unit.

Constraints:

This SCS defaults to disabled upon OBC reset, and is enabled and activated by ground command in preparation for resuming mission activities.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | OCNDEVBR | CONDITIONAL EVENT BRANCH |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB1 | OCCURRENCE FLAG -- 0 - EVENT FAILED TO OCCUR 1 - EVENT OCCURED | 1 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB2 | OCNDEVB1 EV NUMBER -- CONDITIONAL EVENT NUMBER BEING INTERROGATED. | 33 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | OCNDEVB3 | OCNDEVBR SCS STEP -- SCS STEP NUMBER AT WHICH THE PROCESSING WILL CONTINUE | 17 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 6240 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOFUNCDS | PCAD SUBFUNCTION DISABLE |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | AOPCADSD | PCAD_Subfunction – See DM05 | 21 | AOPSAMUL | DISA |  |  |  |  | NA | NA |  |  |  |  |
| 4-5 | 4 | AVAMPOOF | VDE-A VLV PWR SWITCHING CMDS, PBO, MUPS PWR OFF (OBC)--CONTROL COMMAND SERIAL INTERFACE (OBC) |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB1 | AVAMPOOF Data Bits D13 to D0 of Data Field -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB2 | Q Odd Parity -- CPE parity bit over ground bits 19-34 of the command. | 1 | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB3 | AVAMPOOF Least Significant Word and First Command Word -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB4 | AVAMPOOF Filler bit -- |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB5 | AVAMPOOF Address Part of Data Field -- Address part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB6 | AVAMPOOF Channel Part of Data Field -- Channel part of the data field |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB7 | AVAMPOOF Data Bits D15 and D14 -- Data Bits 15 and 14 of second command word |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 4-5 | 4 | AVAMPOB8 | AVAMPOOF Most Significant Word and Second Word of two word command -- Most Significant word of two word command |  | AOVAMPWR | DISA |  |  |  |  | PC | SD |  |  |  |  |
| 6 | 5 | AVTA1DS | VDE-A Thruster Monitor Disabled (Channel 0) |  | PVDETMA1 | DISA | PVDETMA2 | DISA |  |  | EP | SD |  |  |  |  |
| 7 | 6 | AVTA2DS | VDE-A Thruster Monitor Disabled (Channel 1) |  | PVDETMA2 | DISA | PVDETMA1 | DISA |  |  | EP | SD |  |  |  |  |
| 8 | 7 | AOMUNLMO | OBC SET ANGULAR MOMENTUM UNLOADING STATE MONITOR |  | AOUNLOAD | MON |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMOS | SET DESIRED SPACECRAFT ANGULAR MOMENTUM (Stored)--There are Real and Stored Versions of this command |  | AOSYMOM1 |  | AOSYMOM2 |  | AOSYMOM3 |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMS1 | Set Desired System Angular Momentum Command 1 -- 1st command of a multipart command |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMS2 | Set Desired System Angular Momentum Command 2 -- 2nd command of a multipart command |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMS3 | Mom_Tot_Cmd(1) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMS4 | Mom_Tot_Cmd(2) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9-14 | 8 | AODESMS5 | Mom_Tot_Cmd(3) -- Desired system Momentum vector | 0.0 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 9 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 15 | 9 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 56224 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 10 | AOFUNCEN | PCAD SUBFUNCTION ENABLE / REINIT |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 16 | 10 | AOPCADSE | PCAD Subfunction for EN -- PCAD Subfunction Number. See DMO5 | 21 | AOPSAMUL | ACT |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 11 | COSRTDLY | SCS RELATIVE TIME DELAY |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 17 | 11 | COSRTDL1 | Relative Time Delay (SCS Only) -- Relative Time Delay (minor cycles) | 127 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 18 | 12 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 121 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 122 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 123 -- Terminate and Disable Observing SCSs 131 - 135

Description:

This SCS terminates and disables all observation SCSs (131 – 133) plus 134 and 135, which are reserved for possible Science Instrument use.  SCS 123 is called from SCS #: 107 -- Main SI Safing

Main Steps in SCS:

- Terminate SCS 131.

- Terminate SCS 132.

- Terminate SCS 133.

- Terminate SCS 134.

- Terminate SCS 135.

- Disable SCS 131.

- Disable SCS 132.

- Disable SCS 133.

- Disable SCS 134.

- Disable SCS 135.

What Phase is this SCS used in? What Patches are Required for Normal Operations?

This SCS is used in all phases.  No patches are required for Normal Operations.

Constraints:

None.

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 1 | 1 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 131 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 2 | 2 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 132 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 3 | 3 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 133 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 4 | 4 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 134 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COTERMSX | TERMINATE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 5 | 5 | COTERMS1 | COTERMSX - SCS NUMBER -- SCS Number | 135 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 6 | 6 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 131 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 7 | 7 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 132 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 8 | 8 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 133 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 9 | 9 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 134 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | CODISASX | DISABLE SCS# |  |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 10 | 10 | CODISAS1 | CODISASX - SCS NUMBER -- SCS Number | 135 |  |  |  |  |  |  | NA | NA |  |  |  |  |
| 11 | 11 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 124 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 125 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 126 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |

# SCS #: 127 -- Spare SCS

Description:

This SCS is not used.

Main Steps in SCS:

End SCS command

What Phase is this SCS used in? What Patches are Required for Normal Operations?

Constraints:

None

| Step | Count | Mnemonic | Command Description | Par | Cmd Ver 1 | State 1 | Cmd Ver 2 | State 2 | Cmd Ver 3 | State 3 | RCTU | Ch | V | H | Per | Relay |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | COSCSEND | END SCS (SCS ONLY) |  |  |  |  |  |  |  | NA | NA |  |  |  |  |