| PARTICIPANTS: | OC/CC |
| --- | --- |
| OVERVIEW: | This procedure describes the real-time actions to be taken by the OC in the event that ACIS has not been safed in a high radiation environment. |
| SUMMARY: | Determine if unexpected SIM position may be due to serious hardware failure. If so, run SCS 107 without moving the SIM. If not, run SCS 107 completely. |
| CONSTRAINTS: | N/A |
| INITIAL CONDITIONS: | SIM TT position > -25,000 and spacecraft is in the radiation zone as listed in Backstop Report State by Comm. |
| EHS DISPLAYS: | F_ MAIN, M_SIMTABLE, F_SCS_107 |
| GRETA DISPLAYS: | F_MAIN, EHS_M_SIMTABLE, F_SCS107 |
| COMPS: | None |
| SCRIPTS: | O_SCSCTRL |
| PROCEDURES: | N/A |
| COMMAND LOADS | LOAD NAME | CHECKSUM, if SCS |
|  | N/A | N/A |
| DISABLED COMMANDS: | N/A |
| COMMAND SYSTEM: |  |
|  | Clear To Send Mechanism | = TIME |
|  | CAR Processing | = Enabled |
|  | FSV Processing | = Disabled |
|  | Output Format | = NRZM |
|  | Minimum Time Delay (sec) | = 3 |
|  | CAR Time-out (sec) | = 40 |
|  | FSV Time-out (sec) | = 45 |
|  | Blocking Factor | = 90 |

flowchart:

DECLARE S/C EMERGENCY

OC - Work with Ops Chief to extend comm by 2-3 hours, and declare a S/C Emergency.

OC CALL SYSTEMS, MECHANISMS, AND ACIS ENGINEERS, FD AND SOT LEAD

OC - Contact SYSTEMS, MECHANISMS, and ACIS Engineers, FD, FOM, and SOT Lead.  Inform them that ACIS is unsafe, and that this SOP is being executed.

RECORD SIM TT AND FA POSITIONS

OC - Record SIM TT and FA positions.

| MSID | DESCRIPTION | DISPLAY | VALUE |
| --- | --- | --- | --- |
| 3TSCPOS | SIM TT Position | M_SIMTABLE.dsp |  |
| 3FAPOS | SIM FA Position | M_SIMTABLE.dsp |  |

RUN SCS 107

There are failure modes of the SIM which make an unconsidered SIM translation potentially dangerous.  If the values of BOTH of the following MSIDs are > 0, disable SCSs 81 and 108 before activating SCS 107. Otherwise, Activate SCS 107.

| MSID | DESCRIPTION | EXPECTED VALUE | DISPLAY | ACTUAL VALUE |
| --- | --- | --- | --- | --- |
| 3SMOTSTL | SIM TT Stall Counter | 0 | M_SIMTABLE.dsp |  |
| 3SMOTOC | SIM Over Current Counter | 0 | M_SIMTABLE.dsp |  |

If BOTH of these MSIDs are non-zero, go to step 4.a, then 4.b.  Otherwise, go directly to 4.b.

Please refer to the flowchart at the beginning of the procedure.

  - DISABLE SCSs 81 AND 108

****------------------------------------------------------  CAUTION  -----------------------------------------------------------****

EXECUTE THIS STEP (4.a) ONLY IF BOTH 3SMOTSTL AND 3SMOTOC ARE NON-ZERO

****----------------------------------------------------------------------------------------------------------------------------------****

OC - Using script O_PROT_SCSCTRL, DISABLE SCSs 81 and 108.

****---------------------------------------------------------- NOTE --------------------------------------------------------------****

#### EXECUTE THIS STEP (4.b) IN ALL CASES

****---------------------------------------------------------------------------------------------------------------------------------****

  - ACTIVATE SCS 107

OC - Using script O_PROT_SCSCTRL, ACTIVATE SCS 107, if SCS 107 is currently disabled, ENABLE and ACTIVATE SCS 107.

| MSID VALUE | DESCRIPTION | EXPECTED VALUE | ACTUAL VALUE | Time of Verification |
| --- | --- | --- | --- | --- |
|  | FSW |  |  |  |
| COSCS128S through COSCS255S | All Mission SCS states (only valid in EPS subformat) | INAC or DISA |  |  |
| CORADMEN | Radmon Process State | DISA |  |  |
| COSCS107S | SCS #107 State (only valid in EPS subformat) | DISA |  |  |
|  | GRATINGS |  |  |  |
| 4M5IRAX | MCE A: +5 VOLT CONV INH RELAY MONITOR | DISA |  |  |
| 4HEXRAX | MCE A: HETG EXECUTE RELAY STATUS MONITOR | DISA |  |  |
| 4LEXRAX | MCE A: LETG EXECUTE RELAY STATUS MONITOR | DISA |  |  |
| 4M28IRAX | MCE A: +28 VOLT CONV INH RELAY MON | DISA |  |  |
| 4M5IRBX | MCE B: +5 VOLT CONV INH RELAY MONITOR | DISA |  |  |
| 4HEXRBX | MCE B: HETG EXECUTE RELAY STATUS MONITOR | DISA |  |  |
| 4LEXRBX | MCE B: LETG EXECUTE RELAY STATUS MONITOR | DISA |  |  |
| 4M28IRBX | MCE B: +28 VOLT CONV INH RELAY MON | DISA |  |  |
|  | SIM |  |  |  |
| 3TSCPOS | SIM POSITION (If SCS 81 and 108 were NOT disabled) | -99616 |  |  |
| 3TSCPOS | SIM POSITION (If SCS 81 and 108 were disabled) | Unchanged from step 3.0 above |  |  |
| 3SMOTPEN | SEA MOTOR DRIVER POWER RELAY STATUS | OFF |  |  |
| 3SMOTSEL | SEA MOTOR SELECTION RELAY STATUS | TSC |  |  |
|  | HRC |  |  |  |
| 2S1ONST | SHIELD A HVPS ON/OFF | OFF |  |  |
| 2S2ONST | SHIELD B HVPS ON/OFF | OFF |  |  |
| 2SPTPAST | SPECTROSCOPY DET TOP PLATE HV STEP | 43 |  |  |
| 2SPBPAST | SPECTROSCOPY DET BOTTOM PLATE HV STEP | 54 |  |  |
| 2IMTPAST | IMAGING DET TOP PLATE HV STEP | 42 |  |  |
| 2IMBPAST | IMAGING DET BOTTOM PLATE HV STEP | 53 |  |  |
| 2S1HVST | SHIELD A HVPS SETTING | 0 |  |  |
| 2S2HVST | SHIELD B HVPS SETTING | 0 |  |  |
| 2SCTHAST | STEP CTR LAST VALUE | 9000 |  |  |
| 2MCNAAMD | MOTOR CMD REGISTER MV NSTEPS TOWARD A | CMD |  |  |
|  | ACIS |  |  |  |
| 1DPICACU | DPA input current a [amp] | 0.25 to 0.57 |  |  |
| 1DPICBCU | DPA input current b [amp] | 0.19 to 0.43 |  |  |
| 1CBAT | Camera body temp a | -65 to -55 |  |  |
| 1DEICACU | DEA Input Current | ~0.6-0.8 (very noisy - take an average over several updates) |  |  |
| 1STAT1ST | Science run Not Running | 1 |  |  |

WORK TO EXTEND COMM

ACIS should not be considered safe until FOT and SOT engineers have runSOP_SYSTEM_UNSAFE_ACIS_PHASE2.  OC should ensure that comm is available for this procedure tobe run, ~2-3 hours.

-----END OF PROCEDURE-----

APPENDIX

| KEYWORDS: | ACIS, UNSAFE, SIM, PHASE1 |
| --- | --- |
| HISTORY | NAME | AUTHOR | REVISION | DATE |
|  |  | Logan | 3.2 | 10/31/02 |
| EXTERNAL REFERENCES: | SOP_OPS_STATE_OF_HEALTH SOP_SYSTEM_UNSAFE_ACIS_PHASE2 |